## Slide 1: S-100 Interoperability Catalogue
Original: Edward Kuwalek, IIC
Updated for NIPWG4
JP/RMM/EM
May 22nd , 2017

## Slide 2: BAD Interoperability
Ship
Management

## Slide 3: Objectives
Phase 1 - Interoperability Analysis
      Draft - Mar/2016 and Final Report – May/2016
Phase 2 – Interoperability Catalogue Design
      Interoperability Design Document
      UML models + XML schemas + extras
      Jul/2016
Phase 3 – Interoperability Catalogue Authoring
              Draft Interoperability Catalogue (IC) XML
              Sep/2016 – Mar/2017

## Slide 4: Interoperability Analysis – Requirements
Long and diverse list of requirements ~70
Provide support for complex data loading scenarios
  Data Interleaving
  Partial Data Suppression
  Partial Data Replacements
  Data Replacement
  Data Overlays
Facilitate easy loading of predefined product combinations

## Slide 5: Interoperability Analysis - Requirements
Address Potential Data Clashes
  Duplicate Feature Instances
  Duplicate Feature Domains
  Combined Geometry
  Spatial Discrepancies
Facilitate Skin-Of-The Earth Feature Replacement
Provide support for comprehensive hierarchy of data and display priorities

## Slide 6: Interoperability Analysis - Requirements
Support Harmonized Portrayal
  Display of Significant Features
  Avoid Obscuring Data
  Colour Set-Asides
  Day / Night / Dusk Modes
  Portrayal of Data Quality for Combinations of Information Layers
  Display of Text

## Slide 7: Interoperability Catalogue Design
Change of paradigm – ENC is now part of larger data ecosystem
Modular, machine readable design leveraging existing designs for FC, PC, and geospatial rules
Fully user-controlled via system settings
Compatible with existing portrayal engine
Supporting different levels of interoperation
Additional customization by OEMs or users possible

## Slide 8: Interoperability Catalogue Design - Levels
Level 0 – No explicit interoperability and IC is not used; ENC is the main product; all other data is loaded as overlays – effectively current ECDIS
Level 1 – Data interleaving; ENC is the main product but feature layers from other products are interleaved with ENC feature layers
Level 2 - Type-based selective feature class replacement is supported - ENC is the main product but global suppression of equivalent ENC features is allowed in favor of data layers from superior data products

## Slide 9: Interoperability Catalogue Design - Levels
Level 3 - Attribute value-based selectivity and feature hybridization; ENC is treated as one of the components of the data stack, and selected feature instances from other products may be treated as being superior to or enhancing selected ENC feature instances
Level 4 - Spatial operations; This level is the same as Level 3, but permits spatial queries (to determine related subsets) and operations (to define the interoperation result) to determine replacements for selected feature instances; rules are explicitly defined using an adequate set of spatially-capable ‘grammar’

## Slide 10: Interoperability Catalogue model

## Slide 11: Interoperability Catalogue Level 1 & 2
Levels 3 and 4 on hold

## Slide 12
Levels 3 and 4 on hold
Overview of feature processing paths

## Slide 13
Option with portrayal processing before interoperability processing will also be allowed
Hypothetical processing model

## Slide 14
Catalogue will be in XML