## Text in blue: Shom comments and proposals

Some changes are made directly in Track Changes of Word

## Paper for Consideration by WENDWG

## Development of WENS Principles

| Submitted by: | WENDWG Chair |
| --- | --- |
| Executive Summary: | Re-introduction of the WENS Principles with the aim to reach initial consensus at WENDWG-10, and then prepare submission for endorsement at IRCC-12 (June) then C-4 (October), not excluding a possible introduction at A-2 (April) as part of the report on the S-100 Implementation Strategy. |
| Related Documents: | WENDWG9-05A, IRCC11-07D2, IRCC11-07D3, C3-04.2A and C-3 Summary Report. |
| Related Projects: | S-100 Implementation Roadmap (C3-03.6A Rev1) |

## Introduction / Background

- During the WENDWG-9, the need to upgrade the WEND Principles was discussed, shifting it from a pure ENC focus to one that represents a more comprehensive suite of S-100 based services in support of Council actions C2/30 and C2/31.  A drafting group to collect comments regarding the WENS (Worldwide Electronic Navigation Services) Principles was authorized under action WENDWG9/22 and was charged with submitting a progress report to IRCC-11. Progress reports were presented to both IRCC-11 and Council-3 (C-3).  In general, both bodies agreed that the proposed course of action was correct and that the transition to “WENS” principles is needed.  The Council agreed that the proposed timeline (ANNEX 1), aiming for endorsement by Council-4, was acceptable.

- During C-3, it was also agreed that it was more appropriate to keep the current WEND Principles and their Guidelines for Implementation in M-3 as they are, for the time being at least until the “sunset” of S-57 ENC production. In other words, and noting the “WENS” acronym and title still needs to be discussed and approved at the WENDWG level, the WENS Principles are more than an update of the WEND Principles and are not intended to supersede the WEND Principles for now (C-3 Summary Report, Section 4.2 Worldwide Electronic Navigation Services (WENS), refers).

## Analysis/Discussion

- The WENS Principles Drafting Group Coordinator received comments from six Member States, five of which volunteered to be members of the Group.  Comments regarding the WENS direction were generally positive, but there were some notes of caution regarding scope and timing.

- ANNEX 2 of this document presents an edited version of the principles according to initial comments with notes for discussion included.

## Conclusions

- WENDWG-10 aims to gain basic consensus regarding the draft WENS principles, including the consideration of endorsing agreed upon data principles such as those being developed as part of the UN-GGIM Integrated Geospatial Information Framework’s Strategic Pathway 4, Section 4.5 on Data included in ANNEX 3 of this proposal.

## Recommendations

In the context of the S-100 Implementation Strategy:

- Recommend that Member States and RENCs (which play a key role today in data qualification, encryption and have set up a harmonized distribution process) come to the WENDWG-10 prepared to edit and make decisions regarding the WENS Principles.

- Recommend that Member States consider the fact that “WENS” stands for Worldwide Electronic Navigation Services and whether the name should be reconsidered as well as the attached priorities in the WENS Principles.

## Justification and Impacts

- The IHO is on the cusp of realizing the implementation of numerous S-100 based services over the upcoming decade and beyond.  It needs to develop recommendations for the distribution, boundaries, and governance of these new services as it did regarding ENCs.  The WENDWG has a strong history of providing this guidance and is well suited to expand its mandate to become the WENSWG or renamed body.

## Action Required of the WENDWG

- The WENDWG is invited to:

a.	note the work that has been done developing the WENS Principles

b.	prepare to discuss and edit the Principles with the aim of reaching WENDWG consensus, noting that these Principles should become a key component of the S-100 Implementation Strategy

c.	consider the impact of this development on the name and TORs of the WENDWG

d.	anticipate the possible impacts and consequences of the implementation of the WENS Principles (if and when endorsed and approved) on the RENCs capabilities, governance and activities and provide subsequent recommendations

e.	consider taking advantage of other global initiatives (such as the UN-GGIM) with the addition of relevant (IHO specific) thematic considerations regarding navigation services

ANNEX 1

Shom comment:

This proposed timeline needs to be updated in view of the postponement of the second Assembly in November (Assembly CL 17/2020):

- next step IRCC in June 2020

- progress report A-2 in November

- C-4 November (following A2)

- resolution submitted to the MS

provided that WEND10 leads to a consensual drafting of the resolution.

ANNEX 2

WORLDWIDE ELECTRONIC NAVIGATION SERVICES (WENS) PRINCIPLES

Note

*There has been a request to re-name the WENS.

*There has been a request to keep the name WENS.

(WEND WG working draft version, 28 August 2019)

The purpose of WENS is to ensure that high-quality, updated official hydrographic products and services are available to mariners worldwide. These products and services support hydrographic carriage requirements of Safety of Life at Sea (SOLAS) Chapter V (SOLAS/V), and the requirements of the International Maritime Organization (IMO) Performance Standards for Electronic Chart Display and Information Systems (ECDIS). In addition, these same coordinated products and services must be available to support mariners not subject to the provisions of ECDIS and should help to facilitate the transition from a paper to digital environment.

Shom comment:

Instead of “hydrographic services”, “hydrographic products and services” according

http://s100.iho.int/S100/home/s100-introduction should be written here and in the document where appropriate.

Applicability

SOLAS/V, requires signatory States to “arrange for the collection and compilation of hydrographic data and the publication, dissemination and keeping up to date of all nautical information necessary for safe navigation”. The International Hydrographic Organization (IHO) and partners have developed standards for digital products and  services that can functionally replace, and even enhance, their analog predecessors. The principles below apply to these digital products and services intended to meet a nation’s obligations under SOLAS and include high priority specifications referenced in the IHO Roadmap for S-100 Implementation:

| S-101 Electronic Navigational Chart | S-122 Marine Protected Areas | S-126 Marine Physical Environment |
| --- | --- | --- |
| S-102 Bathymetric Surface | S-123 Marine Radio Services | S-127 Marine Traffic Management |
| S-104 Water Level Information for Surface Navigation | S-124 Navigation Warnings | S-128 Catalogue of Nautical Products |
| S-111 Surface Currents | S-125 Marine Navigational Services | S-129 Under Keel Clearance Management |

These principles apply to the above S-1xx products and services, and thus complement the WEND principles for S-57 ENCs.

NOTES:

*These do not include specifications beyond S1xx.  For example Weather Warnings, Inland ENC, Aids to Navigation, or Sea Ice.  Removed S-121 per IRCC guidance.

*Reduced redundant introductory text.

*In reference to IRCC comment regarding “mandatory” carriage, note that “mandatory” in this case refers to ECDIS and says that we are obligated to provide services that are compatible with ECDIS, not that the new services are “mandatory” at this time.

Shom comment:

In order to avoid potential discrepancies in the assessment of "services" it is proposed to use the wording of SOLAS Chapter V Regulation 9.1.

In addition, it is probably useful to recall in this chapter “applicability” that the WENS and WEND principles will be superimposed until the extinction of the first generation S-57 ENCs.

S-103 Sub-surface Navigation could also be taken into account with the development of autonomous underwater vehicles, needs are likely to increase. This raises the need in the future to add S-1xx in the table above and the modalities to update the document.

1. Service Provision

Shom comment:

The term "service" is widely used in the document. This term may refer to elementary "products and services", for example an S-101 cell produced and maintained by a hydrographic office.

But the term can also refer to the overall service, covering the realization of the elementary “products and services” and also their distribution to the end users through ad-hoc services.

It is therefore important to lay down clear and unambiguous definitions to define the perimeter covered by "services".

It is therefore proposed to use the formula "products and services" for S-1xx datasets (in accordance with the IHO S-100 wording).

And the term “Service” for the overall service from the realization of the elementary "products and services" to the distribution to the users.

1.1. Member States will strive to ensure that mariners anywhere in the world can obtain up-to-date products and services for all shipping routes and ports around the world.

1.2. Member States are encouraged to distribute their products and services through compatible and coordinated network distribution systems to reduce distribution complexity and risk, and to ensure the greatest possible standardization, consistency, reliability and availability of services.

RENCs play a key role in the qualification of datasets, their encryption and the distribution of first generation ENCs (S-57/S-63). Member States are therefore encouraged to continue to build on the RENCs structure, supporting their necessary adaptation to the “S-100 era”, in order to ensure the highest standardization, consistency, reliability and availability of the Service.

NOTES

*Should distribution of these services all be the responsibility of the RENCs?  The provision intentionally does not specify a means of distribution in this version, just that services be compatible and coordinated.

*”Cost” has been removed and a draft (new provision) has been suggested as 1.2a.

Shom comment:

RENCs have had a key contribution with regards to standardization, consistency, reliability and avalibility of ENCs.

1.2a Member States should strive to ensure that the Service is not cost prohibitive, prioritizing safety above profit.

Shom comment:

This objective should cover the products and services and the distribution services up to the end users.

1.3. Source and authority of products and services should be preserved in the metadata and remain available to the end user.

1.4. Member States should use the IHO Data Protection Scheme (S-100 Part 15) based for distribution to end users, to ensure data integrity, to safeguard national copyright in data, to protect the mariner from falsified products or services, and to ensure traceability. When an encryption mechanism is employed to protect data, a failure of contractual obligations by the user should not result in a complete termination of the service. This is to assure that the safety of the vessel at sea is not compromised.

1.5. Noting that the content of many of these products and services are also valuable as part of a national or regional Marine Spatial Data Infrastructure (MSDI), the coordination and dissemination of these products and services may be coordinated through the same mechanisms as those intended for maritime navigation.

2. Rights and Responsibilities

2.1. SOLAS/V, Regulation 9, requires Contracting Governments to ensure that hydrographic products and services are available in a suitable manner in order to satisfy the needs of safe navigation. With mandatory carriage of ECDIS, there is a consequential requirement to ensure that such services, as agreed by IMO, are available in a form suitable for use in ECDIS, in current form and as subsequently updated.

2.2. To meet their national obligations under SOLAS, Member States may either:

a) Provide the necessary services, covering waters bounded by the seaward limit of their

Exclusive Economic Zone, or

b) Agree with other States to provide the necessary service coverage on their behalf.

All States retain the right to provide the services within national jurisdictions and according to national legislation. However, Member States should strive to ensure that comprehensive service coverage is available in all areas regardless of producer.

Notes

*This may be too complex to include here at this stage.

*Jurisdictions should be defined.

*Strengthened  coverage statement.

*Added national legislation statement in accordance with IRCC guidance.

Shom comment:

To make unambiguous the responsibilities of the States, Shom recommends the use of the singular instead of the plural (“Member State” rather than “Member States”).

In addition, it is proposed to clarify that the Member State is responsible for making available products and services through the distribution services up to the end users. It is better to write “Service” rather than “service”.

In case b) any product or service produced by another State should be withdrawn when it is made available by the coastal State.

Proposed rewording of  2.2

“To meet its national obligations under SOLAS, each Member State may either:

- Provide the Service deemed necessary, covering waters bounded by the seaward limit of their Exclusive Economic Zone, or

- Delegate to other States the role of providing on its behalf the part of the Service deemed necessary

All States retain the right to provide the products and services within their national jurisdictions and according to national legislation. Any product or service provided by another State should be withdrawn when it is made available by the coastal State.

Member States should strive to ensure that needed Service is available regardless of producer through coordination that could be provided by the Regional Hydrographic Commissions or any relevant body of the IHO.

2.3. Member States should recognize their potential exposure to legal liability for the quality of their hydrographic services.

Notes

*MS should strive to ensure that the safety benefits of services outweigh the risks associated with service liability.

Shom comment:

Instead of “their hydrographic services” is it “for their Service”?

2.4. The nation responsible for originating the data is also responsible for providing metadata on source, methods of collection, and data quality. Metadata should be consistent with IHO standards and practices.

Notes

*Last line added to help ensure consistency with approach to metadata.

Shom comment:

It should be clarified to what “data” refer: the S-1xx products and services or the upstream data that enable the creation of the S-11 products and services?

2.5. National entities are responsible for advising the issuing Hydrographic Office (HO) of available information and for advising the NAVAREA coordinator of Marine Safety Information in a timely manner.

2.6. In producing services, Member States are to take due account of the rights of the owners of source data and previously issued products, honoring any use restrictions or copyrights.

3. Coordination of Services

3.1. In order to ensure the primary objective of safe navigation, redundant services should be avoided. A single producing authority should exist in any given area for each service, though the same authority need not provide all services.

Notes

*Need to recognize the possibility that some services might be better with competition, weather for example.  However, the principles should help to ensure that services be designed and distributed with the intent of minimizing the number of systems and distribution mechanisms required to use them aboard ships.

Shom comment:

It is to the Member State in charge of the products and services to decide the products and services needed over their area of responsibility.

3.2. When the limits of waters of national jurisdiction have not been established, or it is more convenient to establish boundaries other than established national boundaries, producing countries may define the boundaries for hydrographic service provision within a bilateral (or multilateral) technical arrangement. These limits would be for convenience only and shall not be construed as having any significance or status regarding political or other jurisdictional boundaries.

Notes

*We have not been able to realize this with regard to ENC, so maybe it needs stronger language.  Could add something like, “Services will not be released when significant overlaps exist.”

3.3. In international waters, the applicable regional hydrographic commission may coordinate limits of services. In areas of national jurisdiction for which there is no agreed hydrographic service provider nation, the coastal State may designate the service provider nation. Services produced under such arrangements should be offered for transfer to the coastal State in the event that the coastal State subsequently develops the capacity to maintain the services. Such transfer should respect the rights of the coastal State and the  rights of the producer nation.

Notes

*May need to expand the roles of the RHCs.  Each RHC should have a Service Coordination Committee.  Much of the WENS data currently sits outside RHC remits.

Shom comment

This article mixes issues of responsibility (paragraph 2) and coordination (paragraph 3).

In areas of national jurisdiction, there is no need for an “agreed hydrographic service provider nation”. The coastal State is by default the “agreed hydrographic service provider nation” to establish and distribute products and services in its waters. It can delegate this role to another state if it wishes (as stipulated in 2.2).

This article needs clarification and possibly rewriting.

4. Maintenance and Improvement of services and products

4.1. Member States are encouraged to work together on data capture and data management. To the extent possible, data should be widely shared to support continual updates and improvements of hydrographic products and services.

4.2. Technically and economically effective solutions for updating products and services are to be established conforming to the relevant IHO standards. The updating of products and services should be at least as frequent as that provided by the nation for previous analog products and services.

5. Standards and Quality Management

5.1. Products and service providers and distributors should employ a documented Quality Management System to help ensure high quality of hydrographic services. When implemented, this should be certified by a relevant body as conforming to a suitable recognized standard; typically this will be ISO 9001:2015.

Note

*Strengthened statement by putting onus on service providers and distributors, not WENS Principles.

5.2. Products and services provided shall be in conformance with all approved relevant IHO, IMO and World Meteorological Organization (WMO) standards, when they are available.

Note

*Added WMO in accordance with IRCC guidance.

6. Mutual Assistance and Training

6.1. Member States’ HOs are requested to participate in capacity building efforts developed nationally, regionally, and through the IHO, by providing subject matter experts, venues, training materials, and open-source applications. Member States are encouraged to coordinate capacity building activities with the IHO Capacity Building Sub-Committee (CBSC). The goal of this capacity building is to increase the availability of high-quality hydrographic services globally.

Note

*Added reference to the IHO CB Sub-Committee.

ANNEX 3

DRAFT GGIM Integrated Geospatial Information Framework’s Strategic Pathway 4, Section 4.5

There are specific principles and elements for managing geospatial information to

promote consistent data governance, management, discovery, sharing and reuse so that

data organizations may meet their obligations to government and the user community.

These principles also need to be embedded into acts, policies, and directives for

update/compliance and integration into business practices. The guiding principles for data

are:

- Governance: High quality authoritative datasets are delivered through

designated data governance roles and responsibilities. Data governance

roles are mandated for each dataset to ensure responsibility for the

integrity and quality of data.

- Consistent Identification: A common data dictionary, vocabulary,

ontology and persistent identifies are applied to the identification of

data to enhance accessibility, manage effective use of data, and avoid

duplicated collection or purchase.

- Quality Management: Quality management processes are used to

manage the currency, completeness, accuracy and consistency of data

for a specified purpose.

- Metadata: Appropriate metadata is applied according to standards and

used to accurately define and describe geospatial data, including

content, geographic extent, purpose, characteristics, currency and

provenance etc., together with contact details for further information.

- Standards: Appropriate standards are adopted and enforced

throughout the data lifecycle to enhance integration and

interoperability of individual and disparate data sets.

- Accessibility: Easy, efficient and equitable access to spatial data

through common geospatial platforms where technology, data formats,

organizational arrangements, licensing, location, costs and conditions

do not inhibit its use.

- Reusable Formats: Data is in a form suitable for further value-adding by

internal and external users.

- Authoritative: Data is managed responsibly by the designated data

custodian to eliminate the proliferation of duplicate data sets. The

notion is to collect once and use many times.

- Timeliness: Data is managed according to priority, and where required,

is maintained as close to real-time as possible.

- Provenance: The origin and quality of data is readily accessible to the

user via metadata so that they can determine if it is ‘Fit for Purpose”

- Integrity: The interrelationships between data themes collected by

multiple agencies are managed with topological integrity.

- Demand Driven: Data acquisition and maintenance is aligned to user

needs and requirements to achieve optimal resource allocation.

- Efficiency: Geospatial data products are differentiated as close as

possible to the user to create more opportunities for reuse along the

supply chain.

- Security: Data are held with adequate provision for long-term care

including disaster recovery and backup procedures, are disposed or

archived in accordance with government regulations, and considering

technological advancements.

- Respected Rights: Confidentiality, privacy, intellectual property rights

and the security of sensitive information are preserved, and the sharing

of Indigenous knowledge is contingent upon consent of the knowledge

holders in alignment with UNDRIP principles.