|  |  | E |
| --- | --- | --- |

ALBERT EMBANKMENT

LONDON SE1 7SR

Telephone: +44 (0)20 7735 7611	Fax: +44 (0)20 7587 3210

MSC.1/Circ.1310/Rev.1

21 November 2014

REVISED JOINT IMO/IHO/WMO MANUAL ON

MARITIME SAFETY INFORMATION (MSI)

1	The Maritime Safety Committee (MSC), at its ninety-fourth session (17 to 21 November 2014), noted and approved the revised Joint IMO/IHO/WMO Manual on Maritime Safety Information (MSI), as prepared by WMO and IHO and agreed by the Sub-Committee on Navigation, Communications and Search and Rescue (NCSR) at its first session (30 June to 4 July 2014).

2	MSC 94 noted that section 7 provides extensive guidance and examples on the structure and text to be used in navigational warnings and that, to ensure greater uniformity, this section would be provided in the English language in an additional annex in the circulars and publications in the Spanish and French languages.

3	The Committee was of the opinion that the widest possible use of the manual should be encouraged and invited Member Governments to bring the annexed Joint IMO/IHO/WMO Manual to the attention of mariners and those involved in the promulgation of navigational warnings and meteorological forecasts and warnings.

4	This circular supersedes MSC.1/Circ.1310.

5	The Committee decided that the amendments will come into force on 1 January 2016.

Contents

Page

Foreword 		3

1	General information 		5

2	Promulgation of maritime safety information 		5

3	NAVAREA/Sub-Area/National Coordinators' resources and responsibilities 		15

4	Navigational warnings for the World-Wide Navigational Warning Service 		19

5	The structure of navigational warnings 		22

6	Message format of navigational warnings 		24

Part 1 – Preamble 		24

Part 2 – Warning 		26

Part 3 – Postscript 		27

7	Guidance and examples for navigational warnings by type of hazard 		28

8	METAREA Coordinator resources and responsibilities		77

9	Meteorological warnings and forecasts 		78

10	Examples for meteorological warnings and forecasts		86

11	Search and rescue notification 		91

12	Procedure for amending the joint imo/iho/wmo Manual on MSI 		91

Foreword

SOLAS regulation IV/12.2 states that "Every ship, while at sea, shall maintain a radio watch for broadcasts of maritime safety information on the appropriate frequency or frequencies on which such information is broadcast for the area in which the ship is navigating."

At the request of the Sub-Committee on Radiocommunications, the International Hydrographic Organization (IHO) and the World Meteorological Organization (WMO), a joint document on the drafting of maritime safety information broadcasts was produced (the Joint IMO/IHO/WMO Manual on Maritime Safety Information). The document was circulated to IHO Member States under IHB CL 10/1994 and as COMSAR/Circ.4 by the Sub-Committee on Radiocommunications and Search and Rescue (COMSAR) after its first session in February 1996, which action was endorsed by the Maritime Safety Committee at its sixty-sixth session in May/June 1996.

The publication contained sections from IMO resolution A.706(17), "World-Wide Navigational Warning Service", as amended, and relevant sections of the WMO Publication Manual on Marine Meteorological Services (WMO No.558).

At its seventh meeting in September 2005, the IHO's Commission on the Promulgation of Radio Navigational Warnings (CPRNW) established a working group to review all World-Wide Navigational Warning Service (WWNWS) documentation. The working group included representation from the WMO and prepared at first, revisions to IMO resolutions as amended A.705(17), "Promulgation of Maritime Safety Information" and A.706(17), "World-Wide Navigational Warning Service". The proposed revisions of the resolutions were circulated to IHO Member States under IHB CL 104/2007, endorsed by COMSAR at its twelfth session in April 2008 and subsequently approved by the Maritime Safety Committee at its eighty-fifth session in November/December 2008.

The IHO CPRNW working group then prepared the revised Joint IMO/IHO/WMO Manual on Maritime Safety Information incorporating the revised information from resolutions A.705(17), as amended and A.706(17), as amended. The revised text of the Joint IMO/IHO/WMO Manual on Maritime Safety Information was circulated to IHO Member States under cover of IHB CL 70/2008, endorsed by COMSAR at its thirteenth session in January 2009 and subsequently approved by the Maritime Safety Committee at its eighty-sixth session in May/June 2009.

The WMO Executive Council, at its sixty-first session in June 2009, requested WMO to establish and develop, in collaboration with the IMO, terms of reference for an IMO/WMO World-Wide Met-ocean Information and Warning Service guidance document (WWMIWS), to complement the existing IMO/IHO World-Wide Navigational Warning Service guidance document (WWNWS), provided in resolution A.706(17), as amended. This new IMO/WMO guidance document is intended to provide specific guidance for the promulgation of internationally coordinated meteorological information, forecast and warnings services for the GMDSS, which does not apply to purely national services.

The WMO Executive Council adopted the WWMIWS at its sixty-second session in June 2010. It was submitted to IMO's Maritime Safety Committee at the end of 2010, which requested its COMSAR Sub-Committee to review it before its approval at its eighty-ninth session in May 2011. It was officially adopted by the IMO Assembly at its twenty-seventh session in November 2011 and the WWMIWS is included in the regulatory publications as IMO resolution A.1051(27). Future amendments to this guidance document will be considered formally and approved by both WMO and IMO.

The Committee was of the opinion that the widest possible use of the manual should be encouraged and invited Member Governments to bring the Joint IMO/IHO/WMO Manual to the attention of mariners and those involved in the promulgation of navigational warnings and meteorological forecasts and warnings.

Although this is an IMO publication, it is intended that the responsible organizations will maintain their respective sections of this Joint IMO/IHO/WMO Manual.

1	General information

This Manual provides a practical guide for anyone who is concerned with drafting navigational warnings or with the issuance of meteorological warnings and forecasts under the Global Maritime Distress and Safety System (GMDSS). Maritime Safety Information (MSI) is promulgated in accordance with the requirements of IMO resolution A.705(17), as amended. Navigational warnings are issued under the auspices of the IMO/International Hydrographic Organization (IHO) World-Wide Navigational Warning Service (WWNWS) in accordance with the requirements of IMO resolution A.706(17), as amended. Meteorological warnings and forecasts are issued under the auspices of the IMO/World Meteorological Organization (WMO) World-Wide Met-ocean Information and Warnings Service (WWMIWS) in accordance with the requirements of IMO resolution A.1051(27), as amended. In order to achieve the necessary impact on the mariner it is essential to present timely and relevant information in a consistent format that is clear, unambiguous and brief. Within this Manual, it is particularly intended to provide the best form of words for use in all types of navigational warnings and meteorological warnings and forecasts that are required to be broadcast in the English language. Note has been taken of the IMO standard marine communication phrases (IMO resolution A.918(22)), where appropriate.

This Manual cannot provide specimen texts for every type of event which may occur. However, the principles illustrated herein may be applied in general to drafting messages for every kind of navigational warning and covering all types of hazards and for the issuance of meteorological warnings and forecasts .

IMO resolution A.706(17), as amended, on the World-Wide Navigational Warning Service  in paragraph 5.3.1, requires that "All NAVAREA, Sub-area and coastal warnings should be broadcast only in English in the International NAVTEX and in EGC services".

IMO resolution A.1051(27), as amended,  on the IMO/WMO World-Wide Met-Ocean Information and Warnings Service in paragraph 3.4.1 requires that "All Meteorological information shall be broadcast only in English in the International NAVTEX and in EGC services".

Where this Manual has been produced in languages other than English then the message examples given in the English language text should be used.

2	Promulgation of maritime safety information

2.1	Introduction

2.1.1 	The Maritime safety information (MSI) service of the GMDSS is the internationally and nationally coordinated network of broadcasts containing information which is necessary for safe navigation, received on ships by equipment which automatically monitors the appropriate transmissions, displays information which is relevant to the ship and provides a print capability. This concept is illustrated in figure 1.

2.1.2	MSI is of vital concern to all ships. It is therefore essential that common standards are applied to the collection, editing and dissemination of this information. Only by doing so will mariners be assured of receiving the information they need, in a form which they understand, at the earliest possible time.

2.1.3	The purpose of IMO resolution A.705(17), as amended "Promulgation of Maritime Safety Information" is to set out the organization, standards and methods which should be used for the promulgation and reception of MSI.

Figure 1 −  The Maritime Safety Information service of the Global 
Maritime Distress and Safety System

2.2	Definitions

2.2.1 	For the purposes of this Manual, the following definitions apply:

.1	Coastal warning means a navigational warning or in-force bulletin promulgated as part of a numbered series by a National Coordinator. Broadcast should be made by the International NAVTEX service to defined NAVTEX service areas and/or by the International Enhanced Group Call service to the coastal warning area. (In addition, Administrations may issue coastal warnings by other means.)

.2	Coastal warning area means a unique and precisely defined sea area within a NAVAREA/METAREA or Sub-area established by a coastal State for the purpose of coordinating the broadcast of coastal Maritime Safety Information through the Enhanced Group Call service.

.3	Enhanced Group Call (EGC) means the broadcast of coordinated maritime safety information and search and rescue related information, to a defined geographical area using a recognized mobile satellite service.

.4	Global Maritime Distress and Safety System (GMDSS) means a system that performs the functions set out in SOLAS regulation IV/4, as amended.

.5	HF NBDP means High Frequency narrow-band direct-printing, using radio telegraphy as defined in Recommendation ITU-R M.688.

.6	In-force bulletin means a list of serial numbers of those NAVAREA, Sub-area or coastal warnings in force issued and broadcast by the NAVAREA Coordinator, Sub-area Coordinator or National Coordinator.

.7	International Enhanced Group Call service means the coordinated broadcast and automatic reception of Maritime Safety Information and Search and Rescue related information via Enhanced Group Call, using the English language.

.7	International NAVTEX service means the coordinated broadcast and automatic reception on 518 kHz of Maritime Safety Information by means of narrow-band direct-printing telegraphy using the English language.

.8	[International SafetyNET service[s] means the coordinated broadcast and automatic reception of Maritime Safety Information via the Inmarsat Enhanced Group Call  system, using the English language, in accordance with the provisions of the International Convention for the Safety of Life at Sea, 1974, as amended.]

.9	Issuing Service means a National Meteorological and Hydrological Service (NMHS) or National Authority which has accepted responsibility for ensuring that meteorological warnings and forecasts for shipping are disseminated through the International Enhanced Group Call service to the designated METAREA for which the NMHS has accepted responsibility under the broadcast requirements of the Global Maritime Distress and Safety System.

.10	[Land Earth Station (LES) means a fixed terrestrial radio facility acting as a gateway between terrestrial networks and the recognized mobile satellite service. This may also be referred to as a Coast Earth Station (CES).]

.11	Local warning means a navigational warning which covers inshore waters, often within the limits of jurisdiction of a harbour or port authority.

.12	[Main shipping lanes means those routes used by international shipping.]

.13	Maritime Safety Information (MSI) means navigational and meteorological warnings, meteorological forecasts and other urgent safety-related messages broadcast to ships.

.14	Maritime Safety Information service means the internationally and nationally coordinated network of broadcasts containing information, which is necessary for safe navigation.

.15	METAREA means a geographical sea area established for the purpose of coordinating the broadcast of marine meteorological information. The term METAREA followed by a roman numeral may be used to identify a particular sea area. The delimitation of such areas is not related to and shall not prejudice the delimitation of any boundaries between States. (See figure 3).

.16	METAREA Coordinator means the authority charged with coordinating marine meteorological information broadcasts by one or more National Meteorological and Hydrological Services acting as Preparation or Issuing Services within the METAREA.

.17	Meteorological information means the marine meteorological warning and forecast information in accordance with the provisions of the International Convention for the Safety of Life at Sea.

.18	National Coordinator means the national authority charged with collating and issuing coastal warnings within a national area of responsibility.

.19	[National Marine Services Focal Point (NMSFP) means]

.20	National NAVTEX service means the broadcast and automatic reception of Maritime Safety Information by means of narrow-band direct-printing telegraphy using frequencies other than 518[ kHz and languages as decided by the Administration concerned.

.21	[National SafetyNET [and SafetyNET II] service[s] means the broadcast and automatic reception of Maritime Safety Information via the Inmarsat EGC system, using languages as decided by the Administration concerned.]

.22	NAVAREA means a geographical sea area5 established for the purpose of coordinating the broadcast of navigational warnings. The term NAVAREA followed by a roman numeral may be used to identify a particular sea area. The delimitation of such areas is not related to and shall not prejudice the delimitation of any boundaries between States. (See figure 2).

.23	NAVAREA Coordinator means the authority charged with coordinating, collating and issuing NAVAREA warnings for a designated NAVAREA.

.24	NAVAREA warning means a navigational warning or in-force bulletin promulgated as part of a numbered series by a NAVAREA Coordinator.

.25	Navigational warning means a message containing urgent information relevant to safe navigation broadcast to ships in accordance with the provisions of the International Convention for the Safety of Life at Sea, 1974, as amended.

.26	NAVTEX means the system for the broadcast and automatic reception of Maritime Safety Information by means of narrow-band direct-printing telegraphy.

.27	NAVTEX Coordinator means the authority charged with operating and managing one or more NAVTEX stations broadcasting Maritime Safety Information as part of the International NAVTEX service.

.28	NAVTEX coverage area means an area defined by an arc of a circle having a radius from the transmitter calculated according to the method and criteria given in IMO resolution A.801(19), as amended.

.29	NAVTEX service area means a unique and precisely defined sea area, wholly contained within the NAVTEX coverage area, for which Maritime Safety Information is provided from a particular NAVTEX transmitter. It is normally defined by a line that takes full account of local propagation conditions and the character and volume of information and maritime traffic patterns in the region, as given in IMO resolution A.801(19), as amended.

.30	Other urgent safety-related information means Maritime Safety Information broadcast to ships that is not defined as a navigational warning or meteorological information. This may include, but is not limited to, significant malfunctions or changes to maritime communications systems, and new or amended mandatory ship reporting systems or maritime regulations affecting ships at sea.

.31	Preparation Service means a National Meteorological and Hydrological Service or National Authority which has accepted responsibility for the preparation of warnings and forecasts for parts of or an entire METAREA in the WMO system for the dissemination of meteorological warnings and forecasts to shipping under the GMDSS and for their transfer to the relevant Issuing Service for broadcast.

.32	Recognized mobile satellite service (RMSS) means any service which operates through a satellite system and is recognized by the IMO, for use in the GMDSS.

.33	[SafetyNET [and SafetyNET II] means the international service for the broadcast and automatic reception of Maritime Safety Information via the Inmarsat Enhanced Group Call system. Enhanced Group Call receiving capability is part of the mandatory equipment which is required to be carried by certain ships in accordance with the provisions of the International Convention for the Safety of Life at Sea, 1974, as amended.]

.34	Search and Rescue (SAR) related information means distress alert relays and other urgent search and rescue related information broadcast to ships [(See section 11.1)].

.35	[Sea Area A1 means an area within the radiotelephone coverage of at least one VHF coast station in which continuous DSC alerting is available, as may be defined by a SOLAS Contracting Government.]

.36	[Sea Area A2 means an area, excluding sea area A1, within the radiotelephone coverage of at least one MF coast station in which continuous DSC alerting is available, as may be defined by a SOLAS Contracting Government.]

.37	[Sea Area A3 means an area, excluding sea areas A1 and A2, within the coverage of a recognized mobile satellite service satellite in which continuous alerting is available.]

.38	[Sea Area A4 means an area outside of sea areas A1, A2 and A3.]

.39	Sub-area means a subdivision of a NAVAREA/METAREA in which a number of countries have established a coordinated system for the promulgation of Maritime Safety Information. The delimitation of such areas is not related to and shall not prejudice the delimitation of any boundaries between States.

.40	Sub-area Coordinator means the authority charged with coordinating, collating and issuing Sub-area warnings for a designated Sub-area.

.41	Sub-area warning means a navigational warning or in-force bulletin promulgated as part of a numbered series by a Sub-area Coordinator. Broadcast should be made by the International NAVTEX service to defined NAVTEX service areas or by the International Enhance group call service (through the appropriate NAVAREA Coordinator).

.42	User defined area means a temporary geographic area, either circular or rectangular, to which Maritime Safety Information is addressed.

.43	UTC means Coordinated Universal Time which is equivalent to GMT (or ZULU) as the international time standard.

.44	Worldwide Met-Ocean Information and Warning Service Service (WWMIWS) means the internationally coordinated service for the promulgation of meteorological warnings and forecasts.

.45	World-Wide Navigational Warning Service (WWNWS) means the internationally and nationally coordinated service for the promulgation of navigational warnings.

.46	In the operating procedures, coordination means that the allocation of the time for data broadcast is centralized, the format and criteria of data transmissions are compliant as described in the Joint IMO/IHO/WMO Manual on Maritime Safety Information and that all services are managed as set out in IMO resolutions A.705(17), as amended, A.706(17), as amended and A.1051(27), as amended.

2.2.2	Delimitation of NAVAREAs

Figure 2 – NAVAREAs for coordinating and promulgating navigational warnings under 
the World-Wide Navigational Warning Service

The delimitation of such areas is not related to and shall not prejudice 
the delimitation of any boundaries between States.

2.2.3 		Delimitation of METAREAs

Figure 3 – METAREAs for coordinating and promulgating meteorological warnings 
and forecasts within the GMDSS

The delimitation of such areas is not related to and shall not prejudice 
the delimitation of any boundaries between States.

2.3 	Broadcast methods

2.3.1	The two principal methods used for broadcasting MSI in accordance with the provisions of the International Convention for the Safety of Life at Sea, 1974, as amended, in the areas covered by these methods, are as follows:

.1	NAVTEX:  broadcasts to coastal waters; and

.2	EGC:  broadcasts which cover all the waters of the globe except for Sea Area A4, as defined by IMO resolution A.801(19), as amended.

2.3.2	Information should be provided for unique and precisely defined sea areas, each being served only by the most appropriate of the above methods. Although there will be some duplication to allow a ship to change from one method to another, the majority of warnings will be broadcast either on NAVTEX or by EGC.

2.3.3	NAVTEX broadcasts should be made in accordance with the standards and procedures set out in the NAVTEX Manual.

2.3.4	SafetyNET [and SafetyNET II] broadcasts should be made in accordance with the standards and procedures set out in the International SafetyNET Manual.

2.3.5	HF NBDP may be used to promulgate MSI in areas outside EGC and NAVTEX coverage (SOLAS regulation IV/7.1.5).

2.3.6	In addition, Administrations may also provide MSI by other means.

2.3.7	In the event of failure of normal transmission facilities, an alternative means of transmission should be utilized. A NAVAREA/METAREA warning and a coastal warning, if possible, should be issued detailing the failure, its duration and, if known, the alternative route for the dissemination of MSI.

2.4	Scheduling

2.4.1	Automated methods (NAVTEX/EGC)

2.4.1.1	Navigational warnings should be broadcast as soon as possible or as dictated by the nature and timing of the event. Normally, the initial broadcast should be made as follows:

.1	for NAVTEX, at the next scheduled broadcast, unless circumstances indicate the use of procedures for VITAL or IMPORTANT warnings; and

.2	for EGC, within 30 minutes of receipt of original information, or at the next scheduled broadcast.

2.4.1.2	Navigational warnings should be repeated in scheduled broadcasts in accordance with the guidelines promulgated in the NAVTEX Manual and International SafetyNET Manual as appropriate.

2.4.1.3	At least two scheduled daily broadcast times are necessary to provide adequate promulgation of NAVAREA warnings. When NAVAREAs extend across more than six time zones, more than two broadcasts should be considered to ensure that warnings can be received. When using EGC in lieu of NAVTEX for coastal warnings, Administrations may need to consider an increase in the number of scheduled daily broadcasts compared with the requirement for NAVAREA warnings.

2.4.1.4	It is important that where the degree of hazard is known, this information is included in the relevant warning e.g. naval exercises, missile firings, space missions, nuclear tests, ordnance dumping zones, etc. Whenever possible such warnings should be originated not less than five days in advance of the scheduled event and reference may be made to relevant national publications in the warning.

2.4.2	Schedule changes

2.4.2.1	Broadcast times for NAVTEX are defined by the B1 transmitter identification character of the station, allocated by the IMO NAVTEX Coordinating Panel.

2.4.2.2	Times of scheduled broadcasts under the International SafetyNET service are coordinated through the International SafetyNET Coordinating Panel.

2.5 	Shipboard equipment

2.5.1	Ships are required to be capable of receiving MSI broadcasts for the area in which they operate in accordance with the provisions of the International Convention for the Safety of Life at Sea, 1974, as amended.

2.5.2	The NAVTEX receiver should operate in accordance with the technical specifications set out in Recommendation ITU-R M.540, as amended. IMO resolution MSC.148(77) recommends Governments to ensure that NAVTEX receiver equipment, if installed on or after 1 July 2005, conforms to performance standards not inferior to those specified in IMO resolution MSC.148(77), and if installed before 1 July 2005, conforms to performance standards not inferior to those specified in the annex to IMO resolution A.525(13).

2.5.3	The EGC receiver should conform to the Maritime Design and Installation Guidelines (DIGs), annex B, issue 6 of April 2008 published by Inmarsat. IMO resolution MSC.306(87) recommends Governments to ensure that EGC equipment, if installed on or after 1 July 2012, conforms to performance standards not inferior to those specified in the annex to IMO resolution MSC.306(87), and if installed before 1 July 2012, conforms to performance standards not inferior to those specified in the annex to IMO resolution A.664(16).

2.5.4	In Sea Area A4, outside of the coverage of NAVTEX, where MSI is received using HF NBDP, the HF NBDP receiver should operate in accordance with the technical specifications set out in Recommendation ITU-R M.688, as amended, and should meet the performance standards adopted by IMO resolution A.700(17), as amended.

2.6	Provision of information

2.6.1	Navigational warnings should be provided in accordance with the standards, organization and procedures of the WWNWS under the functional guidelines of the IHO through its World-Wide Navigational Warning Service Sub-Committee (WWNWS-SC).

2.6.2	Meteorological warnings and forecasts should be provided in accordance with the WMO technical regulations, recommendations, and procedures defined for the World-Wide Met-Ocean Information and Warning Service (WWMIWS) through the World-Wide Met-Ocean Information Warning Service Committee (WWMIWS-C) of the Joint WMO/IOC Commission for Oceanography and Marine Meteorology (JCOMM).

2.6.3	Other urgent safety-related information should be provided by the relevant national or international authority responsible for managing the system or scheme.

2.6.4	SAR information, which is never MSI, should be provided by the various authorities responsible for coordinating maritime search and rescue operations in accordance with the standards and procedures established by the IMO.

2.6.5	Relevant national or international authorities should take into account the need for contingency planning.

2.7	Coordination procedures

2.7.1	In order to make the best use of automated reception facilities and to ensure that the mariner receives at least the minimum information necessary for safe navigation, careful coordination is required.

2.7.2	In general, this requirement for coordination will be met by the standard operational procedures of IMO, IHO, and the WMO. Coordination issues should be referred, in the first instance, to the most appropriate parent body.

2.7.3	Administrations broadcasting MSI should provide details of services to IMO, which will maintain and publish this as part of the GMDSS Master Plan.

2.7.4	The coordination of changes to operational NAVTEX services and of the establishment of new stations is undertaken by the IMO NAVTEX Coordinating Panel on behalf of the Maritime Safety Committee.

2.7.5	The coordination of changes to operational SafetyNET [and SafetyNET II] services and of the authorization and registration of information providers is undertaken by the International SafetyNET Coordinating Panel on behalf of the Maritime Safety Committee.

2.7.6	Administrations should design their broadcasts to suit specific service areas. The designation of service areas is an important part of the coordination process since it is intended that a ship should be able to obtain all the information relevant to a given area from a single source. The Maritime Safety Committee approves NAVAREAs/METAREAs and service areas for the International NAVTEX and EGC service as advised by the IHO and the WMO.

3	NAVAREA/Sub-Area/National Coordinators' resources and responsibilities

3.1	NAVAREA Coordinator resources

3.1.1	The NAVAREA Coordinator must have:

.1	the expertise and information sources of a well-established national hydrographic service;

.2	effective communications, e.g. telephone, email, facsimile, internet, etc. with Sub-area and National Coordinators in the NAVAREA, with other NAVAREA Coordinators, and with other data providers; and

.3	access to broadcast systems for transmission to the navigable waters of the NAVAREA. As a minimum, this should include those described in paragraph 2.3.1. Reception should normally be possible at least 300 nautical miles beyond the limit of the NAVAREA.

3.2	NAVAREA Coordinator responsibilities

3.2.1	The NAVAREA Coordinator must:

.1	endeavour to be informed of all events that could significantly affect the safety of navigation within the NAVAREA;

.2	assess all information immediately upon receipt for relevance to navigation in the NAVAREA;

.3	select information for broadcast in accordance with the guidance given in paragraph 4.2;

.4	draft NAVAREA warnings in accordance with the Joint IMO/IHO/WMO Manual on Maritime Safety Information;

.5	direct and control the broadcast of NAVAREA warnings, in accordance with the provisions of the SOLAS, 1974, as amended;

.6	forward NAVAREA warnings and relevant associated information which may require wider promulgation directly to adjacent NAVAREA Coordinators and/or others as appropriate, using the quickest possible means;

.7	ensure that NAVAREA warnings which may remain in force for more than six weeks are made available immediately to NAVAREA Coordinators, other authorities and mariners in general, as appropriate;

.8	ensure that information concerning all navigational warning subject areas listed in paragraph 4.2.3 that may not require a NAVAREA warning within their own NAVAREA is forwarded immediately to the appropriate National and NAVAREA Coordinators affected by the event;

.9	broadcast in-force bulletins not less than once per week at a regular scheduled time;

.10	promulgate the cancellation of NAVAREA warnings which are no longer valid;

.11	act as the central point of contact on matters relating to navigational warnings within the NAVAREA;

.12	promote and oversee the use of established international standards and practices with respect to the promulgation of navigational warnings throughout the NAVAREA;

.13	when notified by the authority designated to act on reports of piracy and armed robbery against ships, arrange for the broadcast of a suitable NAVAREA warning. Additionally, keep the national or regional piracy control centre informed of long-term broadcast action(s);

.14	when notified by the appropriate authorities, arrange for the broadcast of suitable NAVAREA warnings to promulgate World Health Organization (WHO) health advisories, tsunami-related warnings and other information which is necessary for safe navigation;

.15	monitor the broadcasts which they originate, to ensure that the warnings have been correctly broadcast;

.16	maintain records of source data relating to NAVAREA warnings in accordance with the requirement of the national Administration of the NAVAREA Coordinator;

.17	coordinate preliminary discussions between neighbouring Member States, seeking to establish or amend NAVTEX services and with other adjacent Administrations, prior to formal application;

.18	contribute to the development of international standards and practices through attendance and participation in the IHO World-Wide Navigational Warning Service Sub-Committee meetings, and also participate in relevant IMO, IHO and WMO fora as appropriate; and

.19	take into account the need for contingency planning.

3.3	Sub-area Coordinator resources

3.3.1	The Sub-area Coordinator must have, or have access to:

.1	the expertise and information sources of a well-established national hydrographic service;

.2	effective communications, e.g. telephone, email, facsimile, internet, etc. with National Coordinators in the Sub-area, with the NAVAREA Coordinator, and with other data providers; and

.3	broadcast systems for transmission to the entire Sub-area.

3.4	Sub-area Coordinator responsibilities

3.4.1	The Sub-area Coordinator must:

.1	endeavour to be informed of all events that could significantly affect the safety of navigation within the Sub-area;

.2	assess all information immediately upon receipt for relevance to navigation in the Sub-area;

.3	select information for broadcast in accordance with the guidance given in paragraph 4.2;

.4	draft Sub-area warnings in accordance with the Joint IMO/IHO/WMO Manual on Maritime Safety Information;

.5	direct and control the broadcast of Sub-area warnings, in accordance with the provisions of the SOLAS, 1974, as amended;

.6	forward Sub-area warnings and relevant associated information which may require wider promulgation directly to their own NAVAREA Coordinator using the quickest possible means;

.7	broadcast in-force bulletins not less than once per week at a regular scheduled time;

.8	promulgate the cancellation of Sub-area warnings which are no longer valid;

.9	act as the central point of contact on matters relating to navigational warnings within the Sub-area;

.10	promote the use of established international standards and practices in the promulgation of navigational warnings within the Sub-area;

.11	monitor the broadcasts which they originate, to ensure that the warnings have been correctly broadcast;

.12	maintain records of source data relating to Sub-area warnings in accordance with the requirement of the national Administration of the Sub-area Coordinator;

.13	contribute to the development of international standards and practices through attendance and participation in the IHO World-Wide Navigational Warning Service Sub-Committee meetings, and also participate in relevant IMO, IHO and WMO fora as appropriate; and

.14	take into account the need for contingency planning.

3.5	National Coordinator resources

3.5.1	The National Coordinator must have:

.1	established sources of information relevant to the safety of navigation within national waters;

.2	effective communications, e.g. telephone, email, facsimile, internet, etc. with the NAVAREA/Sub-area Coordinator and adjacent national Coordinators; and

.3	access to broadcast systems for transmission to their area of national responsibility.

3.6	National Coordinator responsibilities

3.6.1	The national Coordinator must:

.1	endeavour to be informed of all events that could significantly affect the safety of navigation within their area of national responsibility;

.2	assess all information immediately upon receipt for relevance to navigation in their area of national responsibility;

.3	select information for broadcast in accordance with the guidance given in paragraph 4.2;

.4	draft coastal warnings in accordance with the Joint IMO/IHO/WMO Manual on Maritime Safety Information;

.5	direct and control the broadcast of coastal warnings, in accordance with the provisions of the SOLAS, 1974, as amended;

.6	forward coastal warnings and relevant associated information which may require wider promulgation directly to their NAVAREA/Sub-area Coordinator and/or adjacent national Coordinators as appropriate, using the quickest possible means;

.7	broadcast in-force bulletins not less than once per week at a regular scheduled time, if providing broadcast services;

.8	promulgate the cancellation of coastal warnings which are no longer valid;

.9	act as the central point of contact on matters relating to navigational warnings within their area of national responsibility;

.10	promote the use of established international standards and practices in the promulgation of navigational warnings within their area of national responsibility;

.11	monitor the broadcasts which they originate, to ensure that the warnings have been correctly broadcast;

.12	maintain records of source data relating to coastal warnings in accordance with the requirement of the national Administration of the National Coordinator; and

.13	take into account the need for contingency planning.

4	Navigational warnings for the World-Wide Navigational Warning Service

4.1	General

4.1.1	Navigational warnings are issued in response to SOLAS regulation V/4 and carry information which may have a direct bearing on the safety of life at sea. It is the fundamental nature of navigational warnings that they will often be based on incomplete or unconfirmed information and mariners will need to take this into account when deciding what reliance to place on the information contained therein.

4.1.2	In order to achieve the necessary impact on the mariner it is essential to present timely and relevant information in a consistent format that is CLEAR, UNAMBIGUOUS and BRIEF. This is ensured by using structured messages in standard formats, as shown in sections 6 and 7 of this Manual.

4.1.3	The resources employed by Administrations and the mariner are extremely limited. Thus only information which is vital to the safe conduct of ships should be transmitted. Notices to Mariners and other means exist for passing less urgent information to ships after they have reached port. Information of a purely administrative nature should never be broadcasted on the regular international navigational warning schedules.

4.1.4	There are four types of navigational warnings: NAVAREA warnings, Sub-area warnings, coastal warnings and local warnings. The WWNWS guidance and coordination are involved with only three of them:

.1	NAVAREA warnings;

.2	Sub-area warnings, and

.3	Coastal warnings

4.1.5	Navigational warnings should remain in force until cancelled by the originating coordinator. Navigational warnings should be broadcast for as long as the information is valid. However, if they are readily available to mariners by other official means, for example in Notices to Mariners, then after a period of six weeks they may no longer be broadcast.

4.1.6	The minimum information in a navigational warning which a mariner requires is hazard and position. It is usual, however, to include sufficient extra detail to allow some freedom of action in the vicinity of the hazard. This means that the message should give enough extra data for the mariner to be able to recognize the hazard and assess its effect upon their navigation.

4.1.7	If known, the duration of the event causing a navigational warning should be given in the text.

4.1.8	Some of the subjects for navigational warnings listed in paragraph 4.2.3 (e.g. drifting ice and tsunami warnings) may also be suitable for inclusion in METAREA warnings or forecasts. In this event, appropriate coordination between the relevant NAVAREA and METAREA Coordinators should occur.

4.2	NAVAREA warnings

4.2.1	NAVAREA warnings are concerned with the information detailed below which ocean-going mariners require for their safe navigation. This includes, in particular, new navigational hazards and failures of important aids to navigation as well as information which may require changes to planned navigational routes.

4.2.2	Coastal warnings are broadcast by the International NAVTEX service, or by EGC when implemented in lieu of NAVTEX. They are not normally re-broadcast as NAVAREA warnings unless deemed of such significance that the mariner should be aware of them before entering a NAVTEX service area. The National Coordinator will evaluate the significance of the information for consideration as a NAVAREA warning while the NAVAREA Coordinator will make the final determination.

4.2.3	The following subjects are considered suitable for broadcast as NAVAREA warnings. This list is not exhaustive and should be regarded only as a guideline. Furthermore, it presupposes that sufficiently precise information about the item has not previously been disseminated in a Notice to Mariners. Whenever possible, warnings concerning scheduled events, in particular those covered in 4.2.3.13, should be originated not less than five days in advance, and reference may be made to relevant national publications:

.1	casualties to lights, fog signals, buoys and other aids to navigation affecting main shipping lanes;

.2	the presence of dangerous wrecks in or near main shipping lanes and, if relevant, their marking;

.3	establishment of major new aids to navigation or significant changes to existing ones, when such establishment or change might be misleading to shipping;

.4	the presence of large unwieldy tows in congested waters;

.5	drifting hazards (including derelict ships, ice, mines, containers, other large items over 6 metres in length, etc.);

.6	areas where Search and Rescue (SAR) and anti-pollution operations are being carried out (for avoidance of such areas);

.7	the presence of newly discovered rocks, shoals, reefs and wrecks likely to constitute a danger to shipping, and, if relevant, their marking;

.8	unexpected alteration or suspension of established routes;

.9	cable or pipe-laying activities, seismic surveys, the towing of large submerged objects for research or exploration purposes, the employment of manned or unmanned submersibles, or other underwater operations constituting potential dangers in or near shipping lanes;

.10	the establishment of research or scientific instruments in or near shipping lanes;

.11	the establishment of offshore structures in or near shipping lanes;

.12	significant malfunctioning of radio-navigation services and shore-based MSI radio or satellite services;

.13	information concerning events which might affect the safety of shipping, sometimes over wide areas, e.g. naval exercises, missile firings, space missions, nuclear tests, ordnance dumping zones, etc;

.14	operating anomalies identified within ECDIS including ENC issues;

.15	acts of piracy and armed robbery against ships;

.16	tsunamis and other natural phenomena, such as abnormal changes to sea level;

.17	World Health Organization (WHO) health advisory information; and

.18	security-related requirements.

4.3	Sub-area warnings

4.3.1	Sub-area warnings broadcast information which is necessary for safe navigation within a Sub-area. They will normally include all subjects listed in 4.2.3 above, but will usually affect only the Sub-area.

4.4	Coastal warnings

4.4.1	Coastal warnings broadcast information which is necessary for safe navigation within areas seaward of the fairway buoy or pilot station, and should not be restricted to main shipping lanes. Where the area is served by NAVTEX, it should provide navigational warnings for the entire NAVTEX service area. Where the area is not served by NAVTEX, it is necessary to include all warnings relevant to the coastal waters up to 250 miles from the coast in the EGC service broadcast.

4.4.2	Coastal warnings should include at least the subjects in 4.2.3.

4.5	Local warnings

4.5.1	Local warnings broadcast information which covers inshore waters, often within the limits of jurisdiction of a harbour or port authority. They are broadcast by means other than NAVTEX or EGC, and supplement coastal warnings by giving detailed information within inshore waters.

5	The structure of navigational warnings

5.1	Numbering

5.1.1	Navigational warnings in each series should be consecutively numbered throughout the calendar year, commencing with 1/YY at 0000 UTC on 1 January.

5.1.2	Navigational warnings should be transmitted in reverse numerical order on scheduled broadcasts.

5.2	Language

5.2.1	All NAVAREA, Sub-area and coastal warnings should be broadcast only in English in the International NAVTEX and EGC services in accordance with IMO resolution A.706(17), as amended.

5.2.2	In addition to the required broadcasts in English, NAVAREA, Sub-area and coastal warnings may be broadcast in a national language using national NAVTEX and EGC services and/or other means.

5.2.3	Local warnings may be issued in the national language and/or in English.

5.3	"No warnings" message

5.3.1	When there are no navigational warnings to be disseminated at a scheduled broadcast time, a brief unnumbered message should be transmitted to identify the broadcast and advise the mariner that there is no navigational warning message traffic on hand.

5.4	Standard elements of messages

5.4.1	The minimum information which a mariner requires to avoid danger is:

HAZARD + POSITION

It is usual, however, to include amplifying remarks in order to provide sufficient extra details to clearly identify the significance of the hazard and to assist mariners in recognizing and assessing its effect upon their navigation. The time, date and duration of the event should be included if known.

5.4.2	A message can have up to three parts: Preamble, Warning, and Postscript. Sections 6 and 7 of the Manual give guidance on the correct way of phrasing each part of the warning to achieve maximum impact with minimum broadcast time.

5.4.3	The text of a navigational warning should contain specific message elements, identified and ordered by the reference numbers shown in figure 4 and expanded in section 6. The format and structure of a message should ensure that each message element begins on a new line.

5.4.4	The first words of the text of every warning message should always be the message series identifier, followed by the consecutive number; this may be preceded on a separate line by the time of origin of the message.

5.5	Message elements table

| MESSAGE ELEMENTS TABLE |
| --- |
| Part | Reference no. | Message elements |
| Preamble | 1 | Message series identifier |
|  | 2 | General area |
|  | 3 | Locality |
|  | 4 | Chart number |
| Warning | 5 | Key subject |
|  | 6 | Geographical position |
|  | 7 | Amplifying remarks |
| Postscript | 8 | Cancellation details |

Figure 4 – Message elements table showing standard elements for each part of a message

6	Message format of navigational warnings

Part 1 − preamble

Standard Message Element Reference 1 – MESSAGE SERIES IDENTIFIER

The first words of the text of every warning message should always be message series identifier followed by the consecutive number (N/YY) NAVAREA WARNING: NAVAREA III 496/14; NAVAREA VII 42/14 SUB-AREA WARNING: BALTIC SEA NAV WARN 9/14 COASTAL WARNING: AVURNAV TOULON 1015/14; WZ 345/14 Notes: i) The consecutive number re-starts each calendar year at 1/YY (Leading zeros are not mandatory). ii) For coastal warnings the consecutive number is not the same as the NAVTEX Number B3B4.

Standard Message Element Reference 2 – GENERAL AREA

The general area should be sufficient to identify which broad geographic region the message affects. The geographical name which is selected for the general area should be one that can be found on charts and in nautical publications. NAVAREA WARNING: "NORTH SEA" or "MALACCA STRAIT" would be correct; "NORTH AMERICA, EAST COAST" is too general. SUB-AREA WARNING: GULF OF FINLAND COASTAL WARNING: BAY OF BISCAY; CANTABRICO Notes: i) If appropriate, the established meteorological forecast areas as defined in WMO publication No.9 Volume D and also published in various nautical publications may be used. ii) For a NAVAREA-wide event, e.g. failure of satellite or terrestrial positioning systems, a navaid identification acronym "GPS", "LORAN", etc. should be used instead of a general area.

Standard Message Element Reference 3 – LOCALITY

The locality should be stated in terms which allow the mariner to identify warnings which affect their passage without having to plot them. Locality will only need to be stated when it is considered necessary to refine the general area. The geographical name which is selected as locality should be one that can be found on charts and in nautical publications. NAVAREA WARNING: NORTHERN GRAND BANKS PINANG APPROACH SUB-AREA WARNING: STORA MIDDELGRUND COASTAL WARNING: BARRA DE PARANAGUA – CANAL DA GALHETA Note: i) If appropriate the established meteorological forecast areas as defined in WMO publication No.9, Volume D and also published in various nautical publications may be used.

Standard Message Element Reference 4 – CHART NUMBER

For charted features, reference may be made to a national chart (not necessarily the largest scale) identified by the State abbreviation and chart number. Reference may also be made to an international chart number if one exists, consistent with UN LOCODE (See ISO 3166-1). For maritime operations, mobile hazards or events which affect a wider sea area a chart number may not be required. If a chart number is not used particular care should be taken in defining the general area and locality. NAVAREA WARNING: Chart IN 32 (INT 754)

Part 2 − warning

Standard Message Element Reference 5 – KEY SUBJECT

Key subjects referenced in paragraph 4.2.3 are considered suitable for broadcast as NAVAREA, SUB-AREA, or COASTAL Warnings. See examples in section 7.

Standard Message Element Reference 6 – GEOGRAPHICAL POSITION and GEOMETRY

Any key subject mentioned in Message Element 5, should have its geographical information mentioned by geographical positions, whenever possible. Geographical positions should always be given in degrees, minutes and decimal minutes up to the hundredths place where appropriate in the form: Latitude: DD MM.mmN or DD MM.mmS Longitude: DDD MM.mmE or DDD MM.mmW e.g. 32 18.65S 165 02.81E Note that leading zeros should always be included. Three digits are used for reporting degrees of longitude. Geographical positions should be given in WGS84., The same level of accuracy should always be quoted for both latitude and longitude.Any geographic position should have a geometry associated with it. Geometries should be a point, line, polygon, or circle. Often a navigational warning will require multiple geometries or a combination of geometries to properly represent the key subject. The following examples can be used: Point: IN [DD-MM.MMN/S DDD-MM.MMW/E]. Lines: ALONG A LINE JOINING [DD-MM.MMN/S DDD-MM.MMW/E], [DD-MM.MMN/S DDD-MM.MMW/E] Polygon: IN AREA BOUND BY [DD-MM.MMN/S DDD-MM.MMW/E], [DD-MM.MMN/S DDD-MM.MMW/E],\r\n [DD-MM.MMN/S DDD-MM.MMW/E]. Circular area: IN AREA WITHIN *XX* MILES OF [DD-MM.MMN/S DDD-MM.MMW/E] Multiple Point Geometries: IN: A. [DD-MM.MMN/S DDD-MM.MMW/E]. B. [DD-MM.MMN/S DDD-MM.MMW/E]. C. [DD-MM.MMN/S DDD-MM.MMW/E] Multiple line geometries: ALONG TRACKLINES JOINING: A. [DD-MM.MMN/S DDD-MM.MMW/E], [DD-MM.MMN/S DDD-MM.MMW/E]. B. [DD-MM.MMN/S DDD-MM.MMW/E], [DD-MM.MMN/S DDD-MM.MMW/E]. C. [DD-MM.MMN/S DDD-MM.MMW/E], [DD-MM.MMN/S DDD-MM.MMW/E]. Multiple Polygon (Area) Geometries: IN AREAS BOUND BY: A. [DD-MM.MMN/S DDD-MM.MMW/E], [DD-MM.MMN/S DDD-MM.MMW/E], [DD-MM.MMN/S DDD-MM.MMW/E]. B. [DD-MM.MMN/S DDD-MM.MMW/E], [DD-MM.MMN/S DDD-MM.MMW/E], [DD-MM.MMN/S DDD-MM.MMW/E]. C. [DD-MM.MMN/S DDD-MM.MMW/E], [DD-MM.MMN/S DDD-MM.MMW/E], [DD-MM.MMN/S DDD-MM.MMW/E]. Multiple Circular (Area) geometries: IN AREAS WITHIN *XX* MILES OF: A. [DD-MM.MMN/S DDD-MM.MMW/E], [DD-MM.MMN/S DDD-MM.MMW/E]. B. [DD-MM.MMN/S DDD-MM.MMW/E], [DD-MM.MMN/S DDD-MM.MMW/E]. C. [DD-MM.MMN/S DDD-MM.MMW/E], [DD-MM.MMN/S DDD-MM.MMW/E]. Combination Geometries: A. IN [DD-MM.MMN/S DDD-MM.MMW/E]. B. ALONG LINE JOINING [DD-MM.MMN/S DDD-MM.MMW/E], [DD-MM.MMN/S DDD-MM.MMW/E]. C. IN AREA BOUND BY [DD-MM.MMN/S DDD-MM.MMW/E], [DD-MM.MMN/S DDD-MM.MMW/E], [DD-MM.MMN/S DDD-MM.MMW/E]. D. IN AREA WITHIN *XXX* MILES OF [DD-MM.MMN/S DDD-MM.MMW/E] When defining the limits of a polygon, positions should be listed in a clockwise direction starting from the North West corner. With respect to the number of positions used to define a geometry, MSI providers should discuss with the source of the information, the minimum number of positions necessary to accurately represent the hazard while enabling ease of plotting for the mariner. Circular areas should be defined by a radius in nautical miles from a single point. Line geometries should have a minimum of two positions. Polygons should have a minimum of three positions. Positions are to be separated with commas and have a period after the final position. The use of the word "POSITION" or "POS" is not necessary.

Standard Message Element Reference 7 – AMPLIFYING REMARKS

Amplifying remarks may be used to provide sufficient extra details to clearly identify the significance of the hazard and to assist mariners in RECOGNIZING and ASSESSING its effect upon their navigation. Distances should be quoted in nautical miles and decimals. The time, date and duration of the event should be included if known. The time standard for Navigational Warnings should always be UTC (ref: 2.2.1.40) The accepted format for a Date Time Group (DTG) in the text of a message is as follows: DDHHMM UTC MoMoMo YYYY; e.g. 231642 UTC JUN 2022

Part 3 − POSTSCRIPT

| Standard Message Element Reference 8 – CANCELLATION DETAILS |
| --- |
| Cancellation details should be provided in a message that includes a definitive time frame; the cancellation time should be one hour after the event completes or one day later if the time is not accurately known. A reason for the cancellation should only be included if it is of benefit to the mariner and can be stated concisely. Cancellation messages may be "stand alone" and only concern the cancellation of a previous message, as in examples A and B below. When cancellation details relating to the subject of the message are included, it is recommended that paragraph numbers are used in order to clearly distinguish between the subject of the message and the cancellation details, as in example C below. When a message is immediately self cancelling, see example A below. The word "MESSAGE" can be abbreviated to MSG. |
| Examples | Comments |
| A. CANCEL NAVAREA IV 123/14 AND THIS MSG. | For multiple cancellations: CANCEL NAVAREA IV 123/14, 124/14 AND THIS MSG. |
| B. CANCEL ESTONIAN NAV WARN 87/14. ESTONIAN NOTICES TO MARINERS 520/14 REFERS. |  |
| C. 1. MESSAGE TEXT – EVENT OF KNOWN DURATION. 2. CANCEL THIS MSG DDHHMM UTC MoMoMo YYYY. | Choose a time for self-cancelling messages (example C) one hour after the event completes or one day later if time is not accurately known. |

7	Guidance and examples for navigational warnings by type of hazard (as listed in 4.2.3)

1	Casualties to lights, fog signals, buoys and other aids to navigation affecting main shipping lanes

The text of a navigational warning in this category should contain message elements 1, 2, 3, 4, 5, 6, 7 identified and ordered, as in the Message elements table, figure 4.

| LIGHTHOUSES, BEACONS |
| --- |
| Standard remarks | Comments |
| UNLIT | Use UNLIT in place of: Out, Extinguished, Not burning, Not working. See note iv. |
| LIGHT UNRELIABLE | Use LIGHT UNRELIABLE in place of: Weak, Dim, Low power, Fixed, Flashing incorrectly, Out of character, Incorrect colour of light, Sector limits unreliable. See note iv. |
| DAMAGED | Use only for major structural damage. See note vi. |
| DESTROYED | Do not use "Temporarily destroyed". See note iv. |
| RACON INOPERATIVE |  |
| RACON UNRELIABLE | Use UNRELIABLE in place of: Weak, Dim, Low power, Fixed. |
| CHANGED TO FL(3) 20 SECONDS 14 METRES 16 MILES | PERMANENT change of character. See notes v and viii. |
| TEMPORARILY CHANGED TO Q Y 12 MILES | TEMPORARY change. Do not use for listed reserve light. See note ix. |
| RELOCATED 0.3 MILES NORTH TO 63-14.8N 022-15.6E | Only use for established minor changes of position. Should quote former geographical position. Indicate former position by approximate direction and distance. See note x. |
| RE-ESTABLISHED | For previously charted as DESTROYED or TEMPORARILY REMOVED. See note xi. |
| PERMANENTLY REMOVED |  |
| TEMPORARILY REMOVED | Use when an aid is an aid is withdrawn for a limited period of time. |

Notes: Use CHARTED names, not LISTED names. LIGHT LIST number is not required. POSITION normally quoted to nearest whole minute for existing lights. The term "REPORTED" may be used for unconfirmed reports regarding lights. Always quote FULL LIGHT CHARACTERISTIC to avoid confusion over what has been changed. Damage to DAYMARKS is not usually worthy of a navigational warning. Damage to the structure may also be used as a qualifying remark to “UNLIT” or “LIGHT UNRELIABLE”. Do not initiate a navigational warning to request reports on an unwatched light. Use light descriptions as given in the LIGHTS − Glossary of terms table. Temporary use of a listed reserve light is to be expected. A warning would only be required due to a change of character, i.e. reduction of range. Distances should be quoted in nautical miles and decimals. The term "REPORTED" may be used for unconfirmed reports regarding lights. Chart INT 1 Abbreviations for light characters are only suitable for NAVTEX or EGC transmissions.

| LIGHTS − Glossary of terms |
| --- |
| CLASS OF LIGHT | Description for TEXT broadcasts |  |
| Fixed (steady light) | F |  |
| Occulting (total duration of light longer than total duration of darkness) Single-occulting Group-occulting Composite group-occulting | OC OC(2) OC(2+3) |  |
| Isophase (equal periods light and dark) | ISO |  |
| Flashing (total duration of light shorter than total duration of darkness) Single-flashing Long-flashing Group-flashing Composite group-flashing | FL LFL FL(3) FL(2+1) |  |
| Quick (50 to 79 – usually either 50 or 60 flashes per minute) Continuous quick Group quick Interrupted quick | Q Q(3) IQ |  |
| Very quick (80 to 159 – usually either 100 or 120 flashes per minute) Continuous very quick Group very quick Interrupted very quick | VQ VQ(3) IVQ |  |
| Ultra quick (160 or more usually 240 or 300 flashes per minute) Continuous ultra quick Interrupted ultra quick | UQ IUQ |  |
| Morse code | MO(K) |  |
| Fixed and flashing | FFL |  |
| Alternating | ALWR |  |

ELEVATION in METRES or FEET, e.g. 14 METRES or 21 FEET

PERIOD in SECONDS, e.g. 15 SECONDS or 15 SEC (Not S)

| RANGE in nautical miles |  | International abbreviations | RANGE for broadcast |
| --- | --- | --- | --- |
| Single range 2 ranges 3 or more ranges | e.g. e.g. e.g. | 15M 14/12M 22–18M | 15 MILES 14 AND 12 MILES 22 TO 18 MILES (Shortest range only will be sufficient) |

| BUOYS, LANBYS, SUPERBUOYS, LIGHT SHIPS |
| --- |
| Standard remarks | Comments |
| UNLIT | Use UNLIT in place of: Out, Extinguished, Not burning, Not working. See note iv. |
| LIGHT UNRELIABLE | Use LIGHT UNRELIABLE in place of: Weak, Dim, Low power, Fixed, Out of character, Irregular, Reduced power. |
| DAMAGED | No action for Topmark or Radar reflectors. Use only for major structural damage. |
| OFF STATION | Not in charted position, but still in the vicinity of original location. The actual position should be informed, if known. |
| MISSING | Completely absent fand position unknowned. |
| TEMPORARILY CHANGED |  |
| MOVED 0.3 MILES NORTH TO 63-14.8N 022-15.6E | Only use for established minor changes of position. Do not quote former geographical position. Indicate former position by approximate direction and distance. See note viii. |
| PERMANENTLY DISCONTINUED | Use for removed. |
| TEMPORARILY REMOVED | Use when an aid is temporarily removed (i.e. for maintenance purposes). |
| RE-ESTABLISHED | Use for previously charted or listed as DESTROYED or TEMPORARILY REMOVED. See note viii. |
| Notes: POSITION normally quoted to nearest whole minute for existing buoys, lanbys, superbuoys. Use light descriptions as given in the LIGHTS − Glossary of terms table. Do NOT describe the type of buoy, e.g., North Cardinal buoy, Port Hand buoy, unless the buoy is unnamed. UNLIT may be used to amplify "DAMAGED" as in "DAMAGED AND UNLIT". "LANBY" (Large Automated Navigational Buoy) or "SUPERBUOY" may be used in lieu of "BUOY" where appropriate. Chart INT 1 Abbreviations for light characters are only suitable for NAVTEX or EGC transmissions. The term "REPORTED" may be used for unconfirmed reports regarding buoys. Distances should be quoted in nautical miles and decimals. RE-ESTABLISHED is only appropriate for buoys which have previously been CHARTED or LISTED as DESTROYED or TEMPORARILY REMOVED. Navigational Warnings concerning such buoys are cancelled when the buoy is re-established. A new Navigational Warning is only required if the characteristics or position has changed. |

| BUOYAGE − Glossary of terms |
| --- |
| IALA BUOYAGE | Comments |
| PORT HAND BUOY STARBOARD HAND BUOY NORTH CARDINAL BUOY EAST CARDINAL BUOY SOUTH CARDINAL BUOY WEST CARDINAL BUOY ISOLATED DANGER BUOY SAFE WATER BUOY SPECIAL BUOY EMERGENCY WRECK MARKING BUOY | Full description of light and colour not required for IALA standard buoys. "Lightbuoy" may be used to indicate that the buoy is lit. |
| OTHER BUOYS |
| COLOURS | PATTERN | SHAPE/TYPE |
| RED BLACK WHITE GREEN YELLOW BLUE | CHEQUERED HORIZONTALLY STRIPED VERTICALLY STRIPED | CAN CONICAL (not OGIVAL or NUN) PILLAR SPAR SPHERICAL WRECK MOORING ODAS SPM DART |

EXAMPLES OF WARNINGS IN SECTION 4.2.3.1

| Message element | Example 1 – Buoy Missing |
| --- | --- |
| 1. Message series identifier | NAVAREA I 570/21 irish sea. northern ireland. CHART (INT ). hellyhunter lightBUOY 50-00.30n 006-02.00wMISSING. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 2 – Light Unreliable |
| --- | --- |
| 1. Message series identifier | NAVAREA III 451/21 western mediterranean sea. tunisia-north coast canis light 31-21.20n 010-07.40e unreliable. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 3 – Fog Signal Out of Service |
| --- | --- |
| 1. Message series identifier | NAVAREA I 1279/21 england – east Race Bank wind farm.CHART (INT ). fog signals inoperative at turbines in a. 53-14.90n 000-48.90e. b. 53-17.80n 000-46.30e. c. 53-21.10n 000-49.10e. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 4 – RACON temporary removal |
| --- | --- |
| 1. Message series identifier | NAVAREA v 678/21 western south atlantic. brazil-south coast. CHART (INT ). 1. racon at tramandai light 30-00.50s 050-08.2w inoperative until 29 mar 22. 2. cancel this msg 30 mar 22. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 5 – DGPS Station Removal |
| --- | --- |
| 1. Message series identifier | NAVAREA Iv 608/19 gulf of mexico. texas. CHART (INT ). angleton dgps station 29-18.10n 095-29.00w PERMANENTLY discontinued. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

2	The presence of dangerous wrecks in or near main shipping lanes and,
if relevant, their marking

The text of a navigational warning in this category should contain message elements 1, 2, 3, 4, 5, 6, identified and ordered, as in the Message elements table, figure 4.

| Standard remarks | Comments |
| --- | --- |
| DANGEROUS WRECK REPORTED | Reported position unconfirmed. See note i. |
| DANGEROUS WRECK LOCATED | Position confirmed, usually by survey. |

Notes: Position Approximate (PA) is not appropriate since all ''reported'' hazards will be of this nature. Remarks may be amplified e.g.: ". . . MARKED BY SOUTH CARDINAL BUOY 0.2 MILES SOUTHWARD'' or "GUARD SHIP VALIENT STATIONED CLOSE SOUTH EXHIBITING RACON MO(D)". The appropriate action to be taken on receipt of wreck information will depend on its location as well as its depth (and therefore relative danger to navigation). Generally, any wreck with a least depth of 30 m or less will need a navigation warning. Only quote position and depth to an accuracy of which you can be confident. For example, a wreck which has been fully surveyed may have its position quoted to two decimal places and depth to 0.1 m. On the other hand, in cases of reports of a ship which has been abandoned (in a known position) and has then sunk some hours later, the position and depth of water may be vague. The inclusion of the name of the wreck is not necessary; however, details of the type of ship may be included in the amplifying remarks if it is considered relevant, i.e. Super Tanker or Fishing Vessel with nets, etc.

EXAMPLES OF WARNINGS IN SECTION 4.2.3.2

| Message element | Example 1 – Dangerous Wreck |
| --- | --- |
| 1. Message series identifier | NAVAREA vIII 805/21 bay of bengal.off krishnapatnam. CHART (INT ). dangerous WRECK REPORTED IN 14-14.25n 080-09.85e. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 2 – Wreck Located with depth |
| --- | --- |
| 1. Message series identifier | NAVAREA xx 110/14 barents sea. CHART (INT ). WRECK, least depth 20 metres, LOCATED in 70-10.72n 032-56.55e. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 3 – Wreck with buoy |
| --- | --- |
| 1. Message series identifier | NAVAREA ix 279/21 iran. ras e jesk. CHART (INT ). dangerous wreck marked by south cardinal BUOY in 25-38.85n 057-39.51e. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

3	Establishment of major new aids to navigation or significant changes to existing ones, when such establishment or change might be misleading to shipping

The text of a navigational warning in this category should contain message elements 1, 2, 3, 4, 5, 6, identified and ordered, as in the Message elements table, figure 4.

| Standard remarks | Comments |
| --- | --- |
| ESTABLISHED | The use of the word ESTABLISHED conveys that the position and operation of the new or changed aid has been accurately confirmed by the appropriate competent authority. |
| RE-ESTABLISHED | For previously charted or listed as DESTROYED or TEMPORARILY REMOVED. See note ix. |

Notes: Use CHARTED names, not LISTED names. LIGHT LIST number is not required. POSITION normally quoted to nearest whole minute for existing lights. For new lights or changed positions, quote accurate CHARTED position; in degrees, minutes and decimal minutes (maximum 2 decimal places). Always quote FULL LIGHT CHARACTERISTIC to avoid confusion over what has been changed. Damage to DAYMARKS is not usually worthy a navigational warning. Use light descriptions as given in the LIGHTS – Glossary of terms table. Distances should be quoted in nautical miles and decimals. RE-ESTABLISHED is only appropriate for aids which have previously been CHARTED or LISTED as DESTROYED or TEMPORARILY REMOVED. Navigational Warnings concerning such aids are cancelled when the aid is re-established. A new Navigational Warning is only required if the characteristics or position has changed. For new buoys, lanbys, superbuoys or changed positions, quote accurate CHARTED position; in degrees, minutes and decimal minutes (maximum 2 decimal places). Chart INT 1 Abbreviations for light characters are only suitable for NAVTEX or SafetyNET transmissions. Voice broadcasts should be drafted using the terms for lights in the LIGHTS – Glossary of terms table.

EXAMPLES OF WARNINGS IN SECTION 4.2.3.3

| 7. Amplifying remarks |  |
| --- | --- |
| 8. Cancellation details |  |

| Message element | Example 1 – Light Established |
| --- | --- |
| 1. Message series identifier | NAVAREA VIIi 600/21 indian – west coast. valiyazhikal.. CHART (INT ). light, fl (3) W 2 Sec, ESTABLISHED in 09-08.41n 076-27.27e. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 2 – Buoy Established |
| --- | --- |
| 1. Message series identifier | NAVAREA V 556/21 BRAZIL./ ILHA de sao sebastiao. CHART (INT ). 1. Special buoy (odas), yellow, fl(5) y 20 sec, established in 24-28.03s 044-24.36w. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 3 – Range Reduced |
| --- | --- |
| 1. Message series identifier | NAVAREA viii 664/21 andaman sea. port blair. CHART (INT ). north point light 11-42.29n 092-45.219e range reduced to ten miles. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 4 – Sector Light |
| --- | --- |
| 1. Message series identifier | NAVAREA I 245/14 india-west coast. kanhoji angre. CHART (INT ). khanderi island light 18-42.20n 072-48.82e visible sector changed to white 181-018, red 018-181 degrees. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 5 – Light Change |
| --- | --- |
| 1. Message series identifier | NAVAREA III 863/21 WESTERN MEDITERRANEAN SEA ALGERIA CHART (INT ). ILE RACHGOUN LIGHT 35-19.45N 001-28.65W CHANGED TO F R. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 6 – AIS (Physical) |
| --- | --- |
| 1. Message series identifier | NAVAREA I 12/21 SCOTLAND, NORTH-EAST COAST. APPROACHES TO INVERNESS. CHART (INT ). AIS AID TO NAVIGATION MMSI 992351072 ESTABLISHED AT RIFF BANK EAST LIGHT-BUOY 57-38.38N 003-58.15W. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 7 – AIS (Virtual) |
| --- | --- |
| 1. Message series identifier | NAVAREA X 12/21 TORRES STRAITCAPE YORK NORTHWESTWARD. CHART (INT ). HERALD PATCHES BUOY 10-30.16S 142-21.50E TEMPORARILY REMOVED. VIRTUAL AIS AID TO NAVIGATION STARBOARD HAND MARK MMSI 995036022 ESTABLISHED AT THE SAME POSITION. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

4	The presence of large unwieldy tows in congested waters

The text of a navigational warning in this category should contain message elements 1, 2, 3, 5, 6, 7, identified and ordered, as in the Message elements table, figure 4. Element 4 (Chart number) is optional.

| Standard remarks | Comments |
| --- | --- |
| LENGTH OF TOW | Length of tow should be given in unit of measurement as advised by operator, usually cables or metres. |

Notes: Regular communications should be undertaken with the operators of the tow to ensure that the message is cancelled promptly as soon as the operation has been completed. Particular care should be taken when considering including a cancellation time or date for this category of message due to the many factors which could affect the completion of the operation. The name or type of the towing vessel and/or towed object should be included when known. Amplifying remarks regarding length and speed of tow need only be included if relevant or significant. Amplifying remarks regarding the necessity for "WIDE BERTH" should only be included if specifically requested by the operator as it will always be the case that the towing vessel and towed object will have restricted manoeuvrability. Navigational warning concerning towing operations in congested waters should include information for the next 72 hours and may be updated daily if necessary due to traffic density.

EXAMPLES OF WARNINGS IN SECTION 4.2.3.4

| Message element | Example 1 – Unwieldy Tow |
| --- | --- |
| 1. Message series identifier | NAVAREA II 465/21 portugal. off cape finisterre. CHART (INT ). towing operations in progress by tug eems towing m/v angon from leixoes to villagarcia, length of tow 400 metres. a wide berth is requested in the vicinity of trackline joining 38-22.60n 009-38.20w, 40-20.65n 010-03.88w, 42-12.87n 008-56.44w. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 2 – Drill Rig Under Tow |
| --- | --- |
| 1. Message series identifier | NAVAREA vii 342/21 south atlantic ocean. south africa to senegal. CHART (INT ). TUG sea alfa TOWING DRILL RIG petrobras 2000..departs cape town 34-52.45s 018-29.45e destination dakar 18-16.00s 004-28.00e.LENGTH OF TOW 500 METRES. wide berth requested |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 3 – Drill Rig Under Tow with trackline |
| --- | --- |
| 1. Message series identifier | NAVAREA XIII 54/21 SEA OF JAPAN. PROLIV LAPERUZA AND SAKHALIN NORTH EAST COAST. CHART (INT ). TUG TOWING DRILLING RIG PA-B 04,18 JUN 14 along trackline joinning 34-58.10N 128-48.35E, 52-55.90N 143-29.95E, 45-43.00N 141-58.02E, 45-45.00N 142-30.00E, 45-49.00N 143-19.00E, 45-55.00N 143-40.00E, 52-52.00N 143-39.53E, LENGTH OF TOW 1000 METRES SPEED 4.2 KNOTS. ONE MILE BERTH REQUESTED. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 4 – Tow with positional update |
| --- | --- |
| 1. Message series identifier | NAVAREA I 219/21 ENGLISH CHANNEL. DOVER STRAIT AND AT WEST HINDER TSS. CHART (INT ). 1. ALP DEFENDER TOWING MV SPIEGELGRACHT FROM LYME BAY, ENGLAND TO ZEEBRUGGE, BELGIUM IN VICINITY OF LINE JOINING: 50-10.1N 002-22.0W, 50-01.6N 002-17.1W, 50-27.8N 000-58.9E, 50-40.1N 001-20.9E, 50-54.1N 001-29.1E, 51-06.9N 001-47.7E, 51-22.0N 002-29.9E, 51-22.0N 002-40.7E AND 51-25.3N 002-48.7E. LENGTH OF TOW 800 METRES. 2. ALP DEFENDER IN 50-40.1N 001-20.9E AT 020200 UTC DEC 2021. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

5	Drifting hazards (including derelict vessels, ice, mines, containers, other large items etc.)

The text of a navigational warning in this category should contain message elements 1, 2, 3, 5, 6, 7, 8, identified and ordered, as in the Message elements table, figure 4. Element 4 (Chart number) is optional.

| Standard remarks | Comments |
| --- | --- |
| REPORTED | The time of the latest position report of the drifting hazard should ALWAYS be included, if available. |
| ADRIFT |  |
| ADRIFT IN VICINITY |  |
| DERELICT VESSEL | An abandoned vessel with no persons onboard. |

Notes: Warnings concerning drifting hazards should self-cancel within 72 hours. Drifting objects (with the exception of mines) of less than 6 metres in length are not normally considered to be hazards to navigation and therefore should not be promulgated.

EXAMPLES OF WARNINGS IN SECTION 4.2.3.5

| Message element | Example 1 – Container Adrift |
| --- | --- |
| 1. Message series identifier | navarea i 215/21.celtic sea. off ushant tss. CHART (INT ). 1. seven containers adrift in vicinity 48-40.00n 005-56.00w at 250856 UTC nov 21. 2. Cancel this msg 280856 UTC Jun 21. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 2 – Derelict Vessel Adrift |
| --- | --- |
| 1. Message series identifier | NAVAREA II 418/21 eastern north atlantic. madeira. CHART (INT ). 1. derelict sailing vessel ADRIFT IN VICINITY 32-46.60n 014-09.10w AT 031423 UTC nov 21. 2. CANCEL THIS MSG 061423 UTC JUL 21. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 3 – Fishing Net Adrift |
| --- | --- |
| 1. Message series identifier | NAVAREA xi 384/21 TIMOR SEA.CHART (INT ). FISHING NET, 50 METRES LONG, ADRIFT IN 09-27.60S 131-49.00E AT 230022 UTC NOV 21.CANCEL THIS MSG 260022 UTC NOV 21. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 4 – Object Adrift |
| --- | --- |
| 1. Message series identifier | NAVAREA IV 1044/21 western caribbean sea. colombia. CHART (INT ).1. partially submerged rectangular metallic object adrift in vicinity 12-58.31n 08-3.09w AT 190030 UTC nov 21. 2 CANCEL THIS MSG 220030 UTC nov 21. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 5 – Buoy Adrift |
| --- | --- |
| 1. Message series identifier | NAVAREA VIII 709/21. bay of bengal. off machilipatnam. CHART (INT ). 1. buoy adrift in vicinity 15-37.90n 082-10.3e on 04 mar 21. 2. CANCEL THIS MSG 07 mar 21. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 6 – Floating Debris |
| --- | --- |
| 1. Message series identifier | NAVAREA Vii 93/21 western indian ocean. off reunion. CHART (INT ). 1. wood debris adrift in 21-10.50s 055-12.33e at 291036 utc mar 21 2. CANCEL THIS MSG 011036 UTC apr 21. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 7 – Dead Head Adrift |
| --- | --- |
| 1. Message series identifier | NAVAREA iv 05/21 NoVA SCOTIA. off halifax. CHART (INT ). 1. dead head adrift in vicinity 44-30.00n 063-10.00w at 111029 utc sep. 2. CANCEL THIS MSG 141029 UTC sep 19. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 8 – Dead Whale Adrift |
| --- | --- |
| 1. Message series identifier | NAVAREA iv 05/21 northwest atlantic ocean. southeastern grand banks of newfoundland. CHART (INT ). 1. dead whale, 10 metres in length, reported adrift in vicinity 45-02.60n 048-52.80w at 032100 utc aug. 2. CANCEL THIS MSG 042100 UTC aug 19. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 9 – Mines |
| --- | --- |
| 1. Message series identifier | NAVAREA iX 71/20 southern red sea. farasan bank. 1. mines reported adrift in area bound by 16-45.6n 042-15.7e, 15-41.5n 042-39.4e, 15-54.0n 043-02.3e, 16-58.7n 042-35.1e. 2. mariners are requested to navigate with caution in the above area. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

6	Areas where search and rescue (SAR) and anti-pollution operations are 
being carried out (for avoidance of such areas)

The text of a navigational warning in this category should contain message elements 1, 2, 3, 5, 6, 7, identified and ordered, as in the Message elements table, figure 4. Element 4 (Chart number) is optional.

| Standard remarks | Comments |
| --- | --- |
| SAR OPERATION |  |
| ANTIPOLLUTION OPERATIONS |  |

EXAMPLES OF WARNINGS IN SECTION 4.2.3.6

| Message element | Example 1 – Search and Rescue Operations |
| --- | --- |
| 1. Message series identifier | NAVAREA xvI 25/14 peru. paita bay. CHART (INT ). 1. sar operation in progress in area bound by 05-27.32s 081-44.45w, 05-22.53s 081-27.95w, 05-49.57s 081-16.57w, 05-55.43s 081-32.42w. 2. all vessels not under instruction of the sar mission to keep a wide berth. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 2 – Search and Rescue Exercises |
| --- | --- |
| 1. Message series identifier | NAVAREA II 417/21 Morocco. off casablanca. 1. SEARCH AND RESCUE EXERCISE in progress until 041600 utc nov IN AREA BOUND BY 33-57.00N 008-03.03W, 34-04.80n 007-47.00W, 33-46.50n 007-36.00W, 33-39.00n 007-52.00w. 2. CANCEL THIS MSG 041700 UTC nov 21. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 3 – Anti-Pollution Operation |
| --- | --- |
| 1. Message series identifier | NAVAREA IV 6/21 GULF OF MEXICO. LOUISIANA. CHART (INT ). NAVIGATION PROHIBITED ON LOWER MISSISSIPPI RIVER, SOUTHWEST PASS BUOY TO MILE MARKER 98, DUE TO OIL SPILL RESPONSE OPERATIONS. CONTACT CAPTAIN OF THE PORT OF NEW ORLEANS FOR PERMISSION TO ENTER PROHIBITED AREA AND FOR UPDATED INFORMATION. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

7	The presence of newly discovered rocks, shoals, reefs and wrecks likely to 
constitute a danger to shipping, and, if relevant, their marking

The text of a navigational warning in this category should contain message elements 1, 2, 3, 4, 5, 6, identified and ordered, as in the Message elements table, figure 4.

| Standard remarks | Comments |
| --- | --- |
| LOCATED | The word LOCATED should only be used when the position of the hazard has been confirmed by a hydrographic survey. In all other cases the word REPORTED should be used. |
| REPORTED |  |
| LESS WATER REPORTED |  |
| SIGNIFICANTLY LESS WATER THAN CHARTED REPORTED |  |

Note: Due consideration should be taken over the inclusion of a specific depth over a newly discovered submerged hazard to navigation. The terms "LESS WATER REPORTED" or "SIGNIFICANTLY LESS WATER THAN CHARTED REPORTED" may be used prior to a report of survey of the area.

EXAMPLES OF WARNINGS IN SECTION 4.2.3.7

| Message element | Example 1 - Shoal |
| --- | --- |
| 1. Message series identifier | NAVAREA XVII 83/21 CANADIAN ARTIC. VICTORIA STRAIT. CHART (INT ). 27.8 METRE SHOAL LOCATED IN 68-58.95N 101-08.32W. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 2 – Shallow depth reported |
| --- | --- |
| 1. Message series identifier | NAVAREA V 372/21 NORTH PACIFIC OCEAN. off sao sebastiao. CHARt (INT ). depths reported: a. 15 metres in 24-00.75s 045-41.75w. b. 15 metres in 24-01.50s 045-23.90w. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 3 – Uncharted Rock |
| --- | --- |
| 1. Message series identifier | NAVAREA x 290/21 eastern indian ocean. australia-northwest coast. CHARt (INT ). uncharted rock reported in 16-53.06s 122-03.78e. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 4 – Submerged Object |
| --- | --- |
| 1. Message series identifier | NAVAREA xiiI 11/21 kara sea. zaliv chikhachyova. CHART (INT ). underwater obstruction LOCATED in 59-29.25N 140-54.76W. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 5 – Less Water Than Charted |
| --- | --- |
| 1. Message series identifier | NAVAREA XVI 98/21. PERU. BAHIA DEL CALLAO. CHARt (INT ). SIGNIFICANTLY LESS WATER THAN CHARTED REPORTED 11-59.89S 077-17.50W. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

8	Unexpected alteration or suspension of established routes

The text of a navigational warning in this category should contain message elements 1, 2, 3, 4, 5, 6, 7, identified and ordered, as in the Message elements table, figure 4.

EXAMPLES OF WARNINGS IN SECTION 4.2.3.8

| Message element | Example 1 – TSS Closure |
| --- | --- |
| 1. Message series identifier | NAVAREA XIX 15/22 BARENTS SEA 1. DUE TO ROCKET LAUNCHING THE USE OF THE FOLLOWING TRAFFIC SEPARATION SCHEME AND RECOMMENDED ROUTE ARE TEMPORARILY SUSPENDED FROM 191400 TO 221400 UTC FEB 22: A. TSS OFF VARDOE AND TSS OFF SLETTNES B. RECOMMENDED ROUTE BETWEEN TSS OFF VARDOE AND TSS OFF SLETTNES 2. NAVAREA XIX 14/22 3. CANCEL THIS MESSAGE 221400 UTC FEB 22 |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 2 – Compulsory Pilotage |
| --- | --- |
| 1. Message series identifier | NAVAREA X 234/22 AUSTRALIA NORTH COAST. TORRES STRAIT. CHART (INT ). COMPULSORY TORRES STRAIT PILOTAGE 10-32S 143-01E. MASTERS OF ships 70 METRES IN LENGTH OVERALL OR GREATER, AND ALL LOADED OIL, CHEMICAL TANKERS OR LIQUEFIED GAS CARRIERS ARE ADVISED THAT AUSTRALIAN LAW HAS BEEN AMENDED TO REQUIRE A LICENSED PILOT TO BE ENGAGED WHEN NAVIGATING THE TORRES STRAIT. ALL ships WILL BE AUTOMATICALLY CHECKED FOR COMPLIANCE AND THE FAILURE TO EMBARK A LICENSED PILOT MAY RESULT IN PROSECUTION. MASTERS OF ships SHOULD ENSURE CONTACT IS MADE IN A TIMELY MANNER WITH A PILOTAGE PROVIDER TO GUARANTEE A LICENSED PILOT IS BOOKED. THE FOLLOWING ARE THE CONTACT DETAILS OF THE TWO COMPANIES THAT CAN PROVIDE LICENSED PILOTS: AUSTRALIAN REEF PILOTS PTY LTD. – OPERATIONS@REEFPILOTS.COM.AU. TORRES PILOTS PTY LTD - OPERATIONS@TORRESPILOTS.COM.AU. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 3 – Temporary traffic lanes |
| --- | --- |
| 1. Message series identifier | NAVAREA V 206/22 BRAZIL - SOUTH COAST. CHART (INT ). 1. NAVAL CONTROL EXERCISE 091900 UTC TO 130300 UTC NOV 14 IN AREA BOUNDED BY: 31-33.00S 051-14.50W, 32-17.50S 050-07.00W, 33-51.00S 051-33.50W, 33-07.00S 052-38.00W. A. MERCHANT ships SHOULD CROSS MARITIME AREA USING THE FOLLOWING LANES: i) LANE COASTAL-1: (DIRECTION NE-SW) 32-00.00S 050-50.00W AND 33-20.00S 052-03.00W. ii) LANE COASTAL-2: (NC2-PORT RIO GRANDE) 32-38.00S 051-25.00W AND 32-15.00S 051-58.00W. B. WIDTH OF LANE IS SIX NAUTICAL MILES, THREE NAUTICAL MILES ON EACH SIDE OF THE TRACKLINE JOINING: i) NC1: 32-00.00S 050-50.00W. ii) NC2: 32-38.00S 051-25.00W. iii) NC3: 33-20.00S 052-03.00W. C. ACCESS AND DEPART RIO GRANDE PORT FROM: 32-15.00S 051-58.00W. D. ACCORDING TO ENTERING POSITION, MERCHANT shipS IN THE AREA SHOULD CALL LANE CONTROLLER ships BY VHF CHANNELS 16 AND 10, USING THE FOLLOWING: i) NC1 CONTROLLER OF MERCHANT SHIPS ENTERING AND LEAVING BY NORTHEAST OF AREA. ii) NC2 CONTROLLER OF MERCHANT SHIPS REQUESTING AND LEAVING FROM POINT OF ACCESS AND DEPART OF RIO GRANDE PORT. NC3 CONTROLLER OF MERCHANT SHIPS ENTERING AND LEAVING BY SOUTHWEST OF AREA. 2. CANCEL THIS MSG 130400 UTC NOV 14. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 4 – Port Closure |
| --- | --- |
| 1. Message series identifier | NAVAREA IV 785/21 DUE TO PASSAGE OF HURRICANE IDA: 1. THE FOLLOWING PORT(S) ARE CLOSED: A. PORT OF BATON ROUGE 30-27N 091-11W. B. PORT OF NEW ORLEANS 29-57N 090-03W. 2. THE FOLLOWING PORT(S) ARE OPEN WITH RESTRICTIONS: A. PASCAGOULA 30-21N 088-34W. B. PENSACOLA 30-24N 087-13W. 3. THE FOLLOWING PORT(S) HAVE RE-OPENED: A. MOBILE 30-41N 088-07W. 4. CURRENT PORT INFORMATION CAN BE FOUND AT HOMEPORT.USCG.MIL USING THE PORT DIRECTORY TAB. 5. CANCEL NAVAREA IV 780/21. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

9	Cable or pipe-laying activities, seismic survey, the towing of large submerged objects for research or exploration purposes, the employment of manned or unmanned submersibles, or other underwater operations constituting potential dangers in or near shipping lanes

The text of a navigational warning in this category should contain message elements 1, 2, 3, 5, 6, 7, identified and ordered, as in the Message elements table, figure 4. Element 4 (Chart number) is optional.

| Standard remarks | Comments |
| --- | --- |
| CABLE LAYING OPERATIONS IN PROGRESS |  |
| SEISMIC SURVEY IN PROGRESS |  |
| UNDERWATER OPERATIONS | Do not use "SUBMARINE OPERATIONS" |
| SCIENTIFIC OPERATIONS IN PROGRESS |  |

Notes: Regular communications should be undertaken with the operators to ensure that the message is cancelled promptly as soon as the operation has been completed. Particular care should be taken when considering including a cancellation time or date for this category of message due to the many factors which could affect the completion of the operation. Use "REQUESTED" when wide berth is for the benefit of the ship which is performing the operation. Use "ADVISED" when the operations create a significant hazard.

EXAMPLES OF WARNINGS IN SECTION 4.2.3.9

| Message element | Example 1 – Hydrographic Survey |
| --- | --- |
| 1. Message series identifier | NAVAREA III 821/21 eastern mediterranean sea. cyprus. CHART (INT ). 1. hydrographic survey in progress until 17 nov by m/v nautical geo in area bound by 34-18.65n 033-08.00e, 34-24.23n 032-20.74e, 34-20.11n 032-20.63e, 34-13.36n 033-07.27e. wide berth requested. 2. cancel this msg 18 nov 21. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 2 – Scientific Survey |
| --- | --- |
| 1. Message series identifier | NAVAREA xv 95/21 eastern south pacific. chile CHART (INT ). 1, scientific operations by m/v abate molina from 090345 utc may to 07000 utc jun in area bound by 32-10.00s 071-41.00w, 38-02.00s 074-05.00w, 40-20.00s 074-40.00w, 40-20.00s 073-47.00w. wide berth requested. 2. cancel this msg 070100 utc jun 21. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 3 – Seismic Survey |
| --- | --- |
| 1. Message series identifier | NAVAREA XIII 43/21 sea of okhotsk. CHART (INT )1. seismic SURVEY OPERATIONS IN PROGRESS UNTIL 31 AUG BY M/V VYACHESLAV TIKHONOV AND M/V PX GEO TOWING 4050 METER LONG CABLES IN AREA BOUND BY 52-46.56N 143-22.21E, 52-45.73N 143-57-51E, 52-02.62N 143-54.99E, 52-03.61N 143-11.28E. FOUR MILE BERTH REQUESTED. 2. CANCEL THIS MSG 01 SEP 21. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 4 – Dredging Operations |
| --- | --- |
| 1. Message series identifier | NAVAREA xVIII 42/21 huson bay. canada. CHART (INT ). dredging operations 1100 utc to 2300 utc daily until further notice BY tugs poinciana and manuels river in vicinity of 47-12.96n 061-59.09w. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 5 -Pipe Laying Operations |
| --- | --- |
| 1. Message series identifier | NAVAREA iii 795/21 mediterranean sea. tunisia. CHART (INT ). 1. PIPELAYING OPERATIONS IN PROGRESS UNTIL 13 fen 22 BY M/V ievoli ivori in area bound by 37-01.01n 011-04.22e, 37-12.80n 011-15.51e, 37-12.80n 011-15.10e, 37-25.47n 011-42.71e. one mile berth requested. 2. cancel this msg 14 feb 22.. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 6 – UNMANNED OPERATIONS |
| --- | --- |
| 1. Message series identifier | NAVAREA IV 1123/21 north ATLANTIC OCEAN. CHART (INT ). 1. unmanned atlantic crossing by four metre m/v mahi two in vicinity of trackline joining 19-38.30n 035-00.00w, 18-50.01n 036-36.39w, 17-24.81n 044-29.68w, 17-04.67n 051-21.64w, 16-23.00n 059-04.41w. vessels in the vicinity requested to keep a sharp look out. 2. for the most current position of m/v mahi two, go to projectmahi.datylon.com |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 7 -Cable Laying Operations |
| --- | --- |
| 1. Message series identifier | NAVAREA I 193/21 western approaches to the english channel. CHART (INT ). 1. cable laying OPERATIONS IN PROGRESS by m/v ile de brehat in vicinity of lines joining: a. 49-00.80n 007-55.60w, 49-02.20n 007-53.90w. b. 49-05.10n 007-52.40w, 49-06.00n 007-52.60w. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 8 -Ship to Ship Operations |
| --- | --- |
| 1. Message series identifier | NAVAREA IV 20/14 western south atlantic. east of paranagua. CHART (INT ). 1. ship to ship OPERATIONS 290900 dec 21 to 010900 utc jan 22 Between M/V lena knutsen and M/V saveiros in 10-02.28N 060-15.08W. . 2. CANCEL THIS MESSAGE 011000 UTC jan 22. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 9 -Diving Operations |
| --- | --- |
| 1. Message series identifier | NAVAREA IV 20/14 western south ATLANTIC. east of ponta do ubu. CHART (INT ). 1. diving OPERATIONS IN PROGRESS 1100 utc to 2100 utc daily 23 to 26 oct in 20-50.33s 040-03.52w. WIDE BERTH REQUESTED. 2. CANCEL THIS MESSAGE 262200 UTC oct 21. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

10	The establishment of research or scientific instruments in or near shipping lanes

The text of a navigational warning in this category should contain message elements 1, 2, 3, 4, 5, 6, identified and ordered, as in Message elements table, figure 4.

EXAMPLES OF WARNINGS IN SECTION 4.2.3.10

| Message element | Example 1 – Scientific Mooring |
| --- | --- |
| 1. Message series identifier | NAVAREA ii 251/21 bay of biscay. spain. CHART (INT ). 1. scientific moorings established until 01 mar by m/v atalante in: a. 46-06.00n 006-47.00w. b. 44-10.00n 002-10.00w. 2. cancel this msg 02 mar 22. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 2 – Tide Gauge |
| --- | --- |
| 1. Message series identifier | NAVAREA x 180/21 arafura sea. australia-north coast. CHART (INT ). turtle tide guague in 10-31.30s 141-12.70e unreliable. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 3 – Scientific Buoy |
| --- | --- |
| 1. Message series identifier | NAVAREA IV 333/21 NORTH ATLANTIC OCEAN. GRAND BANKS OF NEWFOUNDLAND. CHART (INT ). DART BUOY ESTABLISHED 44-04.58N 055-12.80W. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 4 – Acoustic Recorder |
| --- | --- |
| 1. Message series identifier | NAVAREA xvII 55/19 IONIAN SEA. CENTRAL. CHART (INT ). 1. acoustic seabed instruments deployed from 231500 utc to 242000 utc mar 19 in: a. 44-41.46n 063-37.71w. b, 44-41.46n 063-38.38w. c. 44-41.32n 063-38.04w. 2. cancel this msg 242100 mar 19/ |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

11	The establishment of offshore structures in or near shipping lanes

The text of a navigational warning in this category should contain message elements 1, 2, 3, 4, 5, 6, identified and ordered, as in the Message elements table, figure 4.

Note: It is not necessary to number or alphabetize the list of structures.

EXAMPLES OF WARNINGS IN SECTION 4.2.3.11

| Message element | Example 1 – Drill rig on location |
| --- | --- |
| 1. Message series identifier | NAVAREA x 5/21 indian ocean. australia-northwest coast. CHART (INT ). drill rig valaris ms-1 in 20-57.27s 114-52.10e 2.5 nm clearance requested. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 2 – Drilling site operations |
| --- | --- |
| 1. Message series identifier | NAVAREA VII 358/21 SOUTH ATLANTIC OCEAN. CHART (INT ). RIG LIST: 05-08.58S 011-55.15E PRIDE CAPINDA. 05-33.08S 011-27.08E PRIDE VENEZUELA. 06-03.81S 011-05.86E GSF RIG 140. 06-19.02S 011-03.23E KIZOMBA A (NEW). 06-20.15S 011-18.01E PRIDE SOUTH PACIFIC. 06-20.92S 011-09.22E KIZOMBA B. 07-40.05S 011-45.08E PRIDE AFRICA. 07-43.00S 011-43.00E PRIDE ANGOLA. 35-08.86S 022-31.81E PRIDE SOUTH SEAS. 35-13.99S 021-29.89E ORCA. FOUR MILE EXCLUSION ZONE ABOUT RIGS DUE TO PRESENCE OF UNLIT ANCHOR MARKING BUOYS. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| 2. General area |  |
| --- | --- |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 3 – Platform Established |
| --- | --- |
| 1. Message series identifier | NAVAREA VI 116/21 URUGUAY. MONTEVIDEO. CHART (INT ). PLATFORM m4/25 ESTABLISHED 35-00N 056-20W. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

12	Significant malfunctioning of radio-navigation services and shore-based 
maritime safety information radio or satellite services

The text of a navigational warning in this category should contain message elements 1, 5, identified and ordered, as in the Message elements table, figure 4.

| Standard remarks | Comments |
| --- | --- |
| OFF AIR | Do not use "Until Further Notice" since the fact that the event is complete will always be apparent from the cancellation message. Back-up facility should be included if one is available. |
| UNSTABLE |  |
| REDUCED POWER |  |
| INOPERATIVE |  |
| UNUSABLE |  |
| DISCONTINUED |  |

Notes: Warnings concerning long-range electronic navigational aids will not normally need the message elements; General area, Locality or Chart number. If a definitive time is quoted for the outage, the message cancels one hour after event completes.

EXAMPLES OF WARNINGS IN SECTION 4.2.3.12

| Message element | Example 1 – VHF Services off air |
| --- | --- |
| 1. Message series identifier | NAVAREA I 116/22 gmdss. mrcc shetland vhf r/t and dsc services to dunnet head site, 58-40.3n 003-22.6w off air. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 2 – MF Services off air |
| --- | --- |
| 1. Message series identifier | WZ 169/22 GMDSS. MRCC STORNOWAY. MF R/T AND DSC SERVICES FROM BUTT OF LEWIS SITE, 58-27.7N 006-13.9W, OFF AIR. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 3 – NAVTEX off air |
| --- | --- |
| 1. Message series identifier | NAVAREA I 53/22 GMDSS 1. NAVTEX STATION CULLERCOATS (G), 55-04N 001-28W, OFF AIR DAILY BETWEEN 0900 AND 1530 UTC FROM 12 TO 13 JAN 2022. 2. CANCEL THIS MESSAGE 131630 UTC JAN 2022. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 4 – NAVTEX unstable |
| --- | --- |
| 1. Message series identifier | NAVAREA I 018/22 GMDSS. BALTIC SEA. 1. NAVTEX STATIONS GRIMETON (I), 57-06.3N 012-23.4E, AND GISLOVSHAMMAR (J), 55-29.4N 014-18.9E, OFF AIR. 2. BALTIC SEA NAVIGATION WARNING 007/22 REFERS. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 5 – Seasonal change |
| --- | --- |
| 1. Message series identifier | NAVAREA XVIII 135/21 CANADIAN ARCTIC IQALUIT MCTS 1. REMOTE CONTROL FACILITIES LOCATED AT CORAL HARBOUR OFF AIR FOR THE 2021 NAVIGATIONAL SEASON 161330 UTC NOV 21. 2. CANCEL NAVAREA XVIII 130/21. 3. CANCEL THIS MSG AT 292330 UTC NOV 21 |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |
| Message element | Example 5 – GMDSS Services |
| 1. Message series identifier | NAVAREA XVIII 102/21 CANADIAN ARCTIC GMDSS IQALUIT MCTS ALL GMDSS DSC, NBDP, AND RT TRANSMIT FACILITIES LOCATED AT IQALUIT OFF AIR 212300 UTC SEP 21. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 6 – GPS Disruption |
| --- | --- |
| 1. Message series identifier | NAVAREA X 151/21 POSSIBLE GPS DISTRUPTION DUE TO MILITARY EXERCISES: FROM 191400 UTC JUL 2021 TO 271400 UTC JUL 2021 IN AREA WITHIN 15 NM OF 20-00.4S 148-15.9E. FROM 261400 UTC JUL 2021 TO 311400 UTC JUL 2021 IN AREA WITHIN 15NM OF 18-43.2S 146-17.8E. REPORT SAFETY CONCERNS TO JRCC AUSTRALIA: PHONE: +61262306811 EMAIL: RCCAUS@AMSA.GOV.AU CANCEL THIS MSG 311500 UTC JUL 2021. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

13	Information concerning events which might affect the safety of shipping, sometimes over wide areas, e.g. naval exercises, missile firings, space missions, nuclear tests, ordnance dumping zones, etc.

The text of a navigational warning in this category shall contain message elements 1, 2,  5, 6, 7, 8, identified and ordered, as in the Message elements table, figures 3, 4. Element 4 (Chart Number) is optional.

Note: i) Whenever possible, warnings concerning scheduled events should be originated not less than five days in advance, ii) Warnings may include reference to relevant national publications and contact information. iii) Warnings should cancel one hour following the end of an exercise or operation in message element 8.

EXAMPLES OF WARNINGS IN SECTION 4.2.3.13

| Message element | Example 1 – Firing Operations |
| --- | --- |
| 1. Message series identifier | NAVAREA XVI221/21 EASTERN SOUTH PACIFIC. PERU. CHART ____ (INT ____). 1. NAVAL FIRING EXERCISES 161400 UTC to 170000 UTC IN AREA BOUND BY 11-35.00S 077-43.00W,11-35.00S 077-33.00W, 11-47.00S 077-33.00W, 11-47.00s 077-43.00W. 2. CANCEL THIS MESSAGE 181700 UTC JAN 14. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 2 – Blasting Operation |
| --- | --- |
| 1. Message series identifier | NAVAREA VIII 864/21 INDIA WEST COAST. OFF ALAPPUZHA. 1. SUBSURFACE EXPLOSIVE OPERATIONS SCHEDULED 0330 TO 0630 UTC DAILY ON 17 AND 21 DEC IN AREA WITHIN FIVE MILES OF 09-19.58N 075-46.8E. 2. CANCEL THIS MSG 210730 UTC DEC 21. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 3 – Fallout Hazard (Space Debris) |
| --- | --- |
| 1. Message series identifier | NAVAREA XIV 218/21. SOUTHwest PACIFIC basin. 1. HAZARDOUS OPERATIONS, SPACE DEBRIS scheduled FROM 062240 UTC TO 200925 UTC DEC IN AREAs BOUNDED BY: a. 41-06.00s 176-18.00w, 39-54.00s 175-42.00w, 40-36.00s 171-06.00w, 41-54.00s 171-18.00w. b. 42-36.00s 163-06.00w, 41-36.00s 163-12.00w, 41-42.00s 158-00.00w, 42-36.00s 157-48.00w. 2. CANCEL THIS MSG 201025 UTC dec 21. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 4 – Military Exercise |
| --- | --- |
| 1. Message series identifier | NAVAREA VIII 857/21. ARABIAN SEA. OFF BALASORE. 1. iNDIAN AIR FORCE EXERCISE SCHEDULE ON 0430 TO 0630 UTC AND 0830 TO 1030 20 THRU 22 DEC IN AREA BOUND BY 21-41.00N 087-44.00E, 20-57.00N 086-53.00E 20-56.00N 086-55.00E. 2. CANCEL THIS MSG 221130 UTC DEC 21. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 5 – Fallout Hazard (Rocket Launch) |
| --- | --- |
| 1. Message series identifier | NAVAREA iv 1092/21 western north atlantic. flordia. 1. ROCKET LAUNCHING 090600 utc to 090753 utc dec, alternate 0600 utc to 0753 utc daily 10 thru 14 dec in area bound by 28-39.03n 080–37.70w, 28-41.00n 080-20.00w, 28-38.00n 079-42.00w, 28-35.00n 079-43.00w,28-33.00n 080-17.00w, 28-34.78n 080-34.08w.2. CANCEL THIS MESSAGE 140853 UTC nov 21. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

14	 Operating anomalies identified within ECDIS including ENC issues

The text of a navigational warning in this category should contain message elements 1, 5, 7, identified and ordered, as in the Message elements table, figure 4. Elements 2, 3 and 4 are optional.

Note: A number of ECDIS operating anomalies have been identified. Due to the complex nature of ECDIS, and in particular because it involves a mix of hardware, software and data, it is possible that further anomalies may exist. NAVAREA Coordinators should ensure that mariners are aware of the potential for some ECDIS to exhibit display and behaviour anomalies i.e. alarm, and provide manufacturers guidance if appropriate.

EXAMPLES OF WARNINGS IN SECTION 4.2.3.14

| Message element | Example 1 – ECDIS Anomalies |
| --- | --- |
| 1. Message series identifier | NAVAREA XVII 82/12 DISPLAY ANOMALIES IN SOME ECDIS. SOME ELECTRONIC CHART DISPLAY AND INFORMATION SYSTEMS (ECDIS) MAY EXHIBIT OPERATING ANOMALIES. THE INTERNATIONAL MARITIME ORGANIZATION'S CIRCULAR SN.1/CIRC.312 (HTTP://WWW.IMO.ORG/OURWORK/CIRCULARS/PAGES/IMODOCS.ASPX (REGISTRATION REQUIRED)) LISTS IDENTIFIED ANOMALIES, THEIR CHARACTERISTICS AND REMEDIAL ADVICE. MARINERS ARE REMINDED THAT THEY SHOULD ACCESS THE INTERNATIONAL HYDROGRAPHIC ORGANIZATION (IHO) DATA PRESENTATION AND PERFORMANCE CHECK (DPPC) DATASET (http://www.iho.int/srv1/index.php?option=com_content&view=article&id=585:news&catid=166:1news-links&Itemid=828) AND ENSURE THAT ALL INSTALLED ECDIS UNITS ARE CHECKED. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 2 – ENC Anomaly |
| --- | --- |
| 1. Message series identifier | NAVAREA XVIII 94/18 CANADIAN ARCTIC SIMPSON STRAIT ETA ISLAND CHART CHS 7736 / ENC CA473317THE CHARTED ORIENTATION OF THE RANGE LINE FOR SIMPSON STRAIT #6 RANGE (WEST-FACING RANGE MARKS ON ETA ISLAND) IS IN ERROR. THE CORRECT VISUAL RANGE LINE PASSES 94 METRES SOUTH OF THE ADVERTISED POSITION OF SIMPSON STRAIT BUOY #11 ON HEADINGS 289/109 DEGREES TRUE. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 3 – ENC not safe for navigation |
| --- | --- |
| 1. Message series identifier | NAVAREA II 199/18 IROISE DUE TO A PRODUCTION PROBLEM THAT HAS CAUSED DISPLACED FEATURES, IT HAS BEEN DETERMINED THAT ELECTRONIC NAUTICAL CHART 7066 FR (1800 INT) IS NOT TO BE USED FOR NAVIGATION OR SITUATIONAL AWARENESS. A REVIEW IS IN PROCESS TO ADDRESS THIS SITUATION. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

15	Acts of piracy and armed robbery against ships

The text of a navigational warning in this category should contain message elements 1, 2, 3, 5, 6, 7, 8 identified and ordered, as in the Message elements table, figure 4.

| Standard remarks | Comments |
| --- | --- |
| ACT OF PIRACY | Act of Piracy is defined in UNCLOS article 101 |
| ARMED ROBBERY | Armed robbery is defined IMO Resolution A.1025(26) |

EXAMPLES OF WARNINGS IN SECTION 4.2.3.15

| Message element | Example 1 - Armed Robbery |
| --- | --- |
| 1. Message series identifier | NAVAREA XV 306/22 peru. callao ANCHORAGE. armed robbery. 1. m/v at anchor boarded by seven ARMED ROBBERs IN 12-01.05s 077-11.37w AT 280710 utc jan. robbers attacked crew, stole ship property and escaped. VESSELS ARE ADVISED TO KEEP CLEAR OF THIS POSITION AND TO EXERCISE EXTREME CAUTION. REPORTS TO IMB PIRACY REPORTING CENTER, PHONE: 603 2031 0014, 603 2078 5763, FAX: 603 2078 5769, E-MAIL: IMBKL@ICC-CCS.ORG, PIRACY@ICC-CCS.ORG. 2. CANCEL THIS MSG 040710 utc FEB 22. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 2 - Piracy |
| --- | --- |
| 1. Message series identifier | NAVAREA II 223/21 GULF OF GUINEA. NIGERIA. Act of PIRACY. 1. M/V ATTACKED IN 02-49N 002-31E AT 061700 UTC JUN 21. VESSELS ARE ADVISED TO KEEP CLEAR OF THIS POSITION AND TO EXERCISE EXTREME CAUTION. REPORT TO MDAT-GOG, PHONE: +33 2 98 22 88 88 E-MAIL: WATCHKEEPERS@MDAT-GOG.ORG 2. CANCEL THIS MSG 131930 UTC JUN 21. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 3 – Piracy (Kidnapping) |
| --- | --- |
| 1. Message series identifier | NAVAREA ii 2031/20 gulf of guinea. nigeria. OFF BAYELSA. act of piracy. 1. m/v attacked by pirates in 04-28.15N 005-31.17E at 261258 utc nov. ten persons kidnapped. VESSELS ARE ADVISED TO KEEP CLEAR OF THIS POSITION AND TO EXERCISE EXTREME CAUTION. REPORTS TO IMB PIRACY REPORTING CENTER, PHONE: 603 2031 0014, 603 2078 5763, FAX: 603 2078 5769, E-MAIL: IMBKL@ICC-CCS.ORG, PIRACY@ICC-CCS.ORG. 2. CANCEL THIS MSG 031200 utc dec 20. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 4 – Piracy (Hijacking) |
| --- | --- |
| 1. Message series identifier | NAVAREA IX 3048/19 RED SEA. ERITREA. act of piracy. 1. M/V HIJACKED by six armed pirates IN 16-30N 040-08E AT 170338 utc SEP. VESSELS ARE ADVISED TO KEEP CLEAR OF THIS POSITION AND TO EXERCISE EXTREME CAUTION. REPORTS TO IMB PIRACY REPORTING CENTER, PHONE: 603 2031 0014, 603 2078 5763, FAX: 603 2078 5769, E-MAIL: IMBKL@ICC-CCS.ORG, PIRACY@ICC-CCS.ORG. 2. CANCEL THIS MSG 240237 utc SEP 19. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 5 – Piracy (Mothership Activity) |
| --- | --- |
| 1. Message series identifier | NAVAREA iI 4250/21. GULF OF GUINEA. OFF GHANA. ACT OF PIRACY. SUSPECTED MOTHERSHIP ACTIVITY IN VICINITY 01-50N 001-11E AT 190930 UTC OCT. 24 METER TUG, WHITE HULL AND BLACK SUPERSTRUCTURE, UNNAMED AND NOT TRANSMITTING AIS. VESSELS ARE ADVISED TO KEEP CLEAR OF THIS POSITION AND TO EXERCISE EXTREME CAUTION. REPORTS TO IMB PIRACY REPORTING CENTER, PHONE: 603 2031 0014, 603 2078 5763, FAX: 603 2078 5769, E-MAIL: IMBKL@ICC-CCS.ORG, PIRACY@ICC-CCS.ORG. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

16	Tsunamis and other natural phenomena, such as abnormal changes to sea level

The text of a navigational warning in this category should contain message elements 1, 2, 5, identified and ordered, as in the Message elements table, figure 4.

EXAMPLES OF WARNINGS IN SECTION 4.2.3.16

| Message element | Example 1 – Tsunami (General) |
| --- | --- |
| 1. Message series identifier | NAVAREA XI 0251/21 PACIFIC OCEAN. PHILLIPINES. TSUNAMI WARNING. EARTHQUAKE, MAGNITUDE 7.2, OCCURRED AT 111746 UTC AUG IN 06-30N 126-48E. TSUNAMI WAVES ARE POSSIBLE WHICH COULD CAUSE DAMAGE TO THE COASTS AND ISLANDS OF THE PHILLIPINES. VESSELS IN VICINITY OF COASTAL AREAS ARE ADVISED TO USE CAUTION. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 2 – Tsunami (Earthquake) |
| --- | --- |
| 1. Message series identifier | NAVAREA XII 365 /21 aLASKA COASTAL AREAS. TSUNAMI WARNING. EARTHQUAKE WITH MAGNITUDE OF 8.2 HAS OCCURRED IN VICINITY 55-18N 157-48W AT 290616Z JUL. A TSUNAMI HAS BEEN GENERATED WHICH COULD CAUSE DAMAGE TO COASTS OF SOUTH ALASKA, THE ALASKA PENINSULA AND THE ALEUTIAN ISLANDS. TSUNAMI WAVE HEIGHTS CANNOT BE PREDICTED AND MAY BE A SERIES OF WAVES WHICH COULD BE DANGEROUS FOR SEVERAL HOURS AFTER THE INITIAL WAVE ARRIVAL. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 3 – Tsunami (Arrival Times) |
| --- | --- |
| 1. Message series identifier | NAVAREA IV 702/21 CARIBBEAN SEA. HAITI. TSUNAMI WARNING. 1. EARTHQUAKE WITH MAGNITUDE OF 7.2 OCCURRED IN 18-36N 073-30W AT 141229Z AUG. TSUNAMI WAVES ARE POSSIBLE WHICH COULD CAUSE DAMAGE TO THE SURROUNDING COASTS. 2. TSUNAMI ACTIVITY IS FORECASTED TO START AT THE FOLLOWING TIMES: A. JEREMIE 18-36N 074-06W AT 1239Z. B. JACAMEL 18-06N 072-30W AT 1318Z. C. PORT AU PRINCE 18-30N 072-24W AT 1328Z. 3. TSUNAMI WAVES REACHING THREE METERS ABOVE THE TIDE LEVEL ARE POSSIBLE AND MAY BE A SERIES OF WAVES WHICH COULD BE DANGEROUS FOR SEVERAL HOURS AFTER THE INITIAL WAVE ARRIVAL. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 4 – Volcanic Activity |
| --- | --- |
| 1. Message series identifier | NAVAREA IV 301/21 EASTERN CARIBBEAN SEA. SAINT VINCENT. vOLCANIC ERUPTION. RESTRICTED AREA DUE TO VOLCANIC ACTIVITY IN AREA BOUND BY 13-15.00N 061-19.60W, 13-18.00N 061-18.50W, 13-22.08N 061-15.38W, 13-26.00N 061-09.91W, 13-22.29N 061-04.90W, 13-19.88N 061-04.10W, 13-14.41N 061-03.90W. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 5 – Tsunami (Volcanic Activity) |
| --- | --- |
| 1. Message series identifier | NAVAREA XIV 4/224 SOUTH PACIFIC OCEAN. 1. TSUNAMI THREAT MESSAGE ISSUED BY PACIFIC TSUNAMI WARNING CENTRE AT 152006 UTC JAN 22. A VOLCANIC ERUPTION HAS OCCURRED IN VICINITY 20-30S 175-24W LOCATION TONGA AT 150427 UTC JAN 22. HAZARDOUS TSUNAMI WAVES FROM THIS EARTHQUAKE ARE POSSIBLE WITHIN THE NEXT THREE HOURS. 2. CANCEL THIS MSG 152336 UTC JAN 22. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

17	World Health Organization (WHO) health advisory information

The text of a navigational warning in this category should contain message elements 1, 2, 3, 5, identified and ordered, as in the Message elements table, figure 4.

EXAMPLES OF WARNINGS IN SECTION 4.2.3.17

| Message element | Example 1 – WHO Advisory |
| --- | --- |
| 1. Message series identifier | NAVAREA XVIII 69/21 CANADA 1. ON 11 MARCH 2020, THE WORLD HEALTH ORGANIZATION DECLARED THAT THE GLOBAL OUTBREAK OF COVID-19 IS A PANDEMIC. TO REDUCE THE SPREAD OF COVID-19, WHERE POSSIBLE, PRACTICE PHYSICAL DISTANCING AND PROPER HYGIENE, KEEP ROOMS WELL VENTILATED AND DISINFECT SURFACES ON BOARD. MARINERS ARE REMINDED OF THEIR RESPONSIBILITY TO DECLARE ANY ON-BOARD ILLNESS AS OUTLINED IN PART 4, OF THE CANADIAN COAST GUARD PUBLICATION, RADIO AIDS TO MARINE NAVIGATION. THE CANADIAN COAST GUARD REMAINS READY TO PROVIDE ASSISTANCE TO MARINERS. VISIT WWW.CANADA.CA FOR UPDATES ON COVID-19. VISIT WWW.TC.CANADA.CA FOR COVID-19 UPDATES RELATED TO MARINE TRANSPORTATION. 2. CANCEL NAVAREA XVIII 125/20. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

18	Security-related requirements

The text of a navigational warning in this category should contain message elements 1, 2, 5, identified and ordered, as in the Message elements table, figure 4.

Note: In accordance with the requirements of the International Ship and Port Facility Security Code only.

EXAMPLES OF WARNINGS IN SECTION 4.2.3.18

| Message Element | Example 1 |
| --- | --- |
| 1. Message series identifier | NAVAREA I 88/22 FRANCE NORTH COAST. BAIE DE SEINE AND LE HAVRE HARBOUR. SECURITY ANNOUNCEMENT. REF: ISPS CODE - SECURITY LEVELS IN FRENCH TERRITORIAL WATERS IN THE BAIE DE SEINE AND IN LE HAVRE HARBOUR UPGRADED TO SECURITY LEVEL 3. ALL ships ARE PROHIBITED TO ENTER BAIE DE SEINE AND LE HAVRE HARBOUR. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 2 |
| --- | --- |
| 1. Message series identifier | NAVAREA XI 111/22 JAPAN. THE GOVERNMENT OF JAPAN ANNOUNCES PUBLICLY THAT IT SETS MARITIME SECURITY LEVEL 1. FOR DETAILS, CALL SOLAS CONVENTION IMPLEMENTATION OFFICE, PHONE: 81-3-5253-8071. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 3 |
| --- | --- |
| 1. Message series identifier | SUBAREA I 49/22 SWEDEN. HEIGHTENED ISPS SECURITY LEVEL. THE SWEDISH GOVERNMENT HAS DECIDED THAT ALL SHIPS IN SWEDISH PORTS OR IN SWEDISH TERRITORIAL WATERS ABOUT TO ENTER A SWEDISH PORT, SHALL APPLY SECURITY LEVEL 2. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 4 |
| --- | --- |
| 1. Message series identifier | NAVAREA VI 285/22 ARGENTINA. THE ARGENTINE GOVERNMENT HAS SET MARITIME SECURITY LEVEL 3 FOR ALL PORTS. ALL SHIPS ENTERING ARGENTINA WATERS OR PORTS ARE REQUIRED TO MAINTAIN AN ARMED SECURITY WATCH. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

MISCELLANEOUS

IN-FORCE BULLETIN

Notes: In-force bulletins should be issued once per week at a regular scheduled time. In-force bulletins should:  Be part of the numbered navigational warning series, and be issued as an individual numbered message which remains in force for one week;  Include the DTG of when it was prepared;  List ALL warnings still in force, not just those issued within the past 6 weeks; and  Include details of where mariners can obtain copies of those messages which remain in force, but are no longer being broadcast, as they are more than 6 weeks old.

| Message element | Example 1 |
| --- | --- |
| 1. Message series identifier | NAVAREA I 022/22 1. NAVAREA I WARNINGS IN FORCE AT 041000 UTC MAR 2022: 2021 SERIES: 031. 2022 SERIES: 020, 021, 022. NOTES: A. TEXTS OF NAVAREA I WARNINGS ISSUED EACH WEEK ARE PUBLISHED IN WEEKLY EDITIONS OF THE ADMIRALTY NOTICES TO MARINERS BULLETIN (ANMB). B. NAVAREA I WARNINGS LESS THAN 42 DAYS OLD (020/22 ONWARD) ARE PROMULGATED VIA ENHANCED GROUP CALL (EGC) AND/OR RELEVANT NAVTEX TRANSMITTERS. C. THE COMPLETE TEXTS OF ALL IN-FORCE NAVAREA I WARNINGS, INCLUDING THOSE WHICH ARE NO LONGER BEING BROADCAST, ARE REPRINTED IN SECTION III OF ANMB IN WEEKS 1, 13, 26 AND 39 AND ARE ALSO AVAILABLE FROM THE UKHO WEBSITE AT: WWW.ADMIRALTY.CO.UK/RNW. ALTERNATIVELY, THESE MAY BE REQUESTED BY E-MAIL FROM NAVAREA I CO-ORDINATOR AT: NAVWARNINGS@UKHO.GOV.UK |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

| Message element | Example 1 |
| --- | --- |
| 1. Message series identifier | NAVAREA II 085/22 1. NAVAREA II WARNINGS IN FORCE AT 271630 UTC FEB 22: 2020 SERIES: 083, 2021 SERIES: 251, 476, 2022 SERIES: 020, 027, 040, 041, 046, 057, 066, 069, 071, 073, 079, 080, 082, 083, 085. 2. ONLY THOSE LESS THAN 42 DAYS OLD ARE DAILY BROADCAST ON SAFETY NET AT 04H30 AND 16H30 UTC. 3. THE COMPLETE TEXTS OF ALL IN-FORCE NAVAREA II WARNINGS ARE AVAILABLE FROM THE SHOM WEBSITE AT: DIFFUSION.SHOM.FR 4. ALTERNATIVELY, THESE MAY BE REQUESTED BY E-MAIL AT: COORD.NAVAREA2@SHOM.FR 5. CANCEL NAVAREA II 067/22. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

CANCELLATION MESSAGE

| Message element | Example 1 |
| --- | --- |
| 1. Message series identifier | NAVAREA VII 126/22 CANCEL NAVAREA VII 100/22 and this msg, BAIXO RIBEIRO LIGHT, NORMAL CONDITIONS RESTORED. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

WEBSITE OUT OF SERVICE

| Message element | Example 1 |
| --- | --- |
| 1. Message series identifier | NAVAREA VIII 43/22 NAVAREA VIII WEBSITE. 1. NAVAREA VIII WEBSITE UNUSABLE 122300 UTC TO 132300 UTC NOV 22. FOR URGENT SERVICE, CONTACT NAVAREA VIII, PHONE: 91 135 274 7365, FAX: 91 135 274 8373, E-MAIL: INHO_MARINESAFETY@DATAONE.IN. 2. CANCEL THIS MSG 140001 UTC NOV 22. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

SPACE WEATHER

Note: Space Weather encompasses the conditions and processes occurring in space, including on the sun, in the magnetosphere, ionosphere and thermosphere, which have the potential to affect the near-Earth environment. The effects of Space Weather can range from damage to satellites arising from charged particles to disruption of power during geomagnetic storms, or disturbance of satellite positioning systems. Space weather should include: Geomagnetic Storms, Solar Radiation Storms, and Radio Blackouts.

| Message element | Example 1 |
| --- | --- |
| 1. Message series identifier | NAVAREA IV 43/22 SPACE WEATHER. 1. STRONG SOLAR RADIATION STORM IN PROGRESS UNTIL 081000 UTC MAR 22. RADIO AND SATELLITE NAVIGATION SERVICES may be affected. 2. CANCEL THIS MSG 081100 UTC MAR 22. |
| 2. General area |  |
| 3. Locality |  |
| 4. Chart number |  |
| 5. Key subject |  |
| 6. Geographical position |  |
| 7. Amplifying remarks |  |
| 8. Cancellation details |  |

8	METAREA COORDINATOR RESOURCES AND RESPONSIBILITIES

8.1 	METAREA Coordinator resources

8.1.1	The METAREA Coordinator should have:

.1	the expertise and information sources of National Meteorological Services;

.2	effective communications, e.g. telephone, email, facsimile, internet, telex, etc. with National Meteorological Services in the METAREA, with other METAREA Coordinators, and with other data providers.

8.2	METAREA Coordinator responsibilities

8.2.1	The METAREA Coordinator has to:

.1	act as the central point of contact on matters relating to meteorological information and warnings within the METAREA;

.2	promote and oversee the use of established international standards and practices in the promulgation of meteorological information and warnings throughout the METAREA;

.3	coordinate preliminary discussions between neighbouring Members, seeking to establish or amend NAVTEX services, prior to formal application;

.4	coordinate the promulgation of meteorological bulletins onto WMO's Information System and ensure the correct display of MSI messages on the WWMIWS website hosted by Météo-France;

.5	liaise with entities that have responsibility for maritime safety, marine communications, port authorities, and other relevant maritime responsibilities on the effective use of meteorological information and warning services;

.6	act as a coordination point for implementation of WMO strategic initiatives under the services delivery framework, including verification, quality management, Marine Forecaster Competency framework and resilience activities;

.7	be responsible for maintaining details of marine weather services and marine communications relevant for international service documentation such as WMO No-9, Vol D - Information for Shipping, UKHO Admiralty List of Radio Signals, IMO GMDSS Master Plan; and

.8	contribute to the development of international standards and practices through attendance and participation in the WMO Worldwide Met-Ocean Information and Warning Service Sub-Committee meetings, and also attend and participate in relevant IMO, IHO and WMO meetings as appropriate and required.

.9	The METAREA Coordinator has to also ensure that within its METAREA, National Meteorological Services which act as Issuing Services have the capability to:

.1	select meteorological information and warnings for broadcast in accordance with the guidance given in the WMO's Manual on Marine Meteorological Services (WMO No.558); and

.2	provide insights and monitor changes in customer requirements for updates to the WMO Guide on Marine Meteorological Services (WMO No.471); and

.3	monitor the transmission of their bulletins, broadcast by the Issuing Service.

.10	The METAREA Coordinator has to further ensure that within its METAREA, National Meteorological Services which act as Preparation Services have the capability to:

.1	endeavour to be informed of all meteorological events that could significantly affect the safety of navigation within their area of responsibility;

.2	assess all meteorological information immediately upon receipt in the light of expert knowledge for relevance to navigation within their area of responsibility;

.3	forward marine meteorological information that may require wider promulgation directly to adjacent METAREA Coordinators and/or others as appropriate, using the quickest possible means;

.4	ensure that information concerning all meteorological warning subject areas listed in WMO No.558 that may not require a warning within their own area of responsibility is forwarded immediately to the appropriate National Meteorological Services and METAREA Coordinators affected by the meteorological event;

.5	provide insights and monitor changes in customer requirements for updates to the WMO Guide on Marine Meteorological Services (WMO No.471); and

.6	maintain records of source data relating to meteorological information and warning messages within their area of responsibility.

9	Meteorological warnings and forecasts

9.1 	General

9.1.1		Meteorological warning and forecast services for the high seas include provision of:(a)	Meteorological warnings;

(b)	Marine forecasts;

(c)	Sea ice information services.

The preparation and issue of meteorological warnings, and weather and sea ice information for areas of responsibility are coordinated in accordance with the procedures mentioned in the Manual on Marine Meteorological Services (WMO No.558), and summarized in the following section.

9.2	Structure of weather and sea ice information

Preparation and issue of weather and sea bulletins

9.2.1	Weather and sea ice information  should include, in the order given hereafter:

.1	Part I:  Warnings;

.2	Part II: Synopsis of major features and

.3	Part III: Forecasts.

Language

9.2. 7	Warnings should be given in plain language. Synopses and forecasts should be given in plain language, however some abbreviations may be used, especially when the size of the bulletin needs to be reduced for dissemination by a low bandwidth system, such as the NAVTEX Service (ref: 9.2. .11).).

9.2.8	Warnings, synopses and forecasts intended for the International EGC Services and the International NAVTEX Services should be broadcast in English.

Note: Additionally, if a national Meteorological Service wishes to issue warnings and forecasts to meet national obligations under SOLAS, broadcasts may be made in other languages. These broadcasts will be part of national EGC Services or NAVTEX Services.

9.2.10	The language of the synopsis should be as free as possible from technical phraseology.

9.2.11	The terminology in weather and sea ice information should be in accordance with the Manual on Marine Meteorological Services (WMO No. 558).

9.2.12	A list of common abbreviations for use in the International NAVTEX Service is available in the Manual on Marine Meteorological Services (WMO No. 558).

9.3	Warnings

9.3.1	Warnings should be issued for gales (Beaufort force 8 or 9) and storms (Beaufort force 10 or over), and for tropical cyclones (hurricanes in the North Atlantic and eastern North Pacific, typhoons in the Western Pacific, cyclones in the Indian Ocean and cyclones of a similar nature in other regions). Warnings should be issued  for ice accretion and hazardous sea ice conditions.

9.3.3	Warnings for gales force winds and above and tropical cyclones should have the following content and order of items:

.1	type and severity of warning;

.2	date and time of reference in UTC;

.4	location of disturbance in terms of latitude and longitude or with reference to well-known charted landmarks;

.6	extent of affected area;

.7	description of the warning phenomenon characteristics;

9.3.7	A warning should be issued for broadcast immediately when the need becomes apparent

9.3.8	When no warnings for gales, storms or tropical cyclones or ice accretion are to be issued, that fact should be positively stated in part I of each weather and sea ice information.

9.3.9	Warnings should be updated whenever necessary and then issued immediately.

9.3.10	Warnings should remain in force until amended or cancelled.

9.3.12	Warnings for other severe conditions such as poor visibility, severe sea states (such as high swell, risk of abnormal waves, etc.), ice accretion, etc. should also be issued, as necessary.

9.4	Synopses

9.4.1	The synopses given in part II of weather and sea bulletins should have the following content and order of items:

.1	date and time of reference in UTC;

.2	synopsis of major features; and

.3	direction and speed of movement of significant pressure systems and tropical disturbances.

9.5	Forecasts

9.5.1	The forecasts given in part III of weather and sea bulletins should have the following content and order of items:

.1	the valid period of forecast;

.2	name or designation of forecast area(s) within the main MSI area; and

.3	a description of:

.1	wind speed or force and direction;

.2	sea state; and

.3	visibility, when forecast to be moderate or worse

9.5.2	The forecasts should include expected significant changes during the forecast period, significant hydrometeors such as freezing precipitation, snowfall or rainfall

9.5.3	The valid period should be indicated either in terms of number of hours from the time of issue of the forecast or in terms of dates and time in UTC of the beginning and the end of the period.

9.5.4	The following descriptive terms should be used for visibility:

.1	very poor (less than 0.5 nautical miles);

.2	poor (0.5 to 2 nautical miles);

.3	moderate (2 to 5 nautical miles);

.4	good (greater than 5 nautical miles).

9.5.5	Sea ice information should provide:

- the limit of sea ice and icebergs, where ice conditions pose a hazard to navigation.

- information about sea ice concentration and stage of development.

Other information may be included if available.

10 	EXAMPLES FOR METEOROLOGICAL WARNINGS AND FORECASTS

10.1	Examples of Warnings in section 9.3.

ICE ACCRETION WARNING 404 This affects ocean area: SOUTHERN AT 310600UTC Over waters north of Ice Edge. In an area bounded by 62S 156W 58S 146W 59S 130W 63S 126W 62S 156W: Heavy Ice Accretion. Ice accretion area moving eastsoutheast 15kt. This warning cancels and replaces warning 401. ICE ACCRETION WARNING 401 This affects ocean area: SOUTHERN AT 310000UTC In an area bounded by 62S 156W 58S 146W 59S 130W 63S 126W 62S 156W: Heavy Ice Accretion. Ice accretion area slow moving. This warning cancels and replaces warning 396. ICE ACCRETION WARNING 366 This affects ocean area: SOUTHERN AT 211800UTC Over waters east of western boundary and north of Ice Edge. In an area bounded by 63S 160E 60S 160E 62S 170E 63S 170E 63S 160E: Heavy Ice Accretion easing next 6 hours. Ice accretion area slow moving. This warning cancels and replaces warning 361. GALE WARNING 321 This affects ocean area: PACIFIC AT 241200UTC In a belt 120 nautical miles wide centred on a line 41S 125W 43S 123W 44S 122W: Northwest 35kt easing next 6 hours. Gale area moving eastsoutheast 50kt. This warning cancels and replaces warning 319. GALE WARNING 459 This affects ocean areas: FORTIES and SOUTHERN AT 280600UTC Over waters east of western boundary. Low 985hPa near 57S 165E moving east 30kt. 1. Within 300 nautical miles of low in northern semicircle: Clockwise 35kt developing next 6 hours at times. 2. Within 180 nautical miles of low in southwest quadrant: Clockwise 35kt developing next 6-12 hours. Gale areas moving with low. This warning cancels and replaces warning 454. GALE WARNING 265 This affects ocean areas: FORTIES and PACIFIC AT 141200UTC In a belt 240 nautical miles wide centred on a line 46S 177E 44S 179W 42S 176W: Southwest 35kt. Gale area moving east 30kt. This warning cancels and replaces warning 262.

10.2	Examples of Forecasts in section 9.3.1.3

FZNT01 KWBC 031624 HSFAT1 HIGH SEAS FORECAST FOR METAREA IV NWS OCEAN PREDICTION CENTER WASHINGTON DC 1630 UTC WED NOV 03 2021 CCODE/1:31:04:01:00/AOE/NWS/CCODE SUPERSEDED BY NEXT ISSUANCE IN 6 HOURS SEAS GIVEN AS SIGNIFICANT WAVE HEIGHT...WHICH IS THE AVERAGE HEIGHT OF THE HIGHEST 1/3 OF THE WAVES. INDIVIDUAL WAVES MAY BE MORE THAN TWICE THE SIGNIFICANT WAVE HEIGHT. ONLY YOU KNOW THE WEATHER AT YOUR POSITION. REPORT IT TO THE NATIONAL WEATHER SERVICE. EMAIL US AT VOSOPS@NOAA.GOV(LOWERCASE). METAREA IV BULLETIN WILL ONLY BE BROADCAST FROM THE INMARSAT AOE SATELLITE. PLEASE ENSURE YOUR RECEIVER IS POINTED CORRECTLY. FOR INFORMATION ON ATLANTIC ICEBERGS SEE INFORMATION FROM NORTH ATLANTIC ICE SERVICE AT HTTPS://OCEAN.WEATHER.GOV/ATL_TAB.PHP (ALL LOWERCASE). SECURITE NORTH ATLANTIC NORTH OF 31N TO 67N AND WEST OF 35W ALL FORECASTS VALID OVER ICE FREE FORECAST WATERS SYNOPSIS VALID 1200 UTC NOV 03. 24 HOUR FORECAST VALID 1200 UTC NOV 04. 48 HOUR FORECAST VALID 1200 UTC NOV 05. .WARNINGS. ...TROPICAL STORM WARNING... .TROPICAL STORM WANDA NEAR 38.8N 39.8W 992 MB AT 1500 UTC NOV 03 MOVING NNE OR 015 DEG AT 9 KT. MAXIMUM SUSTAINED WINDS 45 KT GUSTS 55 KT. TROPICAL STORM FORCE WINDS WITHIN 80 NM NE QUADRANT...90 NM SE QUADRANT...60 NM SW QUADRANT...AND 40 NM NW QUADRANT. SEAS 12 FT OR GREATER WITHIN 240 NM S SEMICIRCLE...480 NM NE QUADRANT AND 360 NM NW QUADRANT WITH SEAS TO 16 FT. .24 HOUR FORECAST TROPICAL STORM WANDA NEAR 41.4N 39.6W. MAXIMUM SUSTAINED WINDS 45 KT GUSTS 55 KT. TROPICAL STORM FORCE WINDS WITHIN 60 NM E SEMICIRCLE AND 50 NM W SEMICIRCLE. SEAS 12 FT OR GREATER WITHIN 120 NM OF LOW CENTER...EXCEPT 240 NM NE QUADRANT. WITH SEAS TO 18 FT. .48 HOUR FORECAST TROPICAL STORM WANDA NEAR 40.9N 37.5W. MAXIMUM SUSTAINED WINDS 50 KT GUSTS 60 KT. TROPICAL STORM FORCE WINDS WITHIN 60 NM E SEMICIRCLE...100 NM SW QUADRANT AND 90 NM NW QUADRANT. SEAS 12 FT OR GREATER WITHIN 240 NM W AND 180 NM E SEMICIRCLES WITH SEAS TO 21 FT. .72 HOUR FORECAST TROPICAL STORM WANDA NEAR 39.2N 36.6W. MAXIMUM SUSTAINED WINDS 45 KT GUSTS 55 KT. EXTENDED OUTLOOK...USE FOR GUIDANCE ONLY...ERRORS MAY BE LARGE. .96 HOUR FORECAST POST-TROPICAL CYCLONE WANDA NEAR 40.1N 33.2W. MAXIMUM SUSTAINED WINDS 45 KT GUSTS 55 KT. .120 HOUR FORECAST POST-TROPICAL CYCLONE WANDA NEAR 47.1N 27.1W. MAXIMUM SUSTAINED WINDS 45 KT GUSTS 55 KT. ...GALE WARNING... .LOW 63N55W 982 MB MOVING NW 15 KT. WITHIN 240 NM N SEMICIRCLE...AND 420 NM SW AND 480 NM SW QUADRANTS WINDS 30 TO 45 KT. SEAS 11 TO 22 FT. ELSEWHERE WITHIN 660 NM SE AND 540 NM SW QUADRANTS WINDS 20 TO 30 KT. SEAS TO 8 FT. .24 HOUR FORECAST LOW AND CONDITIONS MOVED N OF AREA. ...GALE WARNING... .N OF 59N E OF THE E COAST OF GREENLAND WINDS 25 TO 40 KT. SEAS TO 10 FT. ELSEWHERE N OF 57N E OF THE E COAST OF GREENLAND WINDS TO 25 KT. SEAS TO 8 FT. .24 N OF 57N E OF THE E COAST OF GREENLAND WINDS 20 TO 30 KT. SEAS TO 11 FT. .48 HOUR FORECAST CONDITIONS DIMINISHED. ...GALE WARNING... .LOW 42N66W 1016 MB MOVING NE 20 KT. WITHIN 960 NM SW QUADRANT WINDS 20 TO 30 KT. SEAS TO 8 FT. .24 HOUR FORECAST LOW 48N56W 1000 MB. WITHIN 360 NM SW QUADRANT WINDS 25 TO 40 KT. SEAS TO 10 FT. ELSEWHERE WITHIN 360 NM SE AND 540 NM SW QUADRANTS WINDS TO 25 KT. SEAS TO 8 FT. .48 HOUR FORECAST LOW 57N36W 996 MB. WITHIN 360 NM SW AND 120 NM NW QUADRANTS WINDS 25 TO 40 KT. SEAS 8 TO 14 FT. ELSEWHERE WITHIN 720 NM SW AND 300 NM NW QUADRANTS WINDS TO 25 KT. SEAS TO 10 FT. ...GALE WARNING... .24 HOUR FORECAST FROM 31N TO 36N BETWEEN 68W AND 81W WINDS 20 TO 30 KT. SEAS TO 10 FT. .48 HOUR FORECAST NEW LOW 40N62W 1004 MB. WITHIN 240 NM N AND 420 NM S SEMICIRCLES WINDS 25 TO 40 KT. SEAS 8 TO 14 FT. ELSEWHERE WITHIN 360 NM NW...540 NM NE...660 NM SE AND 900 NM SW QUADRANTS WINDS TO 25 KT. SEAS TO 9 FT. .SYNOPSIS AND FORECAST. .24 HOUR FORECAST NEW LOW 65N62W 1000 MB. WITHIN 240 NM NE AND 660 NM SE QUADRANTS WINDS TO 25 KT. SEAS TO 9 FT. .48 HOUR FORECAST LOW DISSIPATED AND CONDITIONS DIMINISHED. .48 HOUR FORECAST FROM 52N TO 62N BETWEEN 49W AND 63W WINDS TO 25 KT. SEAS TO 10 FT. .DENSE FOG. VSBY OCCASIONALLY LESS THAN 1 NM FROM 61N TO 67N BETWEEN 50W AND 62W AND FROM 42N TO 48N BETWEEN 42W AND 50W. .24 HOUR FORECAST DENSE FOG FROM 48N TO 57N E OF 40W. .48 HOUR FORECAST DENSE FOG FROM 53N TO 60N E OF 46W. .HIGH 46N56W 1022 MB MOVING NE 25 KT. .24 HOUR FORECAST HIGH 53N47W 1024 MB. .48 HOUR FORECAST HIGH DISSIPATED. .24 HOUR FORECAST NEW HIGH 36N57W 1024 MB. .48 HOUR FORECAST HIGH 46N51W 1028 MB. .FORECASTER HOLLEY. OCEAN PREDICTION CENTER. NWS NATIONAL HURRICANE CENTER MIAMI FL ATLANTIC FROM 07N TO 31N W OF 35W INCLUDING CARIBBEAN SEA AND GULF OF MEXICO SYNOPSIS VALID 1200 UTC WED NOV 3. 24 HOUR FORECAST VALID 1200 UTC THU NOV 4. 48 HOUR FORECAST VALID 1200 UTC FRI NOV 5. .WARNINGS. .NONE. .SYNOPSIS AND FORECAST. .ATLC 36 HOUR FORECAST COLD FRONT FROM 31N77W TO 28N80W. WITHIN 30N78W TO 30N81W TO 31N81W TO 31N78W TO 30N78W N TO NE WINDS 20 TO 25 KT. SEAS 8 TO 9 FT. .48 HOUR FORECAST COLD FRONT FROM 31N72W TO 27N80W. WITHIN 28N80W TO 29N81W TO 31N81W TO 31N78W TO 28N80W NE WINDS 20 TO 25 KT. SEAS 8 TO 10 FT IN NE SWELL. .GULF OF MEXICO 24 HOUR FORECAST WITHIN 28N95W TO 27N97W TO 28N97W TO 29N95W TO 29N94W TO 28N95W N TO NE WINDS 20 TO 25 KT. SEAS LESS THAN 8 FT. .30 HOUR FORECAST COLD FRONT FROM 29N80W TO 27N96W TO 21N98W. WITHIN 26N95W TO 26N97W TO 27N97W TO 28N97W TO 27N94W TO 26N95W NE WINDS 20 TO 25 KT. SEAS LESS THAN 8 FT. .42 HOUR FORECAST COLD FRONT FROM 28N80W TO 26N95W TO 20N97W. CONDITIONS IMPROVE. WINDS 20 KT OR LESS. SEAS LESS THAN 8 FT. .GULF OF MEXICO 48 HOUR FORECAST COLD FRONT FROM 27N80W TO 25N95W TO 19N95W. WITHIN 27N84W TO 27N87W TO 29N87W TO 29N84W TO 27N84W NE TO E WINDS 20 TO 30 KT. SEAS LESS THAN 8 FT. .REMAINDER OF AREA WINDS 20 KT OR LESS. SEAS LESS THAN 8 FT. .FORECASTER ERA. NATIONAL HURRICANE CENTER.

MARINE WEATHER BULLETIN FOR PACIFIC Area from 25S to 55S and 170W to 120W ISSUED BY METEOROLOGICAL SERVICE OF NEW ZEALAND, WELLINGTON ISSUED AT 020702UTC VALID UNTIL 031200UTC Part 1 - WARNINGS WARNINGS IN FORCE: 014 Part 2 - Situation analysis at 020600UTC: Trough T1 33S 148W 37S 135W 40S 120W, slow moving. Front F1 48S 134W 52S 129W 55S 124W, moving eastsoutheast 30kt. Front F2 35S 137W 40S 131W 49S 124W, moving east 20kt. Trough T2 23S 160W 28S 157W 33S 155W, moving southsoutheast 5kt. Ridge R1 39S 160W 47S 175W 55S 177E, moving east 15kt. Part 3 - Forecast: Refer to latest warnings Within 240 nautical miles north of T1 from 33S 148W to 37S 135W: Areas of poor visibility in rain. Within 240 nautical miles north of T1 from 37S 135W to 40S 120W: Areas of poor visibility in rain developing by 021800UTC. Within 240 nautical miles east of F1: Areas of poor visibility in rain, easing by 021800UTC. Within 660 nautical miles east of F2: Areas of fog, easing by 030000UTC. Within 420 nautical miles east of F2 from 40S 131W to 49S 124W: Northwest 25kt, easing by 021800UTC. Within 360 nautical miles east of T2: Areas of poor visibility in rain with possible thunderstorms. Within 300 nautical miles west of T2: Areas of poor visibility in rain with possible thunderstorms. Within 540 nautical miles west of T2 from 28S 157W to 33S 155W: Easterly 25kt developing by 030000UTC. East of R1: Westerly quarter 25kt at times, with gales as in warning 014, areas of poor visibility in showers, areas of heavy westerly quarter swell.

11	Search and rescue notification

11.1	Communications related to search and rescue operations such as distress alerts, coordination of operations, local communications and positioning signals are never MSI, even when (for some shore-to-ship alerts) they use the International SafetyNET or NAVTEX services which are also used for MSI. This guide, therefore, does not apply to them.

11.2	Search and rescue operations may, however, involve the broadcasting of MSI in the navigational warning category, described in 4.2.3.6.

12	Procedure for amending the Joint imo/iho/wmo Manual on msi

12.1	Proposals for amendments or enhancements to the Joint IMO/IHO/WMO Manual on MSI should be submitted for evaluation and endorsement by the appropriate IMO Sub-Committee. Amendments will only be adopted after the approval of the Maritime Safety Committee (MSC).

12.2	Amendments to the Manual should normally be adopted at intervals of approximately two years or at such longer periods as may be determined by the Maritime Safety Committee. Amendments approved by the Maritime Safety Committee will be notified to all concerned, and will come into force on 1 January of the following year or another date decided by the Committee.

12.3	The agreement of the International Hydrographic Organization and World Meteorological Organization and the active participation of other bodies should be sought, according to the nature of the proposed amendments.

___________

# Footnotes

CPRNW was renamed the IHO WWNWS Sub-Committee (WWNWS) with effect from 1 January 2009.

See WMO Publication Manual on Marine Meteorological Services (WMO No 558).

As set out in the IMO NAVTEX Manual.

As defined in SOLAS regulation IV/2.

Which may include inland seas, lakes and waterways navigable by sea-going ships.

5 	Which may include inland seas, lakes and waterways navigable by sea-going ships.

Digital selective calling (DSC) means a technique using digital codes, conforming to the technical structure and content set forth in the most recent version of Recommendations ITU R M.493 and ITU R M.541, which enables a radio station to establish contact with and transfer information to another station or group of stations.

As set out in IMO resolution A.1051(27), as amended.

As set out in resolution A.706(17), as amended.

IOC is the Intergovernmental Oceanographic Commission of UNESCO.

Coordination of HF NBDP broadcasts in the Arctic should be undertaken by relevant MSI service providers.

In accordance with the requirements of the International Ship and Port Facility Security (ISPS) Code only.

Reference number is NOT to be included as part of the message text.

# Comments

TO BE REVIEWED AT MSC

Nick will provide text.

Zhicao Wang: WMO SERCOM

METAREA X: This should be removed. Reference to procedures for updating this document are contained in section 12.

Zhichao Wang: WMO Sercom

MET X: This should be removed, reference to procedures for updating this document are contained within section 12

Is the MSC circ number more appropriate?

International EGC Services - Global

MSC circ number?

Replace “SafetyNET” with “Enhanced Group Call (EGC)”

Remove “SafetyNET” in blue box before “EGC Receiver”

Use graphic within the SafetyCast Manual

METAREA IV/XII: Figure 1 needs information related to Safetycast

New diagram should be inserted from MSC.468(101), which replaces SafteyNET with EGC.

Definitions will need to be numbered

METAREA IV/XII: In the definitions of section 2, add definition for Iridium and Safetycast

New definitions to be added here and for places detailing national services, etc.  Take from resolutions.

Add Safetycast info to Issuing service definition

David Wyatt: Inmarsat SafeyNET should be replace with EGC services, check approved resolutions for wording.

To be defined later

METAREA IV/XII: Add definition for Safetycast before or after number 19.

See above comment.

Move to be after NAVTEX.

Kept due to Joint nature of document.

METAREA IV/XII: Add Safetycast Info to definition 30.

See above comment.

The footnote will just need to refer to the DSC definition within SOLAS IV

Potential to delete all sea area definitions

Replace with: Worldwide Met-Ocean Information and Warning Service

iaw original version of A.706(17) dated 6 November 1991.

David Wyatt: Recommend use captions inserted into NAVTEX manual for both figures 2 and 3

METAREA IV/XII: Figure 2 shows the U.S. with responsibility for METAREA XVI. Peru has responsibility for METAREA XVI.

MAR to provide new map as per 558/1051

Take from NAVTEX manual.

David Wyatt: see comment above regarding caption

MET IV/XII: Add info on safetycast

David Wyatt: Replace SafetyNET with a generic term used in resolutions

METAREA IV/XII: Add information for Safetycast

See above.

Add a new 2.3.5 “Iridium SafetyCast broadcasts should be made in accordance with the standards and procedures set out in the International SafetyCast Manual.”

METAREA IV/XII: Add information for Safetycast throughout section 2.4, 2.5 and 2.7.

Use generic term throughout as detailed in resolutions.

To be reviewed after recognition of Iridium and change of name of Coordinating Panel.

To be revised

MET XIV: METAREA XIV: There are several mentions of only SafetyNET in 4.2. and following points. SafetyCast should be added for all. Perhaps, it would be better to use a generic term, rather than specifically mention SafetyNET and SafetyCast to make the document more future proof?!

D Wyatt: Use Generic term throughout as in the resolutions

Add message example for virtual aids.

Add example of message for “ash clouds”.

Add additional category for Space weather to be considered at WWNWS10.

Delete hyphens in geographical positions.

WZ 570

IRELAND, EAST COAST.

Approaches to Carlingford Lough.

1. Hellyhunter lightbuoy, 54-00.3N 006-02.0W, off station and Racon unstable.

2. Cancel WZ 549 (OA75).

NAVAREA III 0451/21

WESTERN MEDITERRANEAN SEA - TUNISIA NORTH COAST

CANIS LIGHTHOUSE IN POSITION:

37-21.20N 010-07.40E

LIGHT UNRELIABLE

WZ 1279

ENGLAND, EAST COAST. Approaches to the Wash. Race Bank Wind Farm.

1. Fog signals are inoperative at turbines in the following positions,

53-14.9N 000-48.9E

53-17.8N 000-46.3E

53-20.1N 000-49.1E

2. Cancel WZ 1234 (GA28).

NAVAREA VIII 600.

INDIA WEST COAST.

VALIYAZHIKAL.

CHARTS IN 221 260 INT 7362.

NEW LT FL(3)W 20S ESTABLISHED 09-08.4108N 076-27.7268E.

S 0678/21

QUINTAO VICINITY

CHART 2010

TRAMANDAI RADIOBEACON NRORD RF 2730 30-00.60S 050-08.72W RACON INOPERATIVE

CANCEL THIS WARNING 291545 UTC MAR 22.

GULF OF MEXICO.

TEXAS.

CHART 11300.

ANGLETON DGPS STATION 29-18.1N 095-29.0W UNUSABLE

UNTIL FURTHER NOTICE.

WZ 570

IRELAND, EAST COAST.

Approaches to Carlingford Lough.

1. Hellyhunter lightbuoy, 54-00.3N 006-02.0W, off station and Racon unstable.

2. Cancel WZ 549 (OA75).

NAVAREA VIII -805

-------------------------------------------------------------------------------------------------------------------------------

INDIA EAST COAST - OFF KRISHNAPATNAM (.) CHARTS IN 31 356 3034 INT 7400

(.) FISHING BOAT REPORTED SUNK IN APPROXIMATE POSITION 14-14.25N 080-09.85E ON 22

NOV 21

220530 UTC APR 21

NAVAREA XX 50/21

BARENTS SEA.

CHART RUS 12000.

WRECK LOCATED IN 70-10.72N 032-56.55E.

WITH DEPTH 160 METRES ABOVE IT.=

NAVAREA IX (.) 279/21 (.) IRAN (.) RAS E JESK (.)

CHARTS BA 2851, 2858 AND 2888

2.  WRECK REPORTED IN POSITION 25-38.85N 057-39.51E

AT 20 METERS DEPTH

3.  SOUTH CARDINAL LIGHTBUOY ESTABLISHED IN POSITION

25-38.72N 057-39.50E WITH CHARACTERISTICS Q(6)+LFL

15 SECONDS 5 MILES

4.  MARINERS CAUTIONED

NAVAREA VIII 600.

INDIA WEST COAST.

VALIYAZHIKAL.

CHARTS IN 221 260 INT 7362.

NEW LT FL(3)W 20S ESTABLISHED 09-08.4108N 076-27.7268E.

NAVAREA V

NAVAREA WARNING 0556/21

SOUTHEAST OF ILHA DE SAO SEBASTIAO

CHART 21070 (INT 2008)

SPECIAL BUOY (ODAS), YELLOW, LP(5)A.20S

DATA COLLECT, TEMPORARILY ESTABLISHED

IN 24-28.03S 044-24.36W

500 METERS BERTH REQUESTED

CANCEL THIS WARNING 241300 UTC MAY 22.

ST

ANDAMAN SEA - PORT BLAIR (.) CHARTS IN 404 4006 INT 7439 (.) NORTH POINT

LT (11-42.29N 092-45.29E) OPERATING AT REDUCED RANGE OF 10 NM

NAVAREA VIII 528.

INDIA WEST COAST.

KANHOJI ANGRE I.

CHARTS IN 211 2016 INT 7336.

VISIBLE SECTOR OF MAIN LT (18-42.2N 072-48.82E) CHANGED TO WHITE LIGHT FROM TRUE BEARING 181 TO 018 AND RED LIGHT FROM 018 TO 181.

NAVAREA III 0863/21

WESTERN MEDITERRANEAN SEA - ALGERIA

THE LIGHTHOUSE OF RACHGOUN ISLAND IN:

35-19-27N 001-28-39W

WORKS WITH A FIXED RHYTHM

NAVAREA II 468/21

PORTO-FINISTERRE.

TUG EEMS WRESTLER TOWING CARGO ANGON FROM LEIXOES (PORTUGAL) TO

VILLAGARCIA (SPAIN).

ETA 250900 UTC DEC 21.

LENGTH OF TOW 400 METRES. WIDE BERTH REQUESTED.

NAVAREA VII 342 OF 2021

231438 UTC NOV 21

1. SOUTH ATLANTIC OCEAN - NE SECTOR - OFFSHORE MOWE PT 2. CHART SAN 90(INT 2051) 3. TUG SEA ALFA (C/S PHSA) TOWING BARGE EGCM 004. LENGTH OF TOW 500 METERS. DESTINATION DAKAR SENEGAL 4. 18 - 16 S 004 - 28 E 5. VESSELS TO KEEP WELL CLEAR 6. CANCEL NAVAREA VII 338 OF 2021 AND NAVAREA VII 341 OF 2021 7. UNTIL FURTHER NOTICE

NAVAREA I  219/21
ENGLISH CHANNEL,  DOVER STRAIT AND AT WEST HINDER TSS.  
CHARTS GB 2449 AND 2675.
1.  ALP DEFENDER TOWING MV SPIEGELGRACHT FROM LYME BAY, ENGLAND TO ZEEBRUGGE, BELGIUM IN VICINITY OF LINE JOINING:
50-10.1N 002-22.0W, 50-01.6N 002-17.1W, 50-27.8N 000-58.9E, 50-40.1N 001-20.9E, 50-54.1N 001-29.1E, 51-06.9N 001-47.7E, 51-22.0N 002-29.9E, 51-22.0N 002-40.7E AND 51-25.3N 002-48.7E. LENGTH OF TOW 800 METRES.
2.  ALP DEFENDER IN 50-40.1N 001-20.9E AT 020200 UTC DEC 2021.

NAVAREA I 215/21

NAVAREA I 215/21

OFF USHANT TSS.

SOUTH-WEST BOUND LANE.

CHART GB2 (INT 160)

1. SEVEN CONTAINERS REPORTED ADRIFT IN VICINITY 48-40N 005-56W AT 250856 UTC NOV.

2. CANCEL NAVAREA I 214/21.

3. CANCEL THIS MESSAGE 280856 UTC NOV 21.

Questions –

General area (celtic sea)

Locality – TSS (the hydrolant stated France)

NAVAREA II 418/21

NAVAREA II 418/21

MADEIRA.

1. S/V ADRIFT IN VICINITY OF 32-46.6N 014-09.1W AT 031423 UTC NOV 21.

2. CANCEL THIS MSG 061545 UTC NOV 21.

NAVAREA XI 384/21

TIMOR SEA.

FISHING NET, 50 METRE LONG, ADRIFT IN

09-27.6S 131-49.0E AT 230022Z NOV.

CANCEL THIS MSG 260022Z NOV.

NAVAREA IV 1044/21

WESTERN CARIBBEAN SEA.

COLOMBIA.

1. PARTIALLY SUBMERGED RECTANGULAR METALLIC OBJECT

ADRIFT IN VICINITY 12-58.31N 081-37.09W

AT 190030Z NOV.

2. CANCEL THIS MSG 220235Z NOV 21.

NAVAREA VIII 197/21

INDIA EAST COAST.

OFF MACHILIPATNAM.

CHARTS IN 31 355 INT 7405.

1. CONICAL BUOY REPORTED ADRIFT IN APPROXIMATE POSITION  15-37.9N 082-10.3E ON 04 MAR 21

2. CANCEL THIS MSG 071000 UTC MAR 21.

Navarea vii 93/21

NAVAREA VII 093

290723 UTC MAR 2021

1. INDIAN OCEAN - SW SECTOR - OFFSHORE LA REUNION

2. WOOD DEBRIS REPORTED ADRIFT OFF SAINT LEU IN THE FOLLOWING POSITION

A. 21 - 10.5 S 055 - 12.33 E

3. VESSELS TO NAVIGATE WITH CAUTION DUE TO FLOATING DEBRIS

4. CANCEL THIS MESSAGE 311100 UTC MAR 21

NW-M-1880-19

Deadhead 20 feet long reported in the vicinity of 44 30.000N 063 10.000W at 111029 UTC Sep

Pos – 44 -30N 063-10W

NW-M-1880-19

Dead sperm whale, 10 meters in length, reported adrift in vicinity 45-02.6n 048-52.8w at 032100 utc aug 19.

Pos – 44 -30N 063-10W

NAVAREA IX (.) 071/20 (.) SOUTHERN RED SEA (.)

FARASAN BANK (.) CHARTS BA 157, 2964 AND 4071

2. MINES REPORTED ADRIFT IN AREA BOUNDED BY:

A.  16-45.60N 042-15.70E

B.  15-41.50N 042-39.40E

C.  15-54.00N 043-02.30E

D.  16-58.70N 042-35.10E

3. MARINERS ARE REQUESTED TO NAVIGATE WITH

CAUTION IN THE AREA

NAVAREA XVI  137/21

PERU

PIURA

WEST BAY PAITA

HIDRONAV-100 HIDRONAV-120 HIDRONAV-121 HIDRONAV-122 HIDRONAV-113

SAR OPERATION IN PROGRESS CENTRED IN AREA

A. 05B0 27b_18.59b_ S 081B0 44.27.35b_ W

B. 05B0 22b_32.14b_ S 081B0 27.57.29b_ W

C. 05B0 49b_34.29b_ S 081B0 16.34.28b_ W

D. 05B0 55b_25.87b_ S 081B0 32.24.84b_ W

ALL VESSELS NOT UNDER INSTRUCTION OF THE SAR MISSION ARE REQUESTED TO KEEP A WIDE BERTH

NAVAREA II 417/21

CASABLANCA.

- SEARCH AND RESCUE EXERCISE IN PROGRESS UNTIL 041600 UTC NOV 21 IN AREA BOUNDED BY:

- 33-57.0N 008-03.0W

- 34-04.8N 007-47.0W

- 33-46.5N 007-36.0W

- 33-39.0N 007-52.0W

- CANCEL NAVAREA II 412/21.

- CANCEL THIS MSG 041700 UTC NOV 21.

NAVAREA XVIII 83/21

CANADIAN ARCTIC

VICTORIA STRAIT

CHART CHS 7783, 7784

SHOAL LOCATED AT 68-58.945N 101-08.321W, 27.8 METRES

S 0372/21

VICINITY OF ILHA DE SAO SEBASTIAO

CHART 1640

DEPTHS LOWER THAN THOSE REPRESENTED ON CHART

15.0 METROS  IN 24-00.75S 045-41.75W

IN 24-01.50S 045-23.90W

CANCEL THIS WARNING 131710 UTC NOV 21.

FM JRCC AUSTRALIA 210039Z DEC 21

AUSCOAST WARNING 290/21

UNCHARTED ROCK IN POSITION 16-53.06S 122-03.78E

COASTAL WARNING VLADIVOTSOK 11

ZALIV CHIKHACHYOVA

CHART RUS 68060

UNDERWATER OBSTRUCTION IN 51-29.25N 140-54.76E CAUTION ADVISED NNNN

DUE TO PASSAGE OF HURRICANE IDA:

1. THE FOLLOWING PORT(S) ARE CLOSED:

A. PORT OF BATON ROUGE 30-27N 091-11W.

B. PORT OF NEW ORLEANS 29-57N 090-03W.

2. THE FOLLOWING PORT(S) ARE OPEN WITH RESTRICTIONS:

A. PASCAGOULA 30-21N 088-34W.

B. PENSACOLA 30-24N 087-13W.

3. THE FOLLOWING PORT(S) HAVE RE-OPENED:

A. MOBILE 30-41N 088-07W.

4. CURRENT PORT INFORMATION CAN BE FOUND AT

HOMEPORT.USCG.MIL USING THE PORT DIRECTORY TAB.

5. CANCEL NAVAREA IV 780/21.

NAVAREA III 0821/21

EASTERN MEDITERRANEAN SEA - CYPRUS

1.-SURVEY OPERATIONS BY THE SHIP "NAUTICAL GEO" FROM 12 TO 17 NOV21 IN AREA BOUNDED BY:

34-18.652N, 033-08.199E

34-24.227N, 032-20.743E

34-20.107N, 032-20.634E

34-13.363N, 033-07.273E

CAUTION ADVISED, 1,5 NM BERTH REQUESTED.

2.-CANCEL THIS MESSAGE ON 180100 UTC NOV21.

1.- MARINE SCIENTIFIC VESSEL "ABATE MOLINA" PERFORMING

HYDROACOUSTIC TASKS WITH RESTRICTED MANEUVER BETWEEN MAY 090345 UTC

AND JUN 062359 UTC IN:

A. L-3210.0S G-07141.0W.

B. L-3802.0S G-07405.0W.

C. L-4020.0S G-07440.0W.

D. L-4020.0S G-07347.0W.

2.- VESSELS OBEYS COLREGS.

NAVAREA XIII 43/21

SEA OF OKHOTSK

CHART RUS 62175

1. SEISMIC SURVEY WORKS

BY VESSELS VYACHESLAV

TIKHONOV AND PX GEO

TOWING CABLES 4050 METRE

LONG UNTIL 31 AUG

IN AREA BOUNDED BY

52-46-34N 143-22-19E 52-45-46N 143-57-51E

52-02-40N 143-54-59E 52-03-37N 143-11-17E

CAUTION ADVISED

4 VILE BERTH REQUESTED WHEN PASSING

ASTERN AND 2 MILE ON BOTH SIDE OF VESSELS

2. CANCEL THIS MESSAGE 01 SEP 21

Dredging operations taking place daily between 1100 UTC and 2300 UTC in the vicinity of 47 12.96N 061 59.09W. Immersion site at 47 11.80N 061 58.60W is lit and marked.

Tugs Poinciana and Manuels River and barge with excavator on site.

LES 140 - MSG 14499 - NAV/METAREA Safety Call to Area: 3 - PosOk

NAVAREA III 0795/21

MEDITERRANEAN SEA - TUNISIA

1.- MAINTENANCE OF THE SUBMARINE GAS PIPELINE FROM EL HAOUARIA TO SICILY IS CONDUCTED BY THE SHIP "IEVOLI IVORI" UNTIL 13 FEB22 IN AREA BOUNDED BY:

37-01.01N 011-04.22E

37-12.80N 011-15.51E

37-25.47N 011-42.71E

37-11.49N 011-52.01E

37-00.60N 011-21.61E

CAUTION ADVISED, 1000 METERS BERTH REQUESTED

2.- CANCEL THIS MSG ON 132359UTC FEB22

1. UNMANNED ATLANTIC CROSSING BY FOUR METER

M/V MAHI TWO IN VICINITY OF TRACKLINE JOINING

19-38.30N 035-00.00W, 18-50.01N 036-36.39W,

17-24.81N 044-29.68W, 17-04.67N 051-23.64W,

16-23.00N 059-04.41W.

VESSELS IN VICINITY REQUESTED TO KEEP

A SHARP LOOKOUT.

2. FOR MORE INFORMATION REGARDING THE

MOST CURRENT POSITION OF M/V MAHI TWO,

GO TO PROJECTMAHI.DATYLON.COM.

NAVAREA I 193/21

WESTERN APPROACHES TO THE ENGLISH CHANNEL.

MELVILLE KNOLL SOUTH-EASTWARDS.

CHART GB 2649 (INT 1063).

1. UNDERWATER CABLE OPERATIONS IN PROGRESS BY C/S ILE DE BREHAT IN

VICINITY OF LINES JOINING,

A) 49.00.8N 007-55.6W AND 49-02.2N 007-53.9W

B) 49-05.1N 007-52.4W AND 49-06.0N 007-52.6W.

WIDE BERTH OF ONE MILE REQUESTED.

2. CANCEL NAVAREA I 191/21.

NAVAREA V

COASTAL WARNING S 0919/21

EAST OF PARANAGUA

CHART 21070 (INT 2008)

SHIP TO SHIP OPERATION

290900 UTC DEC 21 TO 010900 UTC JAN 22

LENA KNUTSEN, SUR AND SAVEIROS FRAGATA

SHIP TO SHIP AREA OF SANTOS OIL FIELD

CANCEL COASTAL S 0916/21

CANCEL THIS WARNING 020000 UTC JAN 22.

ST

NAVAREA V

COASTAL WARNING E 0732/21

EAST OF PONTA DO UBU

CHART 1402

Diving OPERATIONS

23 OCT 21 TO 26 OCT 21

11:00 TO 21:00

IN 20-50.33S 040-03.52W

CANCEL THIS WARNING 262200 UTC OCT 21.

ST

NAVAREA II 251/21

CANTABRICO-PAZENN.

BAY OF BISCAY.

1. SCIENTIFIC BUOYS MOORING BY M/V ATALANTE

UNTIL 01 MAR 2022.

A. 46-06N 006-47W

B. 44-10N 002-10W

WIDE BERTH REQUESTED.

2. CANCEL THIS MSG 010100 UTC MAR 2022.

AUSCOAST WARNING 180/21

TURTLE HEAD TIDE GAUGE IN POSITION 10 31.30` S 142 12.70` E UNRELIABLE

Acoustic seabed instruments deployed from 231500UTC to 242000UTC March 2019 in the following positions:

44 41.462N 063 37.713W

44 41.462N 063 38.379W

44 41.316N 063 38.040W

AUSCOAST WARNING 284/21

DRILL RIG VALARIS MS-1/D5PI7 IN POSITION 20-57.27S 114-52.10E

2.5 NM CLEARANCE REQUESTED.

WZ 116/22
GMDSS. 
MRCC SHETLAND.
VHF R/T AND DSC SERVICES FROM DUNNET HEAD SITE, 58-40.3N 003-22.6W, OFF AIR.

WZ 169/22

GMDSS.
MRCC STORNOWAY.
MF R/T AND DSC SERVICES FROM BUTT OF LEWIS SITE, 58-27.7N 006-13.9W, OFF AIR.

WZ 053/22
GMDSS.
NORTH SEA.

1. NAVTEX STATION CULLERCOATS (G), 55-04N 001-28W, OFF AIR DAILY BETWEEN 0900 AND 1530 UTC FROM 12 TO 13 JAN 2022.

2. CANCEL THIS MESSAGE 131630 UTC JAN 2022.

NAVAREA I 018/22

GMDSS. 
BALTIC SEA.

1. NAVTEX STATIONS GRIMETON (I), 57-06.3N 012-23.4E, AND GISLOVSHAMMAR (J), 55-29.4N 014-18.9E, OFF AIR.
2. BALTIC SEA NAVIGATION WARNING  007/22 REFERS.

NAVAREA XVIII 135/21

CANADIAN ARCTIC

IQALUIT MCTS

1. REMOTE CONTROL FACILITIES LOCATED AT CORAL HARBOUR OFF AIR FOR THE 2021 NAVIGATIONAL SEASON 161330 UTC NOV 21.

2. CANCEL NAVAREA XVIII 130/21.

3. CANCEL THIS MSG AT 292330 UTC NOV 21

NAVAREA XVIII 102/21

CANADIAN ARCTIC

GMDSS

IQALUIT MCTS

ALL GMDSS DSC, NBDP, AND RT TRANSMIT FACILITIES LOCATED AT IQALUIT OFF AIR 212300 UTC SEP 21.

NAVAREA X 38/21

1.            POSSIBLE TEMPORARY DISRUPTIONS TO VESSEL RADAR AND TERRESTRIAL RACON SYSTEMS

FROM 281300 UTC MAR 2021 TO 311300 UTC MAR 2021 IN AREA BOUND BY

31-00S 160-00E, 24-00S 160-00E,

24-00S 152-00E, 31-00S 152-00E.

2.            DISRUPTIONS CAUSING CONCERNS RELATED TO SAFE NAVIGATION SHOULD BE REPORTED TO JRCC AUSTRALIA

PHONE: +61262306811

EMAIL: RCCAUS@AMSA.GOV.AU

3.            CANCEL THIS MSG 311400 UTC MAR 2021.

NAVAREA XVI 221/21

NAVAREA XVI 221/21

PERU K

WEST CHANCAY

HIDRONAV-200 HIDRONAV-220 HIDRONAV-222 HIDRONAV-223

NAVAL UNITS GUNNER SHOOTING EXERCISE

161400 A 170000 UTC DIC 21 IN AREA BOUNDED BY

A. 11-35-00S 077-43-00W

B.  11-35-00S 077-33-00W

C. 11-47-00S 077-33-00W

D. 11-47-00S 077-43-00W

CANCEL THIS MESSAGE 170100 UTC DIC 21 BT

NAVAREA VIII 864.

INDIA WEST COAST.

OFF ALAPPUZHA.

CHARTS IN 22 221 259 273 INT 7356.

1. DROPPING OF SUBSURFACE EXPLOSIVE SCHEDULED ON 17, 21 DEC 21 FROM 0330 TO 0630 UTC. DANGER AREA OF 05 NM AROUND 09-19.58N 075-46.8E. WIDE BERTH FROM AREA ADVISED

2. CANCEL THIS MSG 210730 UTC DEC 21 .

NAVAREA XIV WARNING 218/21 SOUTHWEST PACIFIC BASIN 1. HAZARDOUS OPERATIONS, SPACE DEBRIS SCHEDULED FROM

062240 UTC DEC 21 UNTIL 200925 UTC DEC 21  IN AREA BOUNDED BY:

AREA 1

A. 41-06S 176-18W

B. 39-54S 175-42W

C. 40-36S 171-06W

D. 41-54S 171-18W

AREA 2

A. 42-36S 163-06W

B. 41-36S 163-12W

C. 41-42S 158-00W

D. 42-36S 157-48W

2. CANCEL NAVAREA XIV WARNING 210/21

NAVAREA VIII 857.

INDIA EAST COAST.

OFF BALASORE.

CHARTS IN 31 301 351 3017 3038 INT 756.

1. IAF EXERCISE SCHEDULED ON. 17, 18, 19, 23 DEC 21 FROM 0430 TO 0630 UTC AND 0830 TO 1030 UTC. 20, 21, 22 DEC 21 FROM 0430 TO 0630 UTC AND 0830 TO

1030 UTC AND 1430 TO 1630 UTC IN DANGER AREA BOUNDED BY (A) 21-41N 087-44E

(B) 20-57N 086-53E (C) 20-56N 086-55E (D) 21-02N 087-13E (E) 20-56N 087-16E

(F) 20-47N 087-02E (G) 20-48N 086-56E (H) 20-12N 087-19E (J) 20-00N 087-59E

(K) 20-35N 087-40E (L) 21-24N 087-38E. DANGER AREA EXTENDING UPTO COASTLINE JOINING POINT A AND B. WIDE BERTH FROM AREA ADVISED 2. CANCEL THIS MSG 231730 UTC DEC 21 .

WESTERN NORTH ATLANTIC.

FLORIDA.

1. HAZARDOUS OPERATIONS, ROCKET LAUNCHING

090600Z TO 090753Z DEC, ALTERNATE

0600Z TO 0753Z DAILY 10 THRU 14 DEC

IN AREAS BOUND BY:

A. 28-39-02N 080-37-42W, 28-41-00N 080-20-00W,

28-38-00N 079-42-00W, 28-35-00N 079-43-00W,

28-33-00N 080-17-00W, 28-33-47N 080-34-05W.

B. 28-04-00N 074-58-00W, 28-34-00N 074-55-00W,

28-39-00N 071-40-00W, 28-17-00N 071-06-00W,

27-41-00N 071-15-00W, 27-33-00N 071-58-00W.

2. CANCEL THIS MSG 140853Z DEC 21.

040509Z DEC 2021 EASTERN RANGE 300000Z NOV 21

NAVAREA II 199/18

IROISE

DUE TO A PRODUCTION PROBLEM THAT HAS CAUSED

DISPLACED FEATURES, IT HAS BEEN DETERMINED THAT

ELECTRONIC NAUTICAL CHART 7066 FR (1800 INT)

IS NOT TO BE USED FOR NAVIGATION OR SITUATIONAL AWARENESS.

A REVIEW IS IN PROCESS TO ADDRESS THIS

SITUATION.

28.01.2022: 0710 UTC: Posn: 12:01.05S - 077:11.38W, Callao Anchorage, Peru.

Seven robbers armed with guns and knives boarded an anchored bulk carrier. They took the duty AB as hostage, hit him on the head and tied his hands and legs. When the duty AB did not answer the radio calls from the bridge, the OOW instructed the second duty crew to check. Alarm raised and crew mustered. A search was carried out. Ship’s properties and stores were reported stolen. Incident reported to TRAMAR and the coast guard who boarded the ship for inspection.

NAVAREA II 223/21

GULF OF GUINEA.

NIGERIA.

PIRACY

1. M/V ATTACKED IN 02-49N 002-31E AT 061700 UTC JUN 21.

VESSELS ARE ADVISED TO KEEP CLEAR OF THIS

POSITION AND TO EXERCISE EXTREME CAUTION.

REPORT TO MDAT-GOG,

PHONE: +33 2 98 22 88 88

E-MAIL: WATCHKEEPERS@MDAT-GOG.ORG

2. CANCEL THIS MSG 081930 UTC JUN 21.

26.11.2020: 1258 UTC: POSN: 04:28.15N - 005:31.17.4E, AROUND 12NM SW OF OFF BAYELSA, NIGERIA.

A MERCHANT VESSEL WAS ATTACKED AND BOARDED BY PIRATES. NIGERIAN NAVY NOTIFIED. TEN CREWS REPORTED KIDNAPPED. FURTHER DETAILS ARE AWAITED.

VESSELS TRANSITING IN THE AREA ARE ADVISED TO EXERCISE EXTREME CAUTION AND REMAIN VIGILANT. MAINTAIN STRICT ANTI PIRACY WATCH AND MEASURES.

VESSELS ARE ADVISED TO STAY AT LEAST 200NM PREFERABLY 250NM FROM NIGERIAN COAST. GO FOR DIRECT BERTHING IF POSSIBLE. DO NOT DRIFT NEAR COAST.

ALL ATTACKS AND SUSPICIOUS SIGHTINGS SHOULD BE REPORTED TO LOCAL AUTHORITIES AND TO THE IMB PIRACY REPORTING CENTRE AS PER IMO CIR 1334

IMB PIRACY REPORTING CENTRE

24 HOURS ANTI PIRACY HELPLINE +603 2031 0014 FAX: +603 2078 5769.

WHATSAPP OR TELEGRAM AT +601126593057. PHOTOGRAPH OR VIDEO SUBMISSION ENCOURAGED.

EMAIL:IMBKL@ICC-CCS.ORG /:PIRACY@ICC-CCS.ORG

17.09.2019: 0338 UTC: POSN: 16:30N - 040:08E, RED SEA.

A YACHT WAS HIJACKED BY ABOUT SIX ARMED PIRATES FROM A SPEED BOAT.  FURTHER REPORT AWAITED.

ALL VESSELS ARE ADVISED TO MAINTAIN A VIGILANT ANTI PIRACY WATCH AND MEASURES.

PASSING SHIPS ARE ADVISED TO STAY CLEAR FROM THIS POSITION.

EARLY ASSESSMENT / DETECTION WILL ALLOW SHIPS TO TAKE EVASIVE MEASURES TO PREVENT BOARDING AND REQUEST FOR ASSISTANCE.

REPORT ALL ATTACKS AND SUSPICIOUS SIGHTINGS TO LOCAL AUTHORITIES AND TO THE IMB PRC AS PER IMO CIR 1334

IMB PIRACY REPORTING CENTRE

24 HOURS ANTI-PIRACY HELPLINE +603 2031 0014 FAX: +603 2078 5769

EMAIL: IMBKL@ICC-CCS.ORG <mailto:IMBKL@ICC-CCS.ORG>  / PIRACY@ICC-CCS.ORG mailto:PIRACY@ICC-CCS.ORG

HYDROPAC 3048/19(62).

RED SEA.

ERITREA.

DNC 10.

1. M/V HIJACKED IN 16-30N 040-08E AT 170338Z SEP.

VESSELS ARE ADVISED TO KEEP CLEAR OF THIS

POSITION AND TO EXERCISE EXTREME CAUTION.

REPORTS TO IMB PIRACY REPORTING CENTER,

PHONE: 603 2031 0014, 603 2078 5763,

FAX: 603 2078 5769,

E-MAIL: IMBKL@ICC-CCS.ORG, PIRACY@ICC-CCS.ORG.

2. CANCEL THIS MSG 250237Z SEP 19.

191600 UTC OCT 2021

TO ALL SHIPS TRANSITING IN / OFF GHANA / BENIN / NIGERIA / GULF OF GUINE

WARNING - SUSPICIOUS TUG BOA

THE IMB PRC RECEIVED THE FOLLOWING INFORMATION FROM ECOWAS MMCC ZONE F.

INFORMATION RECEIVED INDICATES THAT ON 19.10.2021 AT 0930 UTC AN UNKNOWN SUSPICIOUS TUG BOAT WAS SIGHTED IN POSN: 01:50N - 001:11E ABOUT 239NM SSE OF TEMA, GHANA. THE TUG BOAT HAS NO NAME AND NOT TRANSMITTING AIS. THE TUG BOAT MAY BE USED AS A PIRATE MOTHER VESSEL.

DESCRIPTION OF THE SUSPICIOUS TUG BOAT: APPROXIMATELY 24 M LONG LOOKED RUSTY WITH BLACK SUPERSTRUCTURE AND WHITE HULL

ALL VESSELS ARE ADVISED TO MAINTAIN VIGILANT ANTI PIRACY WATCH AND MEASURES.

PASSING SHIPS ARE ADVISED TO BE CAUTIOUS WHEN TRANSITING THE ABOVE AREA

EARLY ASSESSMENT / DETECTION WILL ALLOW SHIPS TO TAKE EVASIVE MEASURES TO PREVENT BOARDING AND REQUEST FOR ASSISTANCE

REPORT ALL ATTACKS AND SUSPICIOUS SIGHTINGS TO LOCAL AUTHORITIES AND TO THE IMB PRC AS PER IMO CIR 1334

IMB PIRACY REPORTING CENTRE

24 HOURS ANTI PIRACY HELPLINE +603 2031 0014 FAX: +603 2078 5769.

WHATSAPP OR TELEGRAM AT +601126593057. PHOTOGRAPH OR VIDEO SUBMISSION ENCOURAGED.

EMAIL: IMBKL@ICC-CCS.ORG / PIRACY@ICC-CCS.ORG

NAVAREA XI 0251/21

TSUNAMI INFORMATION.

PACIFIC OCEAN.

EARTHQUAKE, MAGNITUDE 7.2, OCCURRED

AT ABOUT 111746Z AUG IN 06-30N 126-48E,

VICINITY PHILIPPINES.

TSUNAMI THREATENED TO OCCUR.

VESSELS COAST AREA REQUESTED TO BE

CAUTION ADVISED.

CANCEL THIS MSG 121800Z AUG.

NAVAREA XII 365/2021 (16)

EASTERN NORTH PACIFIC. GULF OF ALASKA. ALASKA. EARTHQUAKE WITH MAGNITUDE OF 8.2 HAS OCCURRED IN VICINITY 55-18N 157-48W AT 290616Z JUL. A TSUNAMI HAS BEEN GENERATED WHICH COULD CAUSE DAMAGE TO COASTS OF SOUTH ALASKA, THE ALASKA PENINSULA AND THE ALEUTIAN ISLANDS. TSUNAMI WAVE HEIGHTS CANNOT BE PREDICTED AND MAY BE A SERIES OF WAVES WHICH COULD BE DANGEROUS FOR SEVERAL HOURS AFTER THE INITIAL WAVE ARRIVAL.

290837Z JUL 2021 PTWC 290802Z JUL 21.

NAVAREA IV 702/21(26).

CARIBBEAN SEA.

HAITI.

1. EARTHQUAKE WITH MAGNITUDE OF 7.2 OCCURRED

IN 18-36N 073-30W AT 141229Z AUG.

TSUNAMI WAVES ARE POSSIBLE WHICH COULD

CAUSE DAMAGE TO THE SURROUNDING COASTS.

2. TSUNAMI ACTIVITY IS FORECASTED TO START AT

THE FOLLOWING TIMES:

A. JEREMIE 18-36N 074-06W AT 1239Z.

B. JACAMEL 18-06N 072-30W AT 1318Z.

C. PORT AU PRINCE 18-30N 072-24W AT 1328Z.

3. TSUNAMI WAVES REACHING THREE METERS ABOVE

THE TIDE LEVEL ARE POSSIBLE AND MAY BE

A SERIES OF WAVES WHICH COULD BE DANGEROUS

FOR SEVERAL HOURS AFTER THE INITIAL WAVE ARRIVAL.

4. CANCEL NAVAREA IV 701/21.

NAVAREA IV 301/2021 (25)

EASTERN CARIBBEAN SEA. SAINT VINCENT.

1. RESTRICTED AREA DUE TO VOLCANIC ACTIVITY IN AREA BOUND BY 13-15.00N 061-19.60W, 13-18.00N 061-18.50W, 13-22.08N 061-15.38W, 13-26.00N 061-09.91W, 13-22.29N 061-04.90W, 13-19.88N 061-04.10W, 13-14.41N 061-03.90W.

2. CANCEL NAVAREA IV 298/21.

121539Z APR 2021 ST. VINCENT AND THE GRENADINES 121435Z APR 21.

NAVAREA XIV WARNING 4/22
SOUTH PACIFIC OCEAN
KIRIBATI / COOK ISLANDS / AMERICAN SAMOA / SAMOA / NIUE / TONGA / 
WALLIS AND FUTUNA / TOKELAU / NEW ZEALAND / FR. POLYNESIA / TUVALU / 
FIJI / PITCAIRN / HOWLAND-BAKER / NAURU / NEW CALEDONIA / SOLOMON IS. / 
VANUATU / KERMADEC ISLANDS / JARVIS IS. / MARSHALL ISLANDS
TSUNAMI THREAT MESSAGE ISSUED BY PACIFIC TSUNAMI WARNING 
CENTRE AT 152006 UTC JAN 22. A VOLCANIC ERUPTION HAS OCCURRED IN VICINITY 
20-30S 175-24W LOCATION TONGA AT 150427 UTC JAN 22. HAZARDOUS TSUNAMI WAVES 
FROM THIS EARTHQUAKE ARE POSSIBLE WITHIN THE NEXT 
THREE HOURS ALONG SOME COASTS OF:
TONGA, NIUE, FIJI, WALLIS AND FUTUNA SAMOA, KERMADEC ISLANDS, TOKELAU, 
COOK ISLANDS, VANUATU, TUVALU, NEW ZEALAND, KIRIBATI, HOWLAND AND BAKER,
NEW CALEDONIA, FRENCH POLYNESIA, JARVIS ISLAND, SOLOMON ISLANDS,
PALMYRA ISLAND, NAURU, MARSHALL ISLANDS, KOSRAE, JOHNSTON ISLAND, 
PAPUA NEW GUINEA, AUSTRALIA, PITCAIRN, POHNPEI, WAKE ISLAND, ANTARCTICA, 
CHUUK, MINAMITORISHIMA, INDONESIA, YAP, CHILE, JAPAN, PALAU, RUSSIA, 
PHILIPPINES, MEXICO, TAIWAN, DPR OF KOREA, REPUBLIC OF KOREA, ECUADOR, 
COSTA RICA, CHINA, GUATEMALA, EL SALVADOR, PERU, VIETNAM, MALAYSIA, 
NICARAGUA, PANAMA, HONDURAS, COLOMBIA AND BRUNEI.
NNNN

NAVAREA I 022/22
1. NAVAREA I WARNINGS IN FORCE AT 041000 UTC MAR 2022:

2021 SERIES: 031.

2022 SERIES: 020, 021, 022.

NOTES:

A. TEXTS OF NAVAREA I WARNINGS ISSUED EACH WEEK ARE PUBLISHED IN WEEKLY EDITIONS OF THE ADMIRALTY NOTICES TO MARINERS BULLETIN (ANMB).

B. NAVAREA I WARNINGS LESS THAN 42 DAYS OLD (020/22 ONWARD) ARE PROMULGATED VIA ENHANCED GROUP CALL (EGC) AND/OR RELEVANT NAVTEX TRANSMITTERS.

C. THE COMPLETE TEXTS OF ALL IN-FORCE NAVAREA I WARNINGS, INCLUDING THOSE WHICH ARE NO LONGER BEING BROADCAST, ARE REPRINTED IN SECTION III OF ANMB IN WEEKS 1, 13, 26 AND 39 AND ARE ALSO AVAILABLE FROM THE UKHO WEBSITE AT: WWW.ADMIRALTY.CO.UK/RNW.

ALTERNATIVELY, THESE MAY BE REQUESTED BY E-MAIL FROM NAVAREA I CO-ORDINATOR AT: NAVWARNINGS@UKHO.GOV.UK

NAVAREA II 085/22

1. NAVAREA II WARNINGS IN FORCE AT 271630 UTC FEB 22:

2020 SERIES: 083,

2021 SERIES: 251, 476,

2022 SERIES: 020, 027, 040, 041, 046, 057, 066, 069, 071, 073,

079, 080, 082, 083, 085.

2. ONLY THOSE LESS THAN 42 DAYS OLD ARE DAILY BROADCAST ON SAFETY

NET AT 04H30 AND 16H30 UTC.

3. THE COMPLETE TEXTS OF ALL IN-FORCE NAVAREA II WARNINGS ARE

AVAILABLE FROM THE SHOM WEBSITE AT: DIFFUSION.SHOM.FR

4. ALTERNATIVELY, THESE MAY BE REQUESTED BY E-MAIL AT:

COORD.NAVAREA2@SHOM.FR

5. CANCEL NAVAREA II 067/22.

Nick to provide updates to this section, ref 1051

METAREA IV/XII: Should .5 be .9 and .6 be .10 and so on?

METAREA XIV: Agree with above comment. If suggested changes are accepted, subsequent numbers after .8 have to change.

Noted

Check sea ice

Think John said it was two words.

Moved from Principles to General section 9.1.

Check after

Neal: Covered by 2.3.  Consider removing.

Neal: Move to General section 9.1.

Neal: Low level detail, part of WMO functions, and not relevant to this Joint Manual.

Neal: Intent captured in 2.3.4.

Neal: Duplicate of para 2.3.2 to 2.3.5.

revise

‘weather and sea ice information’ checked through out this doc

METAREA XIV: Suggesting adding the word meteorological or atmospheric or similar before features to be more precise.

Neal Moodie: Intent captured in 2.3.4. Not replicated in WWNWS section

Duplicate of 2.4.1.3.

Intent of para contained in section 2.7.

Neal Moodie: Duplicate of 2.4.2.2.

Detail not replicated in WWNWS section. Duplicate of 2.3.4.

Comment from Neal Moodie

These numbers would also need to change if above changes are accepted.

done

renumber

Zhichao Wang: International EGC Services as per 470

MET IV/XII: Add International SafeyCast in 9.2.8 and add national safetycast in the note

Zhichao Wang: Review the term of ‘national EGC Services’ and get back to Chris for MET community

Neal: Intent captured in 2.3.4. Not replicated in WWNWS section.

ZW: Double check the appendix in 558/471

ZW: Check ref here in 558/470 if needed this para

METAREA XIV: I suggest using issued rather than given for both gales and ice accretion.

Need to renumber

Zhicaho: Alternative ‘’Issued immediately for broadcast’’

METAREA IV/XII: In 9.3.7,  add "when" between immediately and the

Will have a decision if these included as per MSC.470(101)

MSC.470 didn’t describe this.

METAREA XIV: This point would need updating then too. Remove surface weather chart

MET II: METAREA II : why six natutical miles and not five

MET XIV:

Zhichao Wang: As per WMO 558

Cross check sea ice section in MSC.470

4.2.3 Sea-ice information

4.2.3.1 Sea-ice information services will provide the limits of sea ice and icebergs, where

ice conditions pose a hazard to navigation.

MSC 101/24/Add.1

Annex 22, page 9

I:\MSC\101\MSC 101-24-Add.1.docx

4.2.3.2 Sea-ice information services could include information about sea-ice concentration

and stage of development.

4.2.3.3 Descriptions of the limit of all known ice, ice edge or iceberg risk are given using

latitude and longitude coordinates. The location of the ice, ice edge or iceberg risk are given

relative to the limit.

Use 'sea ice' as two words.

METAREA IV/XII: I can provide an example from METAREA IV and/or XII if that is appropriate. Our METAREA forecasts and warnings are lengthy compared to most others since we have to meet our many national customer needs as well. The METAREA forecasts for IV and XII could be an example of a METAREA forecast with a lot of detail.

Zhichao Wang: No item 9.3.1.3, should be 9.5.

METAREA IV/XII: section 11.1 add Safetycast after SafetyNET

Use generic term.

David Wyatt: Revise to reflect 'fast track' process as articulated in the resolution in the navtex manual