DQWG	DQWG18/3/1

Meeting 18	7 Feb 2023

Agenda Item 3.1

Report on the cross check of DQ chapters of S-1XX Product Specifications

# Submitted by review of S-1XX Product Specifications subWG

1. Introduction/Overview

According to the action DQWG 17/07, the subWG comprised of Chair, NL, SE and UNH has implemented the cross check of DQ chapters of S-104 and S-128.

2. Principles of the cross check of DQ chapters

The cross check of DQ chapters shall follow principles as below:

a) The cross check shall be carried out in accordance with IHO publication S-97 Ed 1.1.0 - “IHO Guidelines for Creating S-100 Product Specifications”.

b) Only the DQ chapters of S-1XX PSs shall be checked and the results will be presented in the form of cross check matrix.

c) DQ elements included in the other parts of each S-1XX PS shall be described in the form of Notes under its cross check matrix.

3. Implementation process of the cross check of DQ chapters

3.1 Identify the DQ requirements for S-1XX PS in S-97

The recommended data quality measures of each S-1XX PS have been identified by the subWG according to S-97 part C Table C-7-1 – Recommended data quality measures.

# Table 1 - DQ requirements for S-1XX PSs in S-97

| Data Quality Measure | DQ measure / description | Applicable to spatial representation types | S-104 | S-128 |
| --- | --- | --- | --- | --- |
| Completeness / Commission | numberOfExcessItems / This data quality measure indicates the number of items in the dataset, that should not have been present in the dataset. | All S-100 based PS | Y | Y |
| Completeness / Commission | numberOfDuplicateFeatureInstances / This data quality measure indicates the total number of exact duplications of feature instances within the data. | All S-100 based PS | Y | Y |
| Completeness / Omission | numberOfMissingItems / This data quality measure is an indicator that shows that a specific item is missing in the data. | All S-100 based PS | Y | Y |
| Logical Consistency / Conceptual Consistency | numberOfInvalidSurfaceOverlaps / This data quality measure is a count of the total number of erroneous overlaps within the data. Which surfaces may overlap and which must not is application dependent. Not all overlapping surfaces are necessarily erroneous. | PS with geometric surfaces. | N | Y |
| Logical Consistency / Domain Consistency | numberOfNonconformantItems / This data quality measure is a count of all items in the dataset that are not in conformance with their value domain. | All S-100 based PS | Y | Y |
| Logical Consistency / Format Consistency | physicalStructureConflictsNumber / This data quality measure is a count of all items in the dataset that are stored in conflict with the physical structure of the dataset. | All S-100 based PS | Y | Y |
| Logical Consistency / Topological Consistency | rateOfFaultyPointCurveConnections / This data quality measure indicates the number of faulty link-node connections in relation to the number of supposed link-node connections. This data quality measure gives the erroneous point-curve connections in relation to the total number of point-curve connections. | PS with curves. | N | Y |
| Logical Consistency / Topological Consistency | numberOfMissingConnectionsUndershoots / This data quality measure is a count of items in the dataset within the parameter tolerance that are mismatched due to undershoots. | PS with curves | N | Y |
| Logical Consistency / Topological Consistency | numberOfMissingConnectionsOvershoots / This data quality measure is a count of items in the dataset within the parameter tolerance that are mismatched due to overshoots. | PS with curves. | N | Y |
| Logical Consistency / Topological Consistency | numberOfInvalidSlivers / This data quality measure is a count of all items in the dataset that are invalid sliver surfaces. A sliver is an unintended area that occurs when adjacent surfaces are not digitized properly. The borders of the adjacent surfaces may unintentionally gap or overlap to cause a topological error. | PS with geometric surfaces. | N | Y |
| Logical Consistency / Topological Consistency | numberOfInvalidSelfIntersects / This data quality measure is a count of all items in the dataset that illegally intersect with themselves. | PS with curves / geometric surfaces. | N | Y |
| Logical Consistency / Topological Consistency | numberOfInvalidSelfOverlap / This data quality measure is a count of all items in the dataset that illegally self-overlap. | PS with curves / geometric surfaces. | N | Y |
| Positional Accuracy / Absolute or External Accuracy | Root Mean Square Error / Standard deviation, where the true value is not estimated from the observations but known a priori. | PS with objects that have coordinative values associated. | Y | Y |
| Positional Accuracy / Vertical Position Accuracy | linearMapAccuracy2Sigma / Half length of the interval defined by an upper and lower limit in which the true value lies with probability 95%. | PS with objects that have a vertical coordinative values associated. | Y | Y |
| Positional Accuracy / Horizontal Position Accuracy | linearMapAccuracy2Sigma / Half length of the interval defined by an upper and lower limit in which the true value lies with probability 95%. | PS with objects that have a horizontal coordinative values associated. | Y | Y |
| Positional Accuracy / Gridded Data Position Accuracy | Root mean square error of planimetry / Radius of a circle around the given point, in which the true value lies with probability P. | PS with objects that have a gridded coordinative values associated. | Y | N |
| Temporal Quality / Temporal Consistency | Correctness of ordered events or sequences, if reported. | PS with objects that have a time value associated. | Y | Y |
| Thematic Accuracy / Thematic Classification Correctness | miscalculationRate / This data quality measure indicates the number of incorrectly classified features in relation to the number of features that are supposed to be there. [Adapted from ISO 19157] This is a RATE which is a ratio, and is expressed as a REAL number representing the rational fraction corresponding to the numerator and denominator of the ratio. For example, if there are 1 items that are classified incorrectly and there are 100 of the items in the dataset then the ratio is 1/100 and the reported rate = 0.01. | All S-100 based PS. | Y | Y |
| Aggregation Measures / Aggregation Measures | DataProductSpecificationPassed / This data quality measure is a boolean indicating that all requirements in the referred data Product Specification are fulfilled. | PS that a require a complete pass of all elements of a dataset/dataset series/spatial object types | Y | Y |
| Aggregation Measures / Aggregation Measures | DataProductSpecificationFailRate / This data quality measure is a number indicating the number of data Product Specification requirements that are not fulfilled by the current product/dataset in relation to the total number of data Product Specification requirements. | PS that a require a complete pass of all elements of a dataset/dataset series/spatial object types | Y | Y |

Y= required, N= not required.

3.2 Implement the cross check of DQ chapter of S-1XX PSs one by one

The cross check of DQ chapters of S-1XX PSs including S-104 Ed1.0.0 and S-128 Ed1.0.0 have been implemented one by one to verify whether these recommended DQ measures are included.

# 3.2.1 S-104

3.2.1.1 DQ chapters of S-104

The DQ chapter of S-104 is as follow:

3.2.1.2 Result of cross check

| Recommendations | S-104 |
| --- | --- |
| 1.Completeness | Y |
| 2.Conceptual consistency | N/A |
| 3. Domain consistency | Y |
| 4. Format consistency | Y |
| 5. Topological consistency | N/A |
| 6. Positional Accuracy | Y |
| 7. Thematic Accuracy | Y |
| 8. Temporal Quality | Y |
| 9. Aggregation | Y |
| 10. Introduction to DQ Paragraph | Y |

Y=YES, N=NO, N/A=not application

## NOTES:

Lack of detailed text description of each quality element.

3.2.1.3 DQ elements included in the other parts of S-104

No DQ element is included in the other parts of S-104.

# 3.2.2 S-128

3.2.2.1 DQ chapters of S-128

The DQ chapter of S-128 is as follow:

3.2.2.2 Result of cross check

| Recommendations | S-128 |
| --- | --- |
| 1.Completeness | N |
| 2.Conceptual consistency | N |
| 3. Domain consistency | N |
| 4. Format consistency | N |
| 5. Topological consistency | N |
| 6. Positional Accuracy | N |
| 7. Thematic Accuracy | N |
| 8. Temporal Quality | N |
| 9. Aggregation | N |
| 10. Introduction to DQ Paragraph | Y |

Y=YES, N=NO, N/A=not application

## NOTES:

The following new text has been added to the introduction：Elements specifically required for the data product (none currently identified for S-128).

3.2.2.3 DQ elements included in the other parts of S-128

No DQ element is included in the other parts of S-128.

4. Cross Check Matrix

| Recommendations | 104 | 128 |
| --- | --- | --- |
| 1.Completeness | Y | N |
| 2.Conceptual consistency | N/A | N |
| 3. Domain consistency | N | N |
| 4. Format consistency | N | N |
| 5. Topological consistency | N/A | N |
| 6. Positional Accuracy | Y | N |
| 7. Thematic Accuracy | Y | N |
| 8. Temporal Quality | Y | N |
| 9. Aggregation | Y | N |
| 10. Introduction to DQ Paragraph | Y | Y |

Y=YES, N=NO, N/A=not application

## NOTES:

a) Similar to the previously reviewed product specifications, DQ chapters of S-104 and S-128 are not in a harmonized way.

b) DQ chapters of S-128 do not conform to the S-97, except for "Introduction to DQ Paragraph", there are no other recommended data quality elements in S-128.

c) S-128 does not implement the table C-7-1 – Recommended data quality measures of S-97.

5. Recommendations

It is recommended to:

a) Feedback comments and suggestions to developers of the two product specifications.

b) Continue review of new and amended Product Specifications.

6. Action

The DQWG is requested to:

# Note the information provided;

# Approve the recommendations above.

# Text boxes

SUMMARY

Executive Summary: The subWG has carried out the cross check of DQ chapters of published S-1XX PSs including S-104 and S-128. The results show that the implementation of S-97 Part C in these PSs is necessary to be harmonized and improved.

Action to be taken: See Section 5&6

Related documents: Action DQWG17/07