S-100 – Part XX

Discovery Metadata for Information Exchange Catalogues

Page intentionally left blank

Contents

4a-1	Scope	1

4a-2	Conformance	1

4a-2.1	Conformance of this Profile with other Standards	1

4a-2.2	Backward compatibility	2

4a-3	Conformance to this Profile	2

4a-4	Normative references	2

4a-4.1	Profile definition	2

4a-4.2	Informative references	2

4a-5	Requirements	3

4a-5.1	Business purpose and Intended use	3

4a-5.2	Metadata for describing geographic data and other resources	4

4a-5.3	Obligations/conditions	5

4a-5.4	Minimum metadata requirements	5

4a-5.5	S-100 compliancy categories	11

4a-5.6	Recommended metadata for geographic datasets	11

4a-5.7	Variations and preferences	14

4a-5.7.1	Metadata element metadataIdentifier	14

4a-5.7.2	Metadata element parentMetadata	14

4a-5.7.3	Geographic extent of the dataset	14

4a-5.7.4	Data and Date Time information	14

4a-5.7.5	Metadata extension information	15

4a-5.8	Metadata for services	16

Appendix 4a-A  Metadata Schema Class Information	19

Appendix 4a-B  Data Dictionary	21

Appendix 4a-C  Metadata Implementation	23

Appendix 4a-D  Discovery Metadata for Information Exchange Catalogues	25

Appendix 4a-E  Metadata Extensions	45

Page intentionally left blank

# Scope

The S-100 Discovery Metadata for Information Exchange Catalogues profile described in  this part provides a specification for describing and creating exchange catalogues that enables users to identify, discover and manage content of the S-100 exchange sets.  More importantly it leverages XML to allow machine to machine discovery and exchange of information about about geographic datasets commonly produced by hydrographic organizations. Its purpose is the creation of metadata records that provide information about the identification, spatial and temporal extent, quality, application schema, spatial reference system, and distribution of digital geographic data. It is applicable to the cataloguing of datasets, clearinghouse activities, and the full description of geographic and non-geographic resources.

For information exchange, there are several categories of metadata required: metadata about the overall exchange catalogue, metadata about each of the datasets contained in the catalogue, and metadata about the support files that make up the package. If the exchange catalogue contains any Feature, Portrayal or Interoperability Catalogues there is a provision to carry additional metadata about those.

This document is intended for developers and implementers of metadata applications, and provides a basic understanding of the principles and the overall requirements for standardisation of geographic information. It should be used in conjunction with the standards listed under clause 4a-4 – Normative references.

# Conformance

## Conformance of this Profile with other Standards

In addition to the elements listed in ISO 19115-1, this profile also adopts all associated 19115-1 obligations and conditions, with the exception of the metadataIdentifier element which has been changed from optional to mandatory.  This has been done to facilitate the implementation and management of metadata records by allowing instances of duplicate metadata records to be identified, and defining the relationship of a child metadata record with its parent metadata record. The specifics of any metadata hierarchy relationships will be detailed in the product specifications.

Taking into account the change identified above, and the requirements documented in ISO 19106:2004, this Profile meets the requirements of conformance class 1. The Profile is a community profile of ISO 19115-1 and includes an extension in the context permitted by the base standard.

This profile includes parentMetadata as a core metadata element for geographic datasets. If a dataset metadata record has a parent metadata record, then this element becomes mandatory and therefore should be considered a ‘core’ element.  Guidance on the XML implementation of this profile is included at Appendix 4a-C.

## Backward compatibility

According to ISO 19115-1:2014, ISO continues to make the UML models from ISO 19115:2003/Cor 1:2006 available for use. Backward compatibility is to be provided using a transformation service.

# Conformance to this Profile

Any metadata claiming conformance to this Profile shall:

- Have content according to the data dictionary definitions in Annex B of ISO 19115-1, (including changes required by ISO 19115-1 Amendment 1:2018) with the exception of the metadata element metadataIdentifier which has a mandatory obligation;

- Prove conformance by validating XML document instances against the S-100 Metadata Profile schemas which are available from the IHO website at Profiles based on this Profile.

All product specific implementations of this profile shall provide an Extensible Stylesheet Language (XSL) transform file/resource that can translate the XML document instances into the S-100 Metadata Profile XML format. These resulting XML document instances shall be validated using the ISO/TS 19115-3 XSDs.

# Normative references

The following referenced documents are required for the application of this document. For dated references, only the edition cited applies. For undated references, the latest edition of the referenced document (including amendments) applies.

## Profile definition

The following documents were the references used to define the S-100 Metadata Profile:

ISO 19115-1:2014, Geographic information – Metadata – Part 1 - Fundamentals

ISO 19115-1/Amdt01:2018, Geographic information – Metadata – Part 1 - Fundamentals (Amendment 1)

ISO 19115-2:2009, Geographic information - Metadata - Part 2: Extensions for imagery and gridded data

ISO 19119:2016, Geographic information – Services

ISO/TS 19115-3:2016, Geographic information - Metadata - XML schema implementation for fundamental concepts

## Informative references

ISO 19115:2003, Geographic information – Metadata

ISO 19115:2003/Cor.1:2006, Geographic information - Metadata (Technical Corrigendum 1)

ISO/TS 19139:2007, Geographic information - Metadata - XML schema implementation

# Overview

###### Introduction

###### Overview

Figures 4a-D-1 to 4a-D-3 outline the overall concept of an S-100 exchange set for the interchange of geospatial data and its relevant metadata. Figure 4a-D-1 depicts the realization of the ISO 19115-3 classes which form the foundation of the exchange set. The overall structure of S-100 Exchange Sets is modelled in Figure 4a-D-3. More detailed information about the various classes is shown in Figure 4a-D-2 and a textual description in the tables at clause 3.

The discovery metadata classes have numerous attributes which enable important information about the datasets and accompanying support files to be examined without the need to process the data, for example decrypt, decompress, load etc.  Other catalogues can be included in the Exchange Set in support of the datasets such as feature, portrayal, coordinate reference systems, codelists etc. The attribute “purpose” of the support file metadata provides a mechanism to update support files more easily.

Figure 4a-D-1 Realization of the Exchange Set Classes

The S100_ExchangeCatalogue is an XML instance, which provides the information needed to exploit all the components of an Exchange Set. It consists of sections for the catalogues and datasets with subsections for support file metadata and a reference to classic ISO 19115-1 dataset metadata. The Exchange Catalogue must be named CATALOG.XML.

Figure 4a-D-2 – S-100 Exchange Set Catalogue

The S-100 Exchange set is a container that combines all the elements needed for the exchange of S-100 data. The exchange set may include S-100 based datasets, files, feature catalogues and portrayal catalogues as shown in figure 4a-D-3 below.

Figure 4a-D-3 – S-100 Exchange Set

Figure 4a-D-4 – S-100 Exchange Set - class details

There are two types of Exchange Sets: simple product Exchange Sets and multiple product Exchange Sets. If only one product type (for example S-101) is included, the Exchange Set is simple type. If more than one product type (for example S-101 and S-102) is included, the Exchange Set is multiple type.

An Exchange Set can contain S-100 conformant dataset files, support files and catalogue files. It can also contain S-57 dataset files.

In any type of S-100 conformant Exchange Set all S-100 products will be available from a top root directory named S100_ROOT. This will be the only top root directory in Exchange Sets containing only S-100 products. Together with the ENC_ROOT and INFO directories (used for S-57 ENCs) the S100_ROOT directory is one of three top directories in a multiple product Exchange Set containing both S-57 and S-100 products.

Page intentionally left blank

###### Elements of the exchange set

S100_ExchangeSet

An S-100 Exchange Set is an aggregation of all the various elements required to support the interchange of geospatial data and metadata. The MultiAggregation association introduces the concept of using subsets which could be domain oriented, for example packaged by scale, producer, region etc.

| Role Name | Name | Description | Mult | Type | Remarks |
| --- | --- | --- | --- | --- | --- |
| Class | S100_ExchangeSet | Aggregation of the elements comprising an exchange set for the transfer of data | - | - | - |
| Role | aggregateFile | Collection of support files in the exchange set | 0..* | - |  |
| Role | partOf | Collection of datasets which are part of the exchange set | 0..* | - |  |
| Role | aggregateCatalogue | Collection of catalogues | 0..* | - |  |
| Role | superSet | The master container exchange set which can contain a subSet of exchange sets | 0..* |  |  |
| Role | subSet | Exchange set which is part of the superSet | 0..* |  |  |

S100_ExchangeCatalogue

Each exchange set has a single S100_ExchangeCatalogue which contains meta information for the data and support files in the exchange set.

| Role Name | Name | Description | Mult | Type | Remarks |
| --- | --- | --- | --- | --- | --- |
| Class | S100_ExchangeCatalogue | An exchange catalogue contains the discovery metadata about the exchange datasets and support files | - | - | - |
| Attribute | identifier | Uniquely identifies this exchange catalogue | 0..1 | S100_CatalogueIdentifier |  |
| Attribute | contact | Details about the issuer of this exchange catalogue | 0..1 | S100_CataloguePointOfContact |  |
| Attribute | productSpecification | Details about the product specifications used for the datasets contained in the exchange catalogue | 0..* | S100_ProductSpecification |  |
| Attribute | metadataLanguage | Details about the Language | 0..1 | CharacterString | Default without this is English |
| Attribute | exchangeCatalogueDescription | Description of what the exchange catalogue contains | 0..1 | CharacterString |  |
| Attribute | exchangeCatalogueComment | Any additional Information | 0..1 | CharacterString |  |
| Attribute | compressionFlag | Is the data compressed | 0..1 | Boolean | Yes or No |
| Attribute | sourceMedia | Distribution media | 0..1 | CharacterString |  |
| Role | datasetDiscoveryMetadata | Exchange catalogues may include or reference discovery metadata for the datasets in the exchange set | 0..* | Aggregation S100_DatasetDiscoveryMetadata |  |
| Role | -- | Metadata for catalogue | 0..* | Aggregation S100_CatalogueMetadata | Metadata for the feature, portrayal, and interoperability catalogues, if any |
| Role | supportFileDiscoveryMetadata | Exchange catalogues may include or reference discovery metadata for the support files in the exchange set | 0..* | Aggregation S100_SupportFileDiscoveryMetadata |  |

S100_CatalogueIdentifier

| Role Name | Name | Description | Mult | Type | Remarks |
| --- | --- | --- | --- | --- | --- |
| Class | S100_CatalogueIdentifier | An exchange catalogue contains the discovery metadata about the exchange datasets and support files | - | - | - |
| Attribute | identifier | Uniquely identifies this exchange catalogue | 1 | CharacterString |  |
| Attribute | editionNumber | The edition number of this exchange catalogue | 1 | CharacterString |  |
| Attribute | dateTime | Creation date and time of the exchange catalogue, including time zone | 1 | Date | Format: yyyymmddThhmmssZ |

S100_CataloguePointofContact

| Role Name | Name | Description | Mult | Type | Remarks |
| --- | --- | --- | --- | --- | --- |
| Class | S100_CataloguePointOfContact | Contact details of the issuer of this exchange catalogue | - | - | - |
| Attribute | organization | The organization distributing this exchange catalogue | 1 | CharacterString | This could be an individual producer, value added reseller, etc. |
| Attribute | phone | The phone number of the organization | 0..1 | CI_Telephone |  |
| Attribute | address | The address of the organization | 0..1 | CI_Address |  |

S100_Dataset

| Role Name | Name | Description | Mult | Type | Remarks |
| --- | --- | --- | --- | --- | --- |
| Class | S100_Dataset |  | - | - | - |
| Role | composedOf | An exchange set is composed of 0 or more datasets | 0..* | - |  |
| Role | datasetCatalogue | Catalogue which is related to this dataset | 0..* | - |  |

S100_DatasetDiscoveryMetadata

| Role Name | Name | Description | Mult | Type | Remarks |
| --- | --- | --- | --- | --- | --- |
| Class | S100_DatasetDiscoveryMetadata | Metadata about the individual datasets in the exchange catalogue | - | - | - |
| Attribute | fileName | Dataset file name | 1 | CharacterString |  |
| Attribute | fileLocation | Full location from the exchange set root directory | 0..1 | CharacterString | Path relative to the root directory of the exchange set. The location of the file after the exchange set is unpacked into directory <S100_ROOT> will be <S100_ROOT>/<fileLocation>/<filename> Without fileLocation the exchange set is unpacked into directory <S100_ROOT>/<filename> |
| Attribute | description | Short description giving the area or location covered by the dataset | 0..1 | CharacterString | For example, a harbour or port name, between two named locations etc. |
| Attribute | dataProtection | Indicates if the data is encrypted | 0..1 | Boolean | 0 indicates an unencrypted dataset 1 indicates an encrypted dataset |
| Attribute | protectionScheme | Specification or method used for data protection | 0..1 | S100_ProtectionScheme | For example S-63 |
| Attribute | digitalSignatureReference | Digital Signature of the file | 1 | S100_DigitalSignature | Specifies the algorithm used to compute digitalSignatureValue |
| Attribute | digitalSignatureValue | Value derived from the digital signature | 1 | S100_DigitalSignatureValue | The value resulting from application of digitalSignatureReference Implemented as the digital signature format specified in Part 15 |
| Attribute | copyright | Indicates if the dataset is copyrighted | 0..1 | MD_LegalConstraints ->MD_RestrictionCode <copyright> (ISO 19115-1) |  |
| Attribute | classification | Indicates the security classification of the dataset | 0..1 | Class MD_SecurityConstraints>MD_ClassificationCode (codelist) | 1. unclassified 2. restricted 3. confidential 4. secret 5. top secret 6. sensitive but unclassified 7. for official use only 8. protected 9. limited distribution |
| Attribute | purpose | The purpose for which the dataset has been issued | 0..1 | MD_Identification>purpose (codelist) | 1. new dataset 2. new edition 3. update 4. re-issue 5. cancellation |
| Attribute | specificUsage | The use for which the dataset is intended | 0..1 | MD_USAGE>specificUsage (character string) MD_USAGE>userContactInfo (CI_Responsibility) | For example, in the case of ENCs this would be a Navigational Purpose classification |
| Attribute | editionNumber | The edition number of the dataset | 0..1 | CharacterString | When a data set is initially created, the edition number 1 is assigned to it. The edition number is increased by 1 at each new edition. Edition number remains the same for a re-issue. |
| Attribute | updateNumber | Update number assigned to the dataset and increased by one for each subsequent update | 0..1 | CharacterString | Update number 0 is assigned to a new dataset |
| Attribute | updateApplicationDate | This date is only used for the base cell files (that is new data set, re-issue and new edition), not update cell files. All updates dated on or before this date must have been applied by the producer | 0..1 | Date |  |
| Attribute | issueDate | Date on which the data was made available by the data producer | 0..1 | Date |  |
| Attribute | issueTime | Time of day at which the data was made available by the data producer | 0..1 | Time | The S-100 datatype Time |
| Attribute | productSpecification | The product specification used to create this dataset | 0..1 | S100_ProductSpecification | If not available, the default is to use file extension, for example S421 for S-421, etc. |
| Attribute | producingAgency | Agency responsible for producing the data | 0..1 | CI_Responsibility>CI_Organisation or CI_Responsibility>CI_Individual | See Tables 4a-2 and 4a-3 |
| Attribute | optimumDisplayScale | The scale with which the data is optimally displayed | 0..1 | Integer | Example: A scale of 1:25000 is encoded as 25000 |
| Attribute | maximumDisplayScale | The maximum scale with which the data is displayed | 0..1 | Integer |  |
| Attribute | minimumDisplayScale | The minimum scale with which the data is displayed | 0..1 | Integer |  |
| Attribute | horizontalDatumReference | Reference to the register from which the horizontal datum value is taken | 0..1 | characterString | For example, EPSG |
| Attribute | horizontalDatumValue | Horizontal Datum of the entire dataset | 0..1 | Integer | For example, 4326 |
| Attribute | epoch | Code denoting the epoch of the geodetic datum used by the CRS | 0..1 | CharacterString | For example, G1762 for the 2013-10-16 realization of the geodetic datum for WGS84 |
| Attribute | verticalDatum | Vertical Datum of the entire dataset | 0..1 | S100_VerticalAndSoundingDatum |  |
| Attribute | soundingDatum | Sounding Datum of the entire dataset | 0..1 | S100_VerticalAndSoundingDatum |  |
| Attribute | dataType | The encoding format of the dataset | 1 | S100_DataFormat |  |
| Attribute | dataTypeVersion | The version number of the dataType. | 1 | CharacterString |  |
| Attribute | dataCoverage | Provides information about data coverages within the dataset | 0..* | S100_DataCoverage |  |
| Attribute | comment | Any additional information | 0..1 | CharacterString |  |
| Attribute | layerID | Identifies other layers with which this dataset is intended to be used or portrayed | 0..* | CharacterString | For example, a marine protected area dataset needs an ENC dataset to portray as intended in an ECDIS |
| Attribute | defaultLocale | Default language and character set used in the dataset | 0..1 | PT_Locale | In absence of defaultLocale the language is English |
| Attribute | otherLocale | Other languages and character sets used in the dataset | 0..* | PT_Locale |  |
| Attribute | metadataFileIdentifier | Identifier for metadata file | 0..1 | CharacterString | For example, for ISO 19115-3 metadata file |
| Attribute | metadataPointOfContact | Point of contact for metadata | 0..1 | CI_Responsibility>CI_Individual or CI_Responsibility>CI_Organisation | Only if metadataPointOfContact is different to producingAgency |
| Attribute | metadataDateStamp | Date stamp for metadata | 0..1 | Date | May or may not be the issue date |
| Attribute | metadataLanguage | Language(s) in which the metadata is provided | 1..* | CharacterString |  |
| Attribute | replacedData | If a data file is cancelled is it replaced by another data file | 0..1 | Boolean |  |
| Attribute | dataReplacement | Cell name | 0..* | CharacterString | A dataset may be replaced by 1 or more datasets |
| Role | -- | Containment of, or reference to, discovery metadata for the support files referenced in the dataset | 0..* | Aggregation S100_SupportFileDiscoveryMetadata |  |

S100_DataCoverage

| Role Name | Name | Description | Mult | Type | Remarks |
| --- | --- | --- | --- | --- | --- |
| Class | S100_DataCoverage | A spatial extent where data is provided; and the display scale information for the provided data | - | - | - |
| Attribute | ID | Uniquely identifies the coverage | 1 | Integer | - |
| Attribute | boundingBox | The extent of the dataset limits | 1 | EX_GeographicBoundingBox | - |
| Attribute | boundingPolygon | A polygon which defines the actual data limit | 1..* | EX_BoundingPolygon | - |
| Attribute | optimumDisplayScale | The scale with which the data is optimally displayed | 0..1 | Integer | Example: A scale of 1:25000 is encoded as 25000 |
| Attribute | maximumDisplayScale | The maximum scale with which the data is displayed | 0..1 | Integer |  |
| Attribute | minimumDisplayScale | The minimum scale with which the data is displayed | 0..1 | Integer |  |

S100_DigitalSignature

| Role Name | Name | Description | Code | Remarks |
| --- | --- | --- | --- | --- |
| Enumeration | S100_DigitalSignature | Algorithm used to compute the digital signature | - | - |
| Value | dsa | Digital Signature Algorithm | - | FIPS 186-4 (2013) |

S100_DigitalSignatureValue

| Role Name | Name | Description | Mult | Type | Remarks |
| --- | --- | --- | --- | --- | --- |
| Class | S100_DigitalSignatureValue | Signed Public Key plus the digital signature | - | Hex | Data type for digital signature values |

S100_VerticalAndSoundingDatum

| Role Name | Name | Description | Code | Remarks |
| --- | --- | --- | --- | --- |
| Enumeration | S100_VerticalAndSoundingDatum | Allowable vertical and sounding datums | - | - |
| Value | meanLowWaterSprings |  | 1 | (MLWS) |
| Value | meanLowerLowWaterSprings |  | 2 | - |
| Value | meanSeaLevel |  | 3 | (MSL) |
| Value | lowestLowWater |  | 4 | - |
| Value | meanLowWater |  | 5 | (MLW) |
| Value | lowestLowWaterSprings |  | 6 | - |
| Value | approximateMeanLowWaterSprings |  | 7 | - |
| Value | indianSpringLowWater |  | 8 | - |
| Value | lowWaterSprings |  | 9 | - |
| Value | approximateLowestAstronomicalTide |  | 10 | - |
| Value | nearlyLowestLowWater |  | 11 | - |
| Value | meanLowerLowWater |  | 12 | (MLLW) |
| Value | lowWater |  | 13 | (LW) |
| Value | approximateMeanLowWater |  | 14 | - |
| Value | approximateMeanLowerLowWater |  | 15 | - |
| Value | meanHighWater |  | 16 | (MHW) |
| Value | meanHighWaterSprings |  | 17 | (MHWS) |
| Value | highWater |  | 18 | (HW) |
| Value | approximateMeanSeaLevel |  | 19 | - |
| Value | highWaterSprings |  | 20 | - |
| Value | meanHigherHighWater |  | 21 | (MHHW) |
| Value | equinoctialSpringLowWater |  | 22 | - |
| Value | lowestAstronomicalTide |  | 23 | (LAT) |
| Value | localDatum |  | 24 | - |
| Value | internationalGreatLakesDatum1985 |  | 25 | - |
| Value | meanWaterLevel |  | 26 | - |
| Value | lowerLowWaterLargeTide |  | 27 | - |
| Value | higherHighWaterLargeTide |  | 28 | - |
| Value | nearlyHighestHighWater |  | 29 | - |
| Value | highestAstronomicalTide |  | 30 | (HAT) |

Note: The numeric codes are the codes specified in the IHO GI Registry for the equivalent listed values of the IHO Hydro domain attribute Vertical datum, since the registry does not at present (20 June 2018) contain entries for exchange set metadata and dataset metadata attributes.

S100_DataFormat

| Role Name | Name | Description | Code | Remarks |
| --- | --- | --- | --- | --- |
| Enumeration | S100_DataFormat | The encoding format | - | - |
| Value | ISO/IEC 8211 | The ISO 8211 data format as defined in Part 10a | - | - |
| Value | GML | The GML data format as defined in Part 10b | - | - |
| Value | HDF5 | The HDF5 data format as defined in Part 10c |  | - |
| Value | undefined | The encoding is defined in the Product Specification | - | Use product specification specific encoding means the data product and product specification is not intended for an IHO S-100 compliant system. |

S100_ProductSpecification

| Role Name | Name | Description | Mult | Type | Remarks |
| --- | --- | --- | --- | --- | --- |
| Class | S100_ProductSpecification | The Product Specification contains the information needed to build the specified product | - | - | - |
| Attribute | name | The name of the product specification used to create the datasets | 0..1 | CharacterString |  |
| Attribute | version | The version number of the Product Specification | 0..1 | CharacterString |  |
| Attribute | date | The version date of the product specification | 0..1 | Date |  |
| Attribute | number | The number (registry index) used to lookup the product in the Product Specification Register of the IHO GI registry | 1 | Integer | From the Product Specification Register, in the IHO Geospatial Information Registry |
| Attribute | compliancyCategory | The level of compliance of the Product Specification to S-100 | 0..1 | S100_CompliancyCategory | See clause 4a-5.5 |

S100_CompliancyCategory

| Role Name | Name | Description | Code | Remarks |
| --- | --- | --- | --- | --- |
| Enumeration | S100_CompliancyCategory |  | - | - |
| Value | category1 | IHO S-100 object model compliant |  |  |
| Value | category2 | IHO S-100 compliant with non-standard encoding |  |  |
| Value | category3 | IHO S-100 compliant with standard encoding |  |  |
| Value | category4 | IHO S-100 and IMO harmonized display compliant |  |  |

S100_ProtectionScheme

| Role Name | Name | Description | Code | Remarks |
| --- | --- | --- | --- | --- |
| Enumeration | S100_ProtectionScheme | Data protection schemes | - | - |
| Value | S100p15 | IHO S-100 Part 15 | - | See Part 15 |

S100_SupportFile

| Role Name | Name | Description | Mult | Type | Remarks |
| --- | --- | --- | --- | --- | --- |
| Class | S100_SupportFile |  | - | - | - |
| Role | aggregateFile | Collection of support files | 0..* | - |  |
| Role | supportFile | File which has information about a dataset | 0..* | - |  |

S100_SupportFileDiscoveryMetadata

| Role Name | Name | Description | Mult | Type | Remarks |
| --- | --- | --- | --- | --- | --- |
| Class | S100_SupportFileDiscoveryMetadata | Metadata about the individual support files in the exchange catalogue | - | - | - |
| Attribute | fileName | Name of the support file | 1 | CharacterString |  |
| Attribute | fileLocation | Full location from the exchange set root directory | 1 | CharacterString | Path relative to the root directory of the exchange set. The location of the file after the exchange set is unpacked into directory <S100_ROOT> will be <S100_ROOT>/<fileLocation>/<filename> |
| Attribute | purpose | The purpose for which the support file has been issued | 1 | S100_SupportFilePurpose | For example new, re-issue, new edition, update etc. |
| Attribute | editionNumber | The edition number of the support file | 1 | CharacterString | When a data set is initially created, the edition number 1 is assigned to it. The edition number is increased by 1 at each new edition. Edition number remains the same for a re-issue |
| Attribute | issueDate | Date on which the data was made available by the data producer | 1 | Date |  |
| Attribute | supportFileSpecification | The specification used to create this file | 1 | S100_SupportFileSpecification |  |
| Attribute | dataType | The format of the support file | 1 | S100_SupportFileFormat |  |
| Attribute | otherDataTypeDescription | Support file format other than those listed | 0..1 | CharacterString |  |
| Attribute | comment | Optional comment | 0..1 | CharacterString |  |
| Attribute | digitalSignatureReference | Digital Signature of the file | 0..1 | CharacterString | Reference to the appropriate digital signature algorithm |
| Attribute | digitalSignatureValue | Value derived from the digital signature | 0..1 | S100_DigitalSignatureValue | The value resulting from application of digitalSignatureReference Implemented as the digital signature format specified in Part 15 |
| Attribute | defaultLocale | Default language and character set used in the exchange catalogue | 0..1 | PT_Locale | A support file is expected to use only one locale, because other files can be created for other languages |

S100_SupportFileFormat

| Role Name | Name | Description | Code | Remarks |
| --- | --- | --- | --- | --- |
| Enumeration | S100_SupportFileFormat | The format used for the support file | - | - |
| Value | ASCII | UTF-8 text excluding control codes | - | Many files use UTF-8 |
| Value | JPEG2000 | JPEG2000 format | - | ISO 15444 |
| Value | HTML | Hypertext Markup Language | - |  |
| Value | XML | Extensible Markup Language | - |  |
| Value | XSLT | Extensible Stylesheet Language Transformations | - |  |
| Value | VIDEO | Representation of moving images in unspecified format | - |  |
| Value | TIFF | Tagged Image File Format | - |  |
| Value | PDF/A or UA | Portable Document Format | - | ISO 19005, ISO 32000 Product Specification developers should take careful consideration in using PDF as a support file format. It is recommended that PDF never be used in products that will be used on a navigation system as it may impair night vision |
| Value | LUA | Lua programming language | - |  |
| Value | other | Other format | - |  |

S100_SupportFilePurpose

| Role Name | Name | Description | Code | Remarks |
| --- | --- | --- | --- | --- |
| Enumeration | S100_SupportFilePurpose | The reason for inclusion of the support file in this exchange set | - | - |
| Value | new | A file which is new | - | Signifies a new file |
| Value | replacement | A file which replaces an existing file | - | Signifies a replacement for a file of the same name |
| Value | deletion | Deletes an existing file | - | Signifies deletion of a file of that name |

S100_SupportFileSpecification

| Role Name | Name | Description | Mult | Type | Remarks |
| --- | --- | --- | --- | --- | --- |
| Class | S100_SupportFileSpecification | The standard or specification to which a support file conforms | - | - | - |
| Attribute | name | The name of the specification used to create the support file | 1 | CharacterString |  |
| Attribute | version | The version number of the specification | 0..1 | CharacterString |  |
| Attribute | date | The version date of the specification | 0..1 | Date |  |

S100_CatalogueMetadata

| Role Name | Name | Description | Mult | Type | Remarks |
| --- | --- | --- | --- | --- | --- |
| Class | S100_CatalogueMetadata | Class for S-100 catalogue metadata | - | - | - |
| Attribute | fileName | The name for the catalogue | 1..* | CharacterString |  |
| Attribute | fileLocation | Full location from the exchange set root directory | 1..* | CharacterString | Path relative to the root directory of the exchange set. The location of the file after the exchange set is unpacked into directory <S100_ROOT> will be <S100_ROOT>/<fileLocation>/<filename> |
| Attribute | scope | Subject domain of the catalogue | 1..* | S100_CatalogueScope |  |
| Attribute | versionNumber | The version number of the product specification | 1..* | CharacterString |  |
| Attribute | issueDate | The version date of the product specification | 1..* | Date |  |
| Attribute | productSpecification | The product specification used to create this file | 1..* | S100_ProductSpecification |  |
| Attribute | digitalSignatureReference | Digital Signature of the file | 1 | S100_DigitalSignature | Reference to the appropriate digital signature algorithm |
| Attribute | digitalSignatureValue | Value derived from the digital signature | 1 | S100_DigitalSignatureValue | The value resulting from application of digitalSignatureReference Implemented as the digital signature format specified in Part 15 |
| Attribute | defaultLocale | Default language and character set used in the exchange catalogue | 1 | PT_Locale |  |
| Attribute | otherLocale | Other languages and character sets used in the exchange catalogue | 0..* | PT_Locale |  |

S100_CatalogueScope

| Role Name | Name | Description | Code | Remarks |
| --- | --- | --- | --- | --- |
| Enumeration | S100_CatalogueScope | The scope of the catalogue | - | - |
| Value | featureCatalogue | S-100 feature catalogue |  |  |
| Value | portrayalCatalogue | S-100 portrayal catalogue |  |  |
| Value | interoperabilityCatalogue | S-100 interoperability information |  |  |

S100_SV_ServiceIdentification

| Role Name | Name | Description | Mult | Type | Remarks |
| --- | --- | --- | --- | --- | --- |
| Class | S100_SV_ServiceIdentitification | Identification of capabilities which a service provider makes available to a service user through a set of interfaces which define a behaviour | - | - | Specialization of SV_ServiceIdentification (ISO 19115-1) and thereby a specialization of MD_Identification (The ISO attributes coupledResource and couplingType are not used.) |
| (Inherited properties) | (Inherited from SV_ServiceIdentification.) |
| Attribute | serviceType | A service type name | 1 | Class GenericName | GenericName is an abstract class for all names in a NameSpace. Each instance of a GenericName is either a LocalName or a ScopedName. A LocalName references a local object directly accessible from the NameSpace. A ScopedName is a composite of a LocalName for locating another NameSpace and a GenericName valid in the NameSpace. (ISO 19103). In short: A name that is defined in a namespace. For S-100 services, the recommended namespace is the IALA/IMO/IHO list of Maritime Services (TBD as of May 2018) |
| Attribute | serviceTypeVersion | The version of the service, supports searching based on the version of serviceType | 0..* | CharacterString |  |
| Attribute | accessProperties | Information about the availability of the service, including fees, planned available date and time, ordering instructions, turnaround | 0..1 | MD_StandardOrderProcess | ISO 19115-1 B.11.5 |
| Attribute | operatedDataset | Provides a reference to the resource on which the service operates | 0..* | CI_Citation | For any single resource referenced, only one of operatedDataset or operatesOn is allowed to be documented (not both for the same resource) |
| Attribute | profile | Profile to which the service adheres | 0..* | CI_Citation | profile of the standard cited in serviceStandard The specification for the data product can be identified here |
| Attribute | serviceStandard | Standard to which the service adheres | 0..* | CI_Citation | For example, citation for OGC WFS, WMS, etc. |
| Role | operatesOn |  | 0..* | MD_DataIdentification | For any single resource referenced, only one of operatedDataset or operatesOn is allowed to be documented (not both for the same resource) |
| (Inherited properties) | (Inherited from MD_Identification.) (not shown) |

PT_Locale

| Role Name | Name | Description | Mult | Type | Remarks |
| --- | --- | --- | --- | --- | --- |
| Class | PT_Locale | Description of a locale | - | - | From ISO 19115-1 |
| Attribute | language | Designation of the locale language | 1 | LanguageCode | ISO 639-2 3-letter language codes. |
| Attribute | country | Designation of the specific country of the locale language | 0..1 | CountryCode | ISO 3166-2 2-letter country codes |
| Attribute | characterEncoding | Designation of the character set to be used to encode the textual value of the locale | 1 | MD_CharacterSetCode | Use (the “Name” from the) IANA Character Set register: http://www.iana.org/assignments/character-sets. (ISO 19115-1 B.3.14) For example, UTF-8 |

The class PT_Locale is defined in ISO 19115-1. LanguageCode, CountryCode, and MD_CharacterSetCode are ISO codelists which should either be defined in resource files and encoded as (string) codes, or represented by the corresponding literals from the namespaces identified in the Remarks column.

# Footnotes

Conformance class 1 as described at Section 2 Conformance and Appendix B.3 Example of a profile with specialisations (ISO 19106:2004).

A profile of a single base standard can include a subset, which is equivalent to the entire base standard. That is, a subset can equal the whole (19106:2005, p15).

This conforms to the rules included at Annex C (ISO 19115-1:2014).

# Comments

From IIC: Since the aim is to develop an independent section covering the S100 exchange sets and exchange set catalogues only these two sections are probably not needed as they are not applicable i.e. S100 exchange set only realizes some of the 19115/19139 concepts and aligns with them in general but it does not conform to them. Similarly, some of the complex data types from other domains are used but this is done very selectively.

These sections are applicable to the classic 19115 metadata records that must be included with each S100 product to ensure interoperability with other geospatial systems. As such they belong in the general metadata section, which should also cover the classic 19115 metadata record requirements for S100 products.

From IIC: Suggest removing #1 as this is not applicable here. Currently the main (and only) option for confirming the conformance is validating against the S-100 XML schemas as outlined in #2.

From IIC: Ideally, the schemas should be available from the IHO site and the location along with some guidence how to use them should be provided in the standard. They should also be live and actively managed for the entire system to function properly. Please see more comprehensive comments about this aspect in IIC Metadata Feedback Report.

From IIC: Suggest removing this section. This might be a good idea but it has not been implemented by any product specification so far to my knowledge. It is best to simply require all product specification authors to ensure their products are distributed with fully conformant S100exchange set catalogues. While it is possible for them to develop a translation from something proprietary to S100 conformant, this possible translation activity should be outside of S100.

From IIC: Suggest overhauling this section. This overview section is a bit of random set of statements inserted at various points in the past that could use a re-write to make it much easier to follow. This would not change the fundamentals but would give implementors a more sensible information to work with. Suggest also including guidelines/best practices covering optimal exchange set structure, handling of support file packaging, optional inclusion of various catalogues. This should also outline the edge cases sending catalogues without data to either cancel some previously released datasets or provide new release of FC for example. Please see more comprehensive comments about this aspect in IIC Metadata Feedback Report.

Suggest also including exchange set and catalogue creation workflow. Currently we have multiple operations that might be executed when producing an exchange set, including creating exchange set folder structure, placing datasets and classic 19115 metadata in their respective folders, adding any required support files and optionally catalogues. At this point the individual files can be digitally signed, the whole exchange set can be compressed and/or encrypted and finally the whole structure can be digitally signed. The order of these operations is currently not prescribed but it is important as, for example, data does not compress much once encrypted. For this reason people frequently wonder if the datasets should be compressed individually and signed before or after that. In my view, the suggested order, for unencrypted exchange sets, should likely be to digitally sign individual files, compress the entire exchange set, and digitally sign the resulting exchange set. The above order of operations seems to be the most optimal for generic data exchange however it requires digital signature for the exchange set catalogue to be added to the model as it is currently not there. The optimal order of operations for an encrypted exchange set will be different as it has to follow its own workflow.

From CCG: This figure shows S100_CatalogueMetadata associated with the S100_ExchangeSet class, while in Figure D4 it is associated with the S100_ExchangeCatalogue class. Moreover, the S100_ExchangeSet class is missing from D4, but present in the tables below. This should be harmonized between the two Figures.

From SMA: Missing details for S100_DigitalSignatureValue. It is not that detailed defined in Part 15 ed 4.

S100_DigitalSignature should allow different size of key/strength. The present strength with 1024bits will/may not be adequate in future.

S100_ProtectionScheme should also include future schemes such as SECOM, but this may be added once SECOM (IEC 63173-2) is released.

From Primar: The agreed upon changes to use fileLocation and not filePath has been implemented in the tables (Elements of the exchange set) for S100_DatasetDiscoveryMetadata, S100_SupportFileDiscoveryMetadata and S100_CatalogueMetadata.

For Figure 4a-D-4 this means filePath must be changed to fileLocation for S100_DatasetDiscoveryMetadata, and not the other way around as stated below in Jeffs comment.

S100_ExchangeCatlogue and S100_DadasetDiscoveryMetadata class attribute lists may need to be amended dependant on decision made in regard to the corresponding Tables below.

S100_ExchangeCatlogue attribute productSpecification requires multiplicity to be amended to [1..*] and S100_SupportFileDiscoveryMetadata and S100_CatalogueMetadata attribute fileLocation needs to be changed to filePath; and attribute matadataPointOfContact requires multiplicity to be amended to [0..1] – refer to proposals associated with Paper S-100WG5-04.09.

S-100_ProductSpecification will need attribute S-100_compliancyCategory added (refer paper s-100WG5-04.16).

From IIC: Will the multi aggregations ever be used? So far we do not really have a valid use case for them so maybe there is no real need for this.

From Furuno: include the class name at other end of associations (role rows) in the tables, like what has been done in Part 3 to remove ambiguity and ease of reading

From IIC: Suggest adding digital signature for the entire exchange set.

From IIC: Suggest adding guidelines for creating them and ensuring that they are unique.

From Furuno: Non-database style products such as S-421 Route plan which is typically exchanged as a single file do not need this at all

From Furuno: Non-database style products such as S-421 Route plan which is typically exchanged as a single file do not need this at all

From Furuno: Should this be removed from this level ?

S100_DatasetDiscoveryMetadata for each Dataset include S100_ProductSpecification

So S100_ProductSpecification at ExchangeCatalogue level is redundant and not needed

If not removed, then at least shall be optional “0..*”

Caris: If used, should be defined like PT_Locale or codelist.

From Furuno: Should be optional

To be used only if non-English

From CCG: Should probably use the PT_Locale type

From KR: Naming convention of Catalogue Name is needed for multi product specifications

From Furuno: No need to repeat the filename inside the the named file

From Furuno: Should be optional

Many eNavigation products do not need this at all

PRIMAR also conured

From PRIMAR: Cannot see the real purpose of this. If justification for keeping it exists, suggest to change type to codelist and define distribution Media encoding options (1. CD, 2. DVD, 3. Internet, 4…….)

From Furuno: Role with undefined name => need drafting of the name

From CCG: Description is identical to S100_ExchangeCatalogue. Should be descriptive of this class.

From CCG: Is this identifier Prod.Spec specific, service specific or should it be standardized at the S-100 level? At a minimum, use guidance is needed.

From Primar: What is the purpose of editioning exchange catalogues? Perhaps sufficient enough to have the identifier and dateTime information to indicate uniqueness if necessary?

Suggest to either remove or explain which value(s) should be used encoding this field

From Furuno: For each separate file included into ExchangeSet S100_DiscoveryExchangeCatalog makes reference to S100_DatasetDiscoveryMetadata

S100_DatasetDiscoveryMetadata makes reference to “fileName” and “fileLocation”

For what purpose do we need this S100_Dataset ?

From CCG: Metadata size is too big. With S-100 Part 11, section 15 ‚stating „The core metadata elements as defined in ISO 19115-1 and S-100 Part 4 (Metadata) shall be included with the data product. Discovery and Quality metadata shall be structured as per S-100 Parts 4a and 4c, respectively.“ It would be helpful to declare explicitly what part of these classes are core metadata. Moreover, the size of the metadata is a significant problem for small datasets like S-124 and S-421, tests show that metadata is twice the size of the dataset on average (assuming 5KB datasets, and 10-12KB metadata)..

Generally, two options seem likely; Either split the S100_DatasetDiscoveryMetadata into a core and an optional class to reduce the size, or allow the small dataset PS to have more metadata inside the dataset. The latter option risk duplicating the issues of current S-63 distribution. E.g. data must be uncompressed and read before it is understood what it is.

There is a risk that the first option also result in metadata that is ‘too big’. A review of core metadata may be necessary in that case.

From KR: Some product specifications have defined means for providing delta changes between new editions. These delta change or update files are not specifically covered by S-100 exchange set metadata model, but several product specifications (S-122, S-123 and S-127) have made special adoption of the S100_DatasetDiscoveryMetadata class for update files.

An abridged discovery metadata would also be benefit  to S-124.

From KR: Suggest making a new data type for external resources. References to external resources are currently CharacterString or Text data types depending on where they are used.

From Furuno: Should be optional

Many eNavigation products do not need this at all

Add remark: Without fileLocation the exchange set is unpacked into directory <S100_ROOT>/<filename>

Should be optional

Many eNavigation products do not need this at all

From Furuno: Should be optional

Many eNavigation products do not need this at al

From Caris: Do we intend to allow any of the possible MD_RestrictionCode values or is it just ‘copyright’?

From KR: S-124, and likely also S-412, makes use of a specialization for cancelling datasets. The question should be analyzed from the perspective of the metadata schema, as there is a potential for having two or more metadata schemas and what this means for exchange sets. S-100 does not currently address the question of multi schema exchange sets, and may need to provide some overall guidance on this.

From KR: Suggest detailed definitions/examples

Each value need a definition to help ensure consistent usage. A seperate clause would be better with more explanation. This new clause could be referenced from remarks. Each product specification can then select the whole list or a subset as applicable for that product

From KR: t may be useful to indicate which ones are intended for navigation. This can be done with designating the MD_USAGE attribute specificUsage with standardized strings such as ‘not for navigation’, ‘for navigation planning’ and ‘for navigation’.

From Caris: This should be of Type Integer otherwise we need to get into string validation. Using Integer type means xsd can easily validate. Must be consistent across product specs to support machine readable S-100

From Caris: This should be of Type Integer otherwise we need to get into string validation. Using Integer type means xsd can easily validate. Must be consistent across product specs to support machine readable S-100

From Furuno: Should be optional

Many eNavigation products do not need this at all

From Furuno: Should be optional

Many eNavigation products do not need this at all

Also proposed Remark.

From Caris: Do we expect ‘Individuals’ to be making official data?

Overlap or duplication of what is in the S100_CataloguePointOfContact and metadataPointOfContact

References a hierarchy of elements, how much is enough?  Some guidance and examples would be good.

From Furuno: Should be optional

Many eNavigation products do not need this at all

From Furuno: Should be optional

Many eNavigation products do not need this at all

From Furuno: Should be optional

Many eNavigation products do not need this at all

From Caris: The description says it is a number but the type is CharacterString. Make it a number type or else define specifically how it should be formatted so that it is consistently used across product specs.

From Caris: How is this supposed to be used? If it is meant for systems to discover and control mandatory backdrops or other operations then it needs to be structured and defined. If it is meant for users what users do we expect will actually see this information and how.

From Caris: Check schema and provided examples for consistency ‘eng’ vs ‘English’ etc.

From Furuno: Should be optional

Many eNavigation products do not need this at all

See remarks also

From CCG: The support for multi language should be reviewed. If there are multiple languages in the dataset, should also the metadata support multi language? If yes, do the CharacterString need re modelling to support multi language?

From IIC: Suggest adding an element for the classic 19115 metadata file location to the main model. Currently the only reference for it is in the figure 4a-D-2 – S-100 Exchange Set Catalogue, which is captured in the schemas as S100_19115DatasetMetadata but it is not covered in the model or text of the standard.

As for the metadataFileIdentifier element this is something from 19115 world we currently do not have a use case for (at the exchange set level) I believe, and unless we have some use for it  I would suggest removing it. Also this is not the same as a reference link to 19115, in contrast to what the note section implies.

From Furuno: Should be optional

Many eNavigation products do not need this at all

From CARIS: Already mentioned above overlap with ProducingAgency and S100_CataloguePointOfContact.
This entails a significant hierarchy under CI_Responsibility which would be good to have more guidance and examples for.  In examples we noticed inconsistencies and variations such as case of CI_RoleCode values ‘Publisher’ vs ‘owner’ etc.

Refer to proposals associated with paper S-100WG5-04.09.  Of teh two options suggested, have opted to make this attribute optional – TBC.

From PRIMAR: Regarding multiplicity, reply to Jeff comment; I believe this reflects the intention of the proposal..

From Furuno: Should be optional

Many eNavigation products do not need this at all

From CCG: Part 4a, Table 4a-1 mentions PT_Locale as the means for expressing language. Sjould be harmonized, and maybe this attribute should be removed.

Need to confirm that this is the cardinality amendment that was identified at S-100WG5 (Refer actions related to S-100WG5-04.07).  Confirm that Remark is OK (email sent to Svein 30/04/20).

From IIC: Suggest refining S100_DataCoverage and its underlying elements and definitions to align with general metadata conventions. As currently modeled a dataset can have 0 or more data coverages, each consisting of 1 bounding box and 1 or more bounding polygon and set of optimum/min/max scales. The same scale elements are also present at the dataset level. Generally there should be one bounding box for the entire dataset. Also it might be optimal to have one polygon per data coverage with one set of scales at the data coverage level (as opposed to dataset level) to remove room for ambiguities. Please see more comprehensive comments about this aspect in IIC Metadata Feedback Report delivered to NOAA.

From IIC: We need digital signature system to be operational so agencies can generate signatures and users are able to verify them etc. Ideally there should also be additional guidance within this section so the users and developers know how to use this sub-system.

From SMA: Propose to allow more variants and key strength. Propose DSA1024, DSA2048

From Furuno: Propose to use Hex

From SMA: Missing all the included attributes.

Propose to include

signatureValue (in HEX)

signedPublicKeyThumbprint

signedRootKeyThumbprint

From IIC: Product specification version is currently a character string. This  makes it challenging to sensibly use it in practice. It might be best to at least change it to a formatted string 6 characters AABBCC where AA, BB, CC are integers representing version, major and minor revisions accordingly. This would not require any changes to schemas etc. Another option would be to create separate elements for each of the above components similar to edition and update numbers. There are a few other placese where version shoudl be adjusted the same way for consistnecy.

From Furuno: Non-standardized free character strings do not facilitate machine readable automation.

If this type remain the attribute has no value and the “Mult” should be changed as “0..1”

From Furuno: Non-standardized free character strings do not facilitate machine readable automation.

If this type remain the attribute has no value and the “Mult” should be changed as “0..1”

From Furuno: The date is just interesting to know. Should be optional

From Caris: Is the name and version not enough, why is this field needed and could these numbers change over time?
Is it possible that a product could exist that is not registered in the IHO GI registry? Such as an unofficial product/dataset. In which case this field would need to be optional.

From Furuno: Is this method already working?

From Caris: Wow (sucking sound as breath stops).

Where to start?  This is a real dogs breakfast. If you want to pick and choose parts of S-100 to be compliant with where does that leave the systems meant to produce/use the data. Essentially if a dataset is not compliant then it will require a separate implementation. What is the value of being model compliant if the encoding is not readable, …

So maybe someone wants to exchange non-S-100 data using the only the S-100 Exchange set structure and meta data.  You would have to do another pass through product spec names, numbers etc because in that case the product spec is not likely registered in IHO.

There will be another rant about the GML spec having been opened up to all kinds of unnecessary random permutations and combinations based on whims of product specs destroying the concept of plug and play S-100. What is the point/value in having custom product specs that only borrow some convenient portions from S-100. They should just be separate things and not live in the same house as S-100.

Products should be S-100 compliant or not, period. Not sort of like S-100, S-100ish etc.

Go make another product, use whatever you want to borrow/copy from S-100 but call it and handle it as something else and don’t expect an S-100 system to support it.

From Caris: If it is a number change the type to Integer so it can be easily validated by xsd. If not an integer then provide explicit format definition.

From Caris: Does the purpose overlap with editionNumber? Perhaps this should be optional.

From Caris: For several of the support file formats this is probably not necessary and should be optional.  What would this structure be filled with when the format is ASCII?

From Caris: This statement in effect means that only one language per support file is allowed. This should probably be explained somewhere else in greater detail.

From Caris: If this is numeric then it should be an integer.

If this is meant to be machine readable information for systems to decide whether it can open the file or not perhaps codelists or something should be used.

If it is meant to be like ‘mp4’ then that is probably redundant with the file extension/type and would be better as a codelist.

From Primar: Change name to S100_CatalogueDiscoveryMetadata?

We have the discovery metadata for datasets and support files defined and named as S100_DatasetDiscoveryMetadata and S100_SupportFileDiscoveryMetadata. As an exchange set also can be used for various catalogue exchange (Feature, Portrayal (Alarms&Indications, Interoperability?), the S100_CatalogueMetadata describes the discovery metadata for such catalogues.

Suggest to  include "Discovery" in naming of this instance.

From KR: Considering Interoperability Catalogue could be combined with exchange set packages of combinations of products from multiple product specifications, perhaps as a set of minimum safe data for entering or leaving a port or constrained waterway. S-100 exchange set model probably supports multi products, but should include more guidance for how to handle this specifically since product specifications would likely focus on itself only.

From KR: A purpose attribute is  necesseary; Support files referenced by datasets are managed via the S100_SupportFileDiscoveryMetadata class. Feature and Portrayal Catalogues are managed via the S100_CatalogueMetadata class. This class does not have a means of updating an old version with a new version.

This guidance need to elaborate on what user systems should do with differenty types of catalogue updates.

From KR: Some product specifications expect updating of feature and/or portrayal and/or interoperability catalogues. Since this function is likely assumed to be identical for all specifications, it may be advisable to define the FC/PC/IC updating process at the S-100 level and include guidance in the product specification template to recommend that product specifications should consider making use of the common methodology.

From CCG: Multiple files and file locations indicate that there need to be some ordered pairing. How will this work with portrayal catalogue consisting of hundreds of files? It it probably best to have one S100_CatalogueMetadata instance per catalogue, and this has impact on packaging of catalogues. Some form of container file is probably needed. It may also have impact on other attribute multiplicities in this class.

From KR: Interoperability Catalogue probably doesn’t fit within the S-100_ProductSpecification attribute. This attribute may therefore need to be optional or conditional.

From CCG: There can be several files, but only one signature?

From CARIS: Should be an integer or defined format string

From CCG: Think there is a need for better guidance in the use of these classes and for this guidance to be formulated in a way that reduces the need for further elaboration in Prod.Specs.