S-100 – Part XX

Discovery Metadata for Information Exchange Catalogues

Page intentionally left blank

Contents

4a-1	Scope	1

4a-2	Conformance	1

4a-2.1	Conformance of this Profile with other Standards	1

4a-2.2	Backward compatibility	2

4a-3	Conformance to this Profile	2

4a-4	Normative references	2

4a-4.1	Profile definition	2

4a-4.2	Informative references	2

4a-5	Requirements	3

4a-5.1	Business purpose and Intended use	3

4a-5.2	Metadata for describing geographic data and other resources	4

4a-5.3	Obligations/conditions	5

4a-5.4	Minimum metadata requirements	5

4a-5.5	S-100 compliancy categories	11

4a-5.6	Recommended metadata for geographic datasets	11

4a-5.7	Variations and preferences	14

4a-5.7.1	Metadata element metadataIdentifier	14

4a-5.7.2	Metadata element parentMetadata	14

4a-5.7.3	Geographic extent of the dataset	14

4a-5.7.4	Data and Date Time information	14

4a-5.7.5	Metadata extension information	15

4a-5.8	Metadata for services	16

Appendix 4a-A  Metadata Schema Class Information	19

Appendix 4a-B  Data Dictionary	21

Appendix 4a-C  Metadata Implementation	23

Appendix 4a-D  Discovery Metadata for Information Exchange Catalogues	25

Appendix 4a-E  Metadata Extensions	45

Page intentionally left blank

# Scope

The S-100 Discovery Metadata for Information Exchange Catalogues profile described in  this part provides a specification for describing and creating exchange catalogues that enables users to identify, discover and manage content of the S-100 exchange sets.  More importantly it leverages XML to allow machine to machine discovery and exchange of information about about geographic datasets commonly produced by hydrographic organizations. Its purpose is the creation of metadata records that provide information about the identification, spatial and temporal extent, quality, application schema, spatial reference system, and distribution of digital geographic data. It is applicable to the cataloguing of datasets, clearinghouse activities, and the full description of geographic and non-geographic resources.

For information exchange, there are several categories of metadata required: metadata about the overall exchange catalogue, metadata about each of the datasets contained in the catalogue, and metadata about the support files that make up the package. If the exchange catalogue contains any Feature, Portrayal or Interoperability Catalogues there is a provision to carry additional metadata about those.

This document is intended for developers and implementers of metadata applications, and provides a basic understanding of the principles and the overall requirements for standardisation of geographic information. It should be used in conjunction with the standards listed under clause 4a-4 – Normative references.

# Conformance

## Conformance of this Profile with other Standards

The S-100 Discovery Metadata for Information Exchange Catalogues profile adopts data types defined in other ISO standards, mainly in ISO 19115 Geographic information - Metadata and ISO 19136 Geographic Information - Geography Markup Language, along with their underlying obligations and conditions. The XML schema references related to these external data types are embedded in the XML schemas for this profile, thus ensuring the conformance of this profile with other standards during authoring and validation of XML catalogue instances.

## Conformance to this Profile

The conformance to this profile can be confirmed by validating XML catalogue instances against the S-100 Metadata Profile schemas which are available from the IHO S-100 repository.

# Normative references

The following referenced documents are required for the application of this document. For dated references, only the edition cited applies. For undated references, the latest edition of the referenced document (including amendments) applies.

## Profile definition

The following documents were the references used to define the S-100 Metadata Profile:

ISO 19115-1:2014, Geographic information – Metadata – Part 1 - Fundamentals

ISO 19115-1/Amdt01:2018, Geographic information – Metadata – Part 1 - Fundamentals (Amendment 1)

ISO 19115-2:2009, Geographic information - Metadata - Part 2: Extensions for imagery and gridded data

ISO 19119:2016, Geographic information – Services

ISO/TS 19115-3:2016, Geographic information - Metadata - XML schema implementation for fundamental concepts

## Informative references

ISO 19115:2003, Geographic information – Metadata

ISO 19115:2003/Cor.1:2006, Geographic information - Metadata (Technical Corrigendum 1)

ISO/TS 19139:2007, Geographic information - Metadata - XML schema implementation

# Overview

## S-100 Exchange Set Structure

The S-100 Exchange Set is a data container that provides all the elements needed for a reliable and secure exchange of S-100 conformant data. It is intended to be a self-contained entity consisting of data files and metadata records packaged together using applicable data integrity and optional security provisions. The overall concept of the S-100 Exchange Set is a realization of the ISO 19115-3 classes, which fundamentally underpin the interchange of geospatial data and relevant metadata, as depicted in figure 4a-D-1.

Figure 4a-D-1 Realization of the Exchange Set Classes

The above diagram illustrates the conceptual correspondence between data exchange provisions in ISO-19115 and S-100 standards. At an implementation level, the S-100 Exchange Set may include a combination of S-100 datasets, support files, and catalogue files along with the metadata information for all such resources in the form of the S-100 Exchange Set Catalogue. Conceptually this leads to the more detailed model, as shown in figure 4a-D-2.

Figure 4a-D-2 – S-100 Exchange Set

The conceptual model depicted in Figure 4a-D-2 is very flexible and can be implemented in a variety of ways as virtually all components, except for the S-100_ExchangeCatalogue, are optional. This level of flexibility is essential to properly support the mainstream use case of exchanging geospatial data, as well as the use cases for releasing dataset cancellation notices or new catalogue releases without any data files present.

This approach ensures that an exchange set catalogue is always included in any S-100 conformant exchange set, providing the essential discovery metadata about any included resources and their intended use.

Preparation of an exchange set consists of packaging its components using a predefined file folder structure shown in figure 4a-D-3.

S-100 Exchange Set Folder Structure.

Figure 4a-D-3 – An S-100 Exchange Set Folder Structure

- An S-100 exchange set must contain an exchange set catalogue, CATALOG.XML, its digital signature CATALOG.SIGN and may contain any number of S-100 conformant dataset files, support files and catalogue files.

- All S-100 content must be placed inside a top root folder named S100_ROOT. This is the only top level root folder in an exchange set containing only S-100 products.

- The S100_ROOT folder must contain a subfolder for each specific S-100 product specification data type included in the exchange set, e.g. S-101, S-104, S-102 (names defined in the IHO product specification register). These subfolders hold S-100 content specific to an individual product specification, all other exchange set files must be located in the S100_ROOT folder.

- Each product subfolder must contain subfolders for the component dataset files (DATASET_FILES), support files (SUPPORT_FILES) and catalogues (CATALOGUES) as required.

- Individual data files, such as base dataset, update files or detailed ISO 19115 metadata may be optionally placed in their own subfolders or grouped together.

- Support files, on the other hand, may be grouped together in one folder to prevent duplication across multiple dataset folders. Similarly, when needed, an exchange set may carry additional catalogues and/or their different versions which should also be grouped together in one folder.

- The required exchange set catalogue XML document instance must be named CATALOG.XML and placed at the root level alongside the S100_ROOT folder, together with its digital signature (CATALOG.SIGN) file. All other digital signatures are included within their corresponding resource metadata records in the CATALOG.XML.

An S-100 exchange set can be optionally defined alongside S-57 datasets with their own ENC_ROOT and INFO root folders as required by the S-57 ENC product specification. In this case there are three top level folders: ENC_ROOT and INFO for S-57, and S100_ROOT with two separate catalogues covering their respective content (CATALOG.031 and CATALOG.XML). Figure 4a-D-4 shows one of these use cases with S-57 and multiple S-100 products included..

Figure 4a-D-4 – Combined S-100 and S-57 Exchange Sets Folder Structure

In addition to the folder structure, it is important to align the exchange set creation workflow with the data integrity and security provisions outlined in S-100 Part 15. These provisions cover digital signing, compression, and encryption of exchange set resources. All resources within an S-100 Exchange Set must be digitally signed and their signatures included in the exchange set catalogue. Data compression and encryption are optional operations.

Exchange set creation, therefore, consists of:

- The creation of a suitable exchange set folder structure

- The arrangement of all resources in their designated folders.

- Creation of digital signatures for all resources

- Optional compression and encryption of any resources which require it.

- Construction of an Exchange Set Catalogue which records the structure created.

S-100 Part 15 defines the requirements and process for creation and verification of digital signature values and production of compressed/encrypted datasets.

## S-100 Exchange Set Catalogue

The S100 Exchange Set Catalogue is an XML document instance, which provides the metadata information needed to discover and use the resources contained in the S-100 Exchange Set. It must be named CATALOG.XML. This mandatory, central component of S-100 exchange sets consists of several components which capture suitable metadata records for each resource type. These components cover metadata for the exchange set catalogue, dataset discovery, support file discovery, any references to ISO 19115 dataset metadata, and additional catalogues as depicted in figure Figure 4a-D-4.

Figure 4a-D-4 – S-100 Exchange Set Catalogue

The discovery metadata subsections have attributes which enable important information about the datasets and accompanying support files to be examined without the need to process the data, for example encryption/compression flags.  Similarly, other catalogues can be included in the S-100 Exchange Set, in support of the datasets, such as feature, portrayal, coordinate reference systems, codelists etc. Additionally, the S100 Exchange Set Catalogue provides mechanisms for managing the life cycle of datasets and support files. For example, the S-100 Support File Purpose enumeration within support file metadata provides revision control for support files.

More detailed information about the various elements of the catalogue is shown in Figure 4a-D-5 and in the textual description in the tables at clause 3.

Figure 4a-D-5 – S-100 Exchange Set Catalogue - class details

Page intentionally left blank

###### Elements of the exchange set

S100_ExchangeCatalogue

Each exchange set has a single S100_ExchangeCatalogue which contains meta information for the data and support files in the exchange set.

| Role Name | Name | Description | Mult | Type | Remarks |
| --- | --- | --- | --- | --- | --- |
| Class | S100_ExchangeCatalogue | An exchange catalogue contains the discovery metadata about the exchange datasets and support files | - | - | - |
| Attribute | identifier | Uniquely identifies this exchange catalogue | 0..1 | S100_CatalogueIdentifier |  |
| Attribute | contact | Details about the issuer of this exchange catalogue | 0..1 | S100_CataloguePointOfContact |  |
| Attribute | productSpecification | Details about the product specifications used for the datasets contained in the exchange catalogue | 0..* | S100_ProductSpecification |  |
| Attribute | metadataLanguage | Details about the Language | 0..1 | PT_Locale | Default without this is English |
| Attribute | exchangeCatalogueDescription | Description of what the exchange catalogue contains | 0..1 | CharacterString |  |
| Attribute | exchangeCatalogueComment | Any additional Information | 0..1 | CharacterString |  |
| Attribute | exchangeCatalogueCertificate | Signed public key certificates referred to by digital signatures in the exchange set | 0..* | exchangeCatalogueType | Content defined in S-100 Part 15. All certificates used, except the SA root certificate (installed separately by the implementing system) shall be included. |
| Role | datasetDiscoveryMetadata | Exchange catalogues may include or reference discovery metadata for the datasets in the exchange set | 0..* | Aggregation S100_DatasetDiscoveryMetadata |  |
| Role | catalogueDiscoveryMetadata-- | Metadata for catalogue | 0..* | Aggregation S100_CatalogueDiscoveryMetadata | Metadata for the feature, portrayal, and interoperability catalogues, if any |
| Role | supportFileDiscoveryMetadata | Exchange catalogues may include or reference discovery metadata for the support files in the exchange set | 0..* | Aggregation S100_SupportFileDiscoveryMetadata |  |

S100_ExchangeCatalogueIdentifier

| Role Name | Name | Description | Mult | Type | Remarks |
| --- | --- | --- | --- | --- | --- |
| Class | S100_ExchangeCatalogueIdentifier | An exchange catalogue contains the discovery metadata about the exchange datasets and support files | - | - | The concatenation of identifier, editionNumber and dateTime form the unique name |
| Attribute | identifier |  | 1 | CharacterString | Uniquely identifies this exchange catalogue <S100XC:identifier>US_101_20200101_120101_01</S100XC:identifier> |
| Attribute | dateTime | Creation date and time of the exchange catalogue, including time zone | 1 | DateTime | Format: yyyymmddThhmmssZ |

S100_CataloguePointofContact

| Role Name | Name | Description | Mult | Type | Remarks |
| --- | --- | --- | --- | --- | --- |
| Class | S100_CataloguePointOfContact | Contact details of the issuer of this exchange catalogue | - | - | - |
| Attribute | organization | The organization distributing this exchange catalogue | 1 | CharacterString | This could be an individual producer, value added reseller, etc. |
| Attribute | phone | The phone number of the organization | 0..1 | CI_Telephone |  |
| Attribute | address | The address of the organization | 0..1 | CI_Address |  |

S100_ ExchangeCatalogueCertificateType

| Role Name | Name | Description | Code | Remarks | Data |
| --- | --- | --- | --- | --- | --- |
| Enumeration | S100_ExchangeCatalogueCertificateType | Certificate for digital signature | - | - |  |
| Attribute | id | The data server id | - |  | e.g. “UKHO”, “PRIMAR” |
| Attribute | signedPublicKey | The data server’s public key | 1 | CharacterString |  |

S100_DatasetDiscoveryMetadata

| Role Name | Name | Description | Mult | Type | Remarks |
| --- | --- | --- | --- | --- | --- |
| Class | S100_DatasetDiscoveryMetadata | Metadata about the individual datasets in the exchange catalogue | - | - | - |
| Attribute | fileName | Dataset file name | 1 | CharacterString |  |
| Attribute | fileLocation | Full location from the exchange set root directory | 0..1 | S100_FileLocation | Without fileLocation the exchange set is unpacked into directory <ROOT>/S100_ROOT/DATASET_FILES/<fileName> |
| Attribute | description | Short description giving the area or location covered by the dataset | 0..1 | CharacterString | For example, a harbour or port name, between two named locations etc. |
| Attribute | compressionFlag | Is the data compressed | 0..1 | Boolean | Yes or No |
| Attribute | dataProtection | Indicates if the data is encrypted | 0..1 | Boolean | 0 indicates an unencrypted dataset 1 indicates an encrypted dataset |
| Attribute | protectionScheme | Specification or method used for data protection | 0..1 | S100_ProtectionScheme | For example S-63 |
| Attribute | digitalSignatureReference | Digital Signature of the file | 1 | S100_DigitalSignature | Specifies the algorithm used to compute digitalSignatureValue |
| Attribute | digitalSignatureValue | Value derived from the digital signature | 1..* | S100_DigitalSignatureValue | The value resulting from application of digitalSignatureReference Implemented as the digital signature format specified in Part 15 |
| Attribute | copyright | Indicates if the dataset is copyrighted | 0..1 | Boolean |  |
| Attribute | classification | Indicates the security classification of the dataset | 0..1 | Class MD_SecurityConstraints>MD_ClassificationCode (codelist) | 1. unclassified 2. restricted 3. confidential 4. secret 5. top secret 6. sensitive but unclassified 7. for official use only 8. protected 9. limited distribution |
| Attribute | purpose | The purpose for which the dataset has been issued | 0..* | S100_Purpose (codelist) |  |
| Attribute | specificUsage | The use for which the dataset is intended | 0..1 | MD_USAGE>specificUsage (character string) | For example, in the case of ENCs this would be a Navigational Purpose classification. This is strictly for discovery catalogue purposes |
| Attribute | editionNumber | The edition number of the dataset | 0..1 | Integer | When a data set is initially created, the edition number 1 is assigned to it. The edition number is increased by 1 at each new edition. Edition number remains the same for a re-issue. |
| Attribute | updateNumber | Update number assigned to the dataset and increased by one for each subsequent update | 0..1 | Integer | Update number 0 is assigned to a new dataset |
| Attribute | updateApplicationDate | This date is only used for the base cell files (that is new data set, re-issue and new edition), not update cell files. All updates dated on or before this date must have been applied by the producer | 0..1 | Date |  |
| Attribute | issueDate | Date on which the data was made available by the data producer | 1 | Date |  |
| Attribute | issueTime | Time of day at which the data was made available by the data producer | 0..1 | Time | The S-100 datatype Time |
| Attribute | boundingBox | The extent of the dataset limits | 0..1 | EX_GeographicBoundingBox | - |
| Attribute | productSpecification | The product specification used to create this dataset | 1 | S100_ProductSpecification |  |
| Attribute | producingAgency | Agency responsible for producing the data | 1 | CI_Responsibility>CI_Organisation | See Tables 4a-2 |
| Attribute | horizontalDatumReference | Reference to the register from which the horizontal datum value is taken | 1 | characterString | For example, EPSG |
| Attribute | horizontalDatumValue | Horizontal Datum of the entire dataset | 1 | Integer | For example, 4326 |
| Attribute | epoch | Code denoting the epoch of the geodetic datum used by the CRS | 0..1 | CharacterString | For example, G1762 for the 2013-10-16 realization of the geodetic datum for WGS84 |
| Attribute | verticalDatum | Vertical Datum of the entire dataset | 0..1 | S100_VerticalAndSoundingDatum |  |
| Attribute | soundingDatum | Sounding Datum of the entire dataset | 0..1 | S100_VerticalAndSoundingDatum |  |
| Attribute | encodingFormat | The encoding format of the dataset | 1 | S100_EncodingFormat |  |
| Attribute | dataCoverage | Provides information about data coverages within the dataset | 0..* | S100_DataCoverage |  |
| Attribute | comment | Any additional information | 0..1 | CharacterString |  |
| Attribute | defaultLocale | Default language and character set used in the dataset | 0..1 | PT_Locale | In absence of defaultLocale the language is English |
| Attribute | otherLocale | Other languages and character sets used in the dataset | 0..* | PT_Locale |  |
| Attribute | metadataPointOfContact | Point of contact for metadata | 0..1 | CI_Responsibility>CI_Individual or CI_Responsibility>CI_Organisation | Only if metadataPointOfContact is different to producingAgency |
| Attribute | metadataDateStamp | Date stamp for metadata | 0..1 | Date | May or may not be the issue date |
| Attribute | replacedData | If a data file is cancelled is it replaced by another data file | 0..1 | Boolean |  |
| Attribute | dataReplacement | Cell name | 0..* | CharacterString | A dataset may be replaced by 1 or more datasets |
| Role | -- | Containment of, or reference to, discovery metadata for the support files referenced in the dataset | 0..* | Aggregation S100_SupportFileDiscoveryMetadata |  |

S100_DataCoverage

| Role Name | Name | Description | Mult | Type | Remarks |
| --- | --- | --- | --- | --- | --- |
| Class | S100_DataCoverage | A spatial extent where data is provided; and the display scale information for the provided data | - | - | This field is used by user systems as part of the data loading and unloading algorithms and it is strongly encouraged that product specifications mandate the use of one or more of the displayScale provided as part of S100_DataCoverage |
| Attribute | ID | Uniquely identifies the coverage | 1 | Integer | - |
| Attribute | boundingPolygon | A polygon which defines the actual data limit | 1..1 | EX_BoundingPolygon |  |
| Attribute | optimumDisplayScale | The scale with which the data is optimally displayed | 0..1 | Integer | Example: A scale of 1:25000 is encoded as 25000 |
| Attribute | maximumDisplayScale | The maximum scale with which the data is displayed | 0..1 | Integer |  |
| Attribute | minimumDisplayScale | The minimum scale with which the data is displayed | 0..1 | Integer |  |

S100_DigitalSignature

| Role Name | Name | Description | Code | Remarks |
| --- | --- | --- | --- | --- |
| Enumeration | S100_DigitalSignature | Algorithm used to compute the digital signature | - | - |
| Value | dsa | Digital Signature Algorithm | - | FIPS 186-4 (2013) |

S100_DigitalSignatureValue

| Role Name | Name | Description | Mult | Type | Remarks |
| --- | --- | --- | --- | --- | --- |
| Class | S100_DigitalSignatureValue | Signed Public Key plus the digital signature | - | - | Data type for encoding digital signature values |
| Attribute | dataServerCertificate | Data Server Certificate as defined in S-100 Part 15 | 0..1 | CharacterString | A certificate will be encoded in PEM format as a character string as defined in S-100 Part 15. Optional. digitalSignature can use ref to refer to certificates defined in S100_ExchangeCatalogue to avoid repetition. |
| Attribute | digitalSignature | Digital signature as defined in S-100 Part 15 | 1 | CharacterString | A digital signature will be in ASN.1 in base64 and encoded as a character string as defined in S-100 Part 15. |

S100_FileLocation

| Role Name | Name | Description | Mult | Type | Remarks |
| --- | --- | --- | --- | --- | --- |
| Class | S100_FileLocation | Full location relative to the exchange set root directory |  | - | - |
| Attribute | fileName | Name of the dataset file | 1 | CharacterString |  |
| Attribute | filePath | Path Relative to the root directory | 1 | CharacterString | Path relative to the root directory of the exchange set. The location of the file after the exchange set is unpacked into directory <ROOT> will be <ROOT>/<fileLocation>/<fileName>. If fileLocation is undefined the file is located in the appropriate directory as per the folder structure defined in 4a-4.2 |

S100_Purpose

| Role Name | Name | Description | Code | Remarks |
| --- | --- | --- | --- | --- |
| Enumeration | S100_Purpose | The Purpose of the Dataset | - |  |
| Value | New dataset | Brand New dataset | - | - |
| Value | New Edition | New edition of the dataset | - | - |
| Value | Update | Dataset update |  | - |
| Value | reissue | Dataset that has been re-issued | - |  |
| Value | cancellation | Dataset that has been cancelled |  |  |
| Value | delta | Dataset difference |  |  |
| Value | navigation | Dataset Intended for navigation |  |  |
| Value | notForNavigation | Dataset not intended for navigation |  |  |

S100_VerticalAndSoundingDatum

| Role Name | Name | Description | Code | Remarks |
| --- | --- | --- | --- | --- |
| Enumeration | S100_VerticalAndSoundingDatum | Allowable vertical and sounding datums | - | - |
| Value | meanLowWaterSprings |  | 1 | (MLWS) |
| Value | meanLowerLowWaterSprings |  | 2 | - |
| Value | meanSeaLevel |  | 3 | (MSL) |
| Value | lowestLowWater |  | 4 | - |
| Value | meanLowWater |  | 5 | (MLW) |
| Value | lowestLowWaterSprings |  | 6 | - |
| Value | approximateMeanLowWaterSprings |  | 7 | - |
| Value | indianSpringLowWater |  | 8 | - |
| Value | lowWaterSprings |  | 9 | - |
| Value | approximateLowestAstronomicalTide |  | 10 | - |
| Value | nearlyLowestLowWater |  | 11 | - |
| Value | meanLowerLowWater |  | 12 | (MLLW) |
| Value | lowWater |  | 13 | (LW) |
| Value | approximateMeanLowWater |  | 14 | - |
| Value | approximateMeanLowerLowWater |  | 15 | - |
| Value | meanHighWater |  | 16 | (MHW) |
| Value | meanHighWaterSprings |  | 17 | (MHWS) |
| Value | highWater |  | 18 | (HW) |
| Value | approximateMeanSeaLevel |  | 19 | - |
| Value | highWaterSprings |  | 20 | - |
| Value | meanHigherHighWater |  | 21 | (MHHW) |
| Value | equinoctialSpringLowWater |  | 22 | - |
| Value | lowestAstronomicalTide |  | 23 | (LAT) |
| Value | localDatum |  | 24 | - |
| Value | internationalGreatLakesDatum1985 |  | 25 | - |
| Value | meanWaterLevel |  | 26 | - |
| Value | lowerLowWaterLargeTide |  | 27 | - |
| Value | higherHighWaterLargeTide |  | 28 | - |
| Value | nearlyHighestHighWater |  | 29 | - |
| Value | highestAstronomicalTide |  | 30 | (HAT) |
| Value | ITRF2014 | International Terrestrial Reference Frame 2014 | 31 |  |
| Value | ITRF2020 | International Terrestrial Reference Frame 2020 | 32 |  |
| Value | ellipsoidalHeightGeneric |  | 33 |  |
| Value | balticSeaChartDatum2000 |  | 34 |  |
| Value | geoidGeneric |  | 35 |  |
| Value | internationalGreatLakesDatum2020 |  | 36 |  |
| Value | seaSurface |  | 37 | Local sea bottom |
| Value | seaBottom |  | 38 | Local sea bottom reference |

Note: The numeric codes are the codes specified in the IHO GI Registry for the equivalent listed values of the IHO Hydro domain attribute Vertical datum, since the registry does not at present (20 June 2018) contain entries for exchange set metadata and dataset metadata attributes.

S100_EncodingFormat

| Role Name | Name | Description | Code | Remarks |
| --- | --- | --- | --- | --- |
| Enumeration | S100_DataFormat | The encoding format | - | - |
| Value | ISO/IEC 8211 | The ISO 8211 data format as defined in Part 10a | - | - |
| Value | GML | The GML data format as defined in Part 10b | - | - |
| Value | HDF5 | The HDF5 data format as defined in Part 10c |  | - |
| Value | undefined | The encoding is defined in the Product Specification | - | Use product specification specific encoding means the data product and product specification is not intended for an IHO S-100 compliant system. |

S100_ProductSpecification

| Role Name | Name | Description | Mult | Type | Remarks |
| --- | --- | --- | --- | --- | --- |
| Class | S100_ProductSpecification | The Product Specification contains the information needed to build the specified product | - | - | - |
| Attribute | name | The name of the product specification used to create the datasets | 0..1 | CharacterString | The name in the GI Registry should be used for this field |
| Attribute | version | The version number of the Product Specification | 0..1 | CharacterString | TR 2/2007 specifies versioning of product specifications. |
| Attribute | date | The version date of the product specification | 0..1 | Date |  |
| Attribute | number | The number used to lookup the product in the Product Specification Register of the IHO GI registry | 0..1 | Integer | From the Product Specification Register, in the IHO Geospatial Information Registry |
| Attribute | compliancyCategory | The level of compliance of the Product Specification to S-100 | 0..1 | S100_CompliancyCategory | See clause Part 4a-5.5 |

S100_CompliancyCategory

| Role Name | Name | Description | Code | Remarks |
| --- | --- | --- | --- | --- |
| Enumeration | S100_CompliancyCategory |  | - | - |
| Value | category1 | IHO S-100 object model compliant |  |  |
| Value | category2 | IHO S-100 compliant with non-standard encoding |  |  |
| Value | category3 | IHO S-100 compliant with standard encoding |  |  |
| Value | category4 | IHO S-100 and IMO harmonized display compliant |  |  |

S100_ProtectionScheme

| Role Name | Name | Description | Code | Remarks |
| --- | --- | --- | --- | --- |
| Enumeration | S100_ProtectionScheme | Data protection schemes | - | - |
| Value | S100p15 | IHO S-100 Part 15 | - | See Part 15 |

S100_SupportFile

| Role Name | Name | Description | Mult | Type | Remarks |
| --- | --- | --- | --- | --- | --- |
| Class | S100_SupportFile |  | - | - | - |
| Role | aggregateFile | Collection of support files | 0..* | - |  |
| Role | supportFile | File which has information about a dataset | 0..* | - |  |

S100_SupportFileDiscoveryMetadata

| Role Name | Name | Description | Mult | Type | Remarks |
| --- | --- | --- | --- | --- | --- |
| Class | S100_SupportFileDiscoveryMetadata | Metadata about the individual support files in the exchange catalogue | - | - | - |
| Attribute | fileName | Name of the support file | 1 | CharacterString |  |
| Attribute | fileLocation | Full location from the exchange set root directory | 1 | CharacterString | Path relative to the root directory of the exchange set. The location of the file after the exchange set is unpacked into a directory <ROOT> will be <ROOT>/S100_ROOT/<fileLocation>/<filename>. If fileLocation is undefined the file is located in <ROOT>/S100_ROOT/SUPPORT_FILES/fileName |
| Attribute | purpose | The purpose for which the support file has been issued | 1 | S100_SupportFilePurpose | For example new, re-issue, new edition, update etc. |
| Attribute | editionNumber | The edition number of the support file | 1 | Integer | When a data set is initially created, the edition number 1 is assigned to it. The edition number is increased by 1 at each new edition. Edition number remains the same for a re-issue |
| Attribute | issueDate | Date on which the data was made available by the data producer | 0..1 | Date |  |
| Attribute | supportFileSpecification | The specification used to create this file | 0..1 | S100_SupportFileSpecification |  |
| Attribute | dataType | The format of the support file | 1 | S100_SupportFileFormat |  |
| Attribute | otherDataTypeDescription | Support file format other than those listed | 0..1 | CharacterString |  |
| Attribute | comment | Optional comment | 0..1 | CharacterString |  |
| Attribute | compressionFlag | Is the data compressed | 0..1 | Boolean | Yes or No |
| Attribute | digitalSignatureReference | Digital Signature of the file | 0..1 | CharacterString | Reference to the appropriate digital signature algorithm |
| Attribute | digitalSignatureValue | Value derived from the digital signature | 1..* | S100_DigitalSignatureValue | The value resulting from application of digitalSignatureReference Implemented as the digital signature format specified in Part 15 |
| Attribute | defaultLocale | Default language and character set used in the exchange catalogue | 0..1 | PT_Locale | A support file is expected to use only one locale, because other files can be created for other languages |

S100_SupportFileFormat

| Role Name | Name | Description | Code | Remarks |
| --- | --- | --- | --- | --- |
| Enumeration | S100_SupportFileFormat | The format used for the support file | - | - |
| Value | ASCII | UTF-8 text excluding control codes | - | Many files use UTF-8 |
| Value | JPEG2000 | JPEG2000 format | - | ISO 15444 |
| Value | HTML | Hypertext Markup Language | - |  |
| Value | XML | Extensible Markup Language | - |  |
| Value | XSLT | Extensible Stylesheet Language Transformations | - |  |
| Value | VIDEO | Representation of moving images in unspecified format | - |  |
| Value | TIFF | Tagged Image File Format | - |  |
| Value | PDF/A or UA | Portable Document Format | - | ISO 19005, ISO 32000 Product Specification developers should take careful consideration in using PDF as a support file format. It is recommended that PDF never be used in products that will be used on a navigation system as it may impair night vision |
| Value | LUA | Lua programming language | - |  |
| Value | other | Other format | - |  |

S100_SupportFilePurpose

| Role Name | Name | Description | Code | Remarks |
| --- | --- | --- | --- | --- |
| Enumeration | S100_SupportFilePurpose | The reason for inclusion of the support file in this exchange set | - | - |
| Value | new | A file which is new | - | Signifies a new file |
| Value | replacement | A file which replaces an existing file | - | Signifies a replacement for a file of the same name |
| Value | deletion | Deletes an existing file | - | Signifies deletion of a file of that name |

S100_SupportFileSpecification

| Role Name | Name | Description | Mult | Type | Remarks |
| --- | --- | --- | --- | --- | --- |
| Class | S100_SupportFileSpecification | The standard or specification to which a support file conforms | - | - | - |
| Attribute | name | The name of the specification used to create the support file | 1 | CharacterString |  |
| Attribute | version | The version number of the specification | 0..1 | CharacterString |  |
| Attribute | date | The version date of the specification | 0..1 | Date |  |

S100_CatalogueDiscoveryMetadata

| Role Name | Name | Description | Mult | Type | Remarks |
| --- | --- | --- | --- | --- | --- |
| Class | S100_CatalogueDiscoveryMetadata | Class for S-100 catalogue metadata | - | - | - |
| Attribute | fileName | The name for the catalogue | 1 | S100_FIleName |  |
| Attribute | purpose | The purpose for which the dataset has been issued | 0..1 | S100_Purpose (codelist) | 2. new edition 5. cancellation Default is value 2:new edition |
| Attribute | fileLocation | Full location from the exchange set root directory | 1 | CharacterString | Path relative to the root directory of the exchange set. The location of the file after the exchange set is located in a directory <ROOT> will be <ROOT>/<fileLocation>/<fileName> If fileLocation is undefined then the file will be located in <ROOT>/S100_ROOT/CATALOGUES/<fileName> |
| Attribute | scope | Subject domain of the catalogue | 1 | S100_CatalogueScope |  |
| Attribute | versionNumber | The version number of the product specification | 1 | CharacterString |  |
| Attribute | issueDate | The version date of the product specification | 1 | Date |  |
| Attribute | productSpecification | The product specification used to create this file | 0..1 | S100_ProductSpecification |  |
| Attribute | digitalSignatureReference | Digital Signature of the file | 1 | S100_DigitalSignature | Reference to the appropriate digital signature algorithm |
| Attribute | digitalSignatureValue | Value derived from the digital signature | 1..* | S100_DigitalSignatureValue | The value resulting from application of digitalSignatureReference Implemented as the digital signature format specified in Part 15 |
| Attribute | defaultLocale | Default language and character set used in the exchange catalogue | 1 | PT_Locale |  |
| Attribute | otherLocale | Other languages and character sets used in the exchange catalogue | 0..* | PT_Locale |  |

S100_CatalogueScope

| Role Name | Name | Description | Code | Remarks |
| --- | --- | --- | --- | --- |
| Enumeration | S100_CatalogueScope | The scope of the catalogue | - | - |
| Value | featureCatalogue | S-100 feature catalogue |  |  |
| Value | portrayalCatalogue | S-100 portrayal catalogue |  |  |
| Value | interoperabilityCatalogue | S-100 interoperability information |  |  |

S100_SV_ServiceIdentification

| Role Name | Name | Description | Mult | Type | Remarks |
| --- | --- | --- | --- | --- | --- |
| Class | S100_SV_ServiceIdentitification | Identification of capabilities which a service provider makes available to a service user through a set of interfaces which define a behaviour | - | - | Specialization of SV_ServiceIdentification (ISO 19115-1) and thereby a specialization of MD_Identification (The ISO attributes coupledResource and couplingType are not used.) |
| (Inherited properties) | (Inherited from SV_ServiceIdentification.) |
| Attribute | serviceType | A service type name | 1 | Class GenericName | GenericName is an abstract class for all names in a NameSpace. Each instance of a GenericName is either a LocalName or a ScopedName. A LocalName references a local object directly accessible from the NameSpace. A ScopedName is a composite of a LocalName for locating another NameSpace and a GenericName valid in the NameSpace. (ISO 19103). In short: A name that is defined in a namespace. For S-100 services, the recommended namespace is the IALA/IMO/IHO list of Maritime Services (TBD as of May 2018) |
| Attribute | serviceTypeVersion | The version of the service, supports searching based on the version of serviceType | 0..* | CharacterString |  |
| Attribute | accessProperties | Information about the availability of the service, including fees, planned available date and time, ordering instructions, turnaround | 0..1 | MD_StandardOrderProcess | ISO 19115-1 B.11.5 |
| Attribute | operatedDataset | Provides a reference to the resource on which the service operates | 0..* | CI_Citation | For any single resource referenced, only one of operatedDataset or operatesOn is allowed to be documented (not both for the same resource) |
| Attribute | profile | Profile to which the service adheres | 0..* | CI_Citation | profile of the standard cited in serviceStandard The specification for the data product can be identified here |
| Attribute | serviceStandard | Standard to which the service adheres | 0..* | CI_Citation | For example, citation for OGC WFS, WMS, etc. |
| Role | operatesOn |  | 0..* | MD_DataIdentification | For any single resource referenced, only one of operatedDataset or operatesOn is allowed to be documented (not both for the same resource) |
| (Inherited properties) | (Inherited from MD_Identification.) (not shown) |

PT_Locale

| Role Name | Name | Description | Mult | Type | Remarks |
| --- | --- | --- | --- | --- | --- |
| Class | PT_Locale | Description of a locale | - | - | From ISO 19115-1 |
| Attribute | language | Designation of the locale language | 1 | LanguageCode | ISO 639-2 3-letter language codes. |
| Attribute | country | Designation of the specific country of the locale language | 0..1 | CountryCode | ISO 3166-2 2-letter country codes |
| Attribute | characterEncoding | Designation of the character set to be used to encode the textual value of the locale | 1 | MD_CharacterSetCode | Use (the “Name” from the) IANA Character Set register: http://www.iana.org/assignments/character-sets. (ISO 19115-1 B.3.14) For example, UTF-8 |

The class PT_Locale is defined in ISO 19115-1. LanguageCode, CountryCode, and MD_CharacterSetCode are ISO codelists which should either be defined in resource files and encoded as (string) codes, or represented by the corresponding literals from the namespaces identified in the Remarks column.

XML encoding example:
See April2020\S100 Edition 4.0.0 Schemas_FINAL\samples\S101\1.0.0\CATALOG.XML

<lan:PT_Locale>

<lan:language>

<lan:LanguageCode codeList="http://www.iho.int/S100/4.0.0/resources/Codelists/cat/codelists.xml#S100_MD_LanguageCode" codeListValue="eng">English</lan:LanguageCode>

</lan:language>

<lan:characterEncoding>

<lan:MD_CharacterSetCode codeList="http://www.iho.int/S100/4.0.0/resources/Codelists/cat/codelists.xml#S100_MD_CharacterSetCode" codeListValue="UTF-8">UTF-8</lan:MD_CharacterSetCode>

</lan:characterEncoding>

</lan:PT_Locale>

# Comments

UML Needs to be UPDATED

UML Needs to UPDATED

UML Needs to updated

UML needs to REALLY UPDATED

From RM: Convention for naming exchange sets should be well-defined, e.g., for S-104, specify where the “S104” string must be in the exchange set name.

One S-104 commenter expressed an interest in harmonizing exchange set names with other product specifications (in particular, S-102).

Note: The naming rule in S-97 1.1.0 (A-6.2.18) is for datasets. While each product specification could define its own naming rules for exchange sets, some S-104 PT members think a convention for naming exchange sets should be specified at the “S-100 level”.

Note: The exchange set container could be a zip file or a folder, and could contain more than one dataset.

Discuss whether an S-100-wide convention (or conventions), for naming exchange sets is (are) appropriate.

Perhaps different conventions for different distribution frequencies (some products could use timestamps as part of the name)?

If “S-100 level” conventions are appropriate, what should they be?

From IIC: Suggest adding digital signature for the entire exchange set.

Agree in principle, but needs more work and discussion.

From Furuno: Non-database style products such as S-421 Route plan which is typically exchanged as a single file do not need this at all

Agree – but need to define the scope of when it is optional – ask Hannu

From Furuno: Non-database style products such as S-421 Route plan which is typically exchanged as a single file do not need this at all

Need more clarification as to how you know who sent the file without having to open the file.

Suggestion to replace whole class with a URN/URI.  But will clean up the rest of the metadata and then come back to this in a seperate editing session.

From CCG: Description is identical to S100_ExchangeCatalogue. Should be descriptive of this class.

Eivind to supply some words

From CCG: Is this identifier Prod.Spec specific, service specific or should it be standardized at the S-100 level? At a minimum, use guidance is needed.

Ed to supply Julia with NOAA’s process as a starting point

Julia: it is worth noting that this is the framework that was used for our NOAA Metadata API implementation focusing on one product at a time. For S-100 V5 we have agreed to have multi-product exchange sets so the product number should be replace with either all products present in the particular exchange set i.e. US_101_102_111_... or omitted entirely from the identifier. Personally, I like the first options as it gives an immediate indication of the data content to humans, machines will likely still need to process CATALOG.XML each time.

From KR: Some product specifications have defined means for providing delta changes between new editions. These delta change or update files are not specifically covered by S-100 exchange set metadata model, but several product specifications (S-122, S-123 and S-127) have made special adoption of the S100_DatasetDiscoveryMetadata class for update files.

An abridged discovery metadata would also be benefit  to S-124.

Sewoong to propose amendements

SEE ATTACHED DOCUMENT FOR DISCUSSION

From Caris: Do we expect ‘Individuals’ to be making official data?

Overlap or duplication of what is in the S100_CataloguePointOfContact and metadataPointOfContact

References a hierarchy of elements, how much is enough?  Some guidance and examples would be good.

Need more review on what we actually need from CI_Organization or if Producer Code will suffice

From Caris: Check schema and provided examples for consistency ‘eng’ vs ‘English’ etc.

Hugh to provide example

From CCG: The support for multi language should be reviewed. If there are multiple languages in the dataset, should also the metadata support multi language? If yes, do the CharacterString need re modelling to support multi language?

CCG to explore further

From SMA: Propose to allow more variants and key strength. Propose DSA1024, DSA2048

Need to tighten up S-100 Part 15 and then add in what is defined after that has been completed.  Also need to consider an IHO TR to define the digital signature algorithm used by IHO products.

JUNE 2021 – ASK JP to edit directly.

TSM8_2020_6.12 proposal from TWLCWG.  In addition the proposal suggested that this be changed to a codelist and will need more dissucssion from the metadata correspondence group.

From IIC: Product specification version is currently a character string. This  makes it challenging to sensibly use it in practice. It might be best to at least change it to a formatted string 6 characters AABBCC where AA, BB, CC are integers representing version, major and minor revisions accordingly. This would not require any changes to schemas etc. Another option would be to create separate elements for each of the above components similar to edition and update numbers. There are a few other placese where version shoudl be adjusted the same way for consistnecy.

From ED (May 2021) Product specification version is currently a character string. This makes it challenging to sensibly use it in practice. It might be best to at least change it to a formatted string 6 characters AABBCC where AA, BB, CC are integers representing version, major and minor revisions accordingly. This would not require any changes to schemas etc. Another option would be to create separate elements for each of the above components similar to edition and update numbers. There are a few other places where version should be adjusted the same way for consistency.

Needs more work and a strawman to fix.  Ed and Eivind to noodle.

From ED (May 2021) - Suggested change for all version numbers:

S100_VersionNumber

+ version: Integer

+ majorRevision: Integer

+ minorRevision: Integer

+ alternativeVersion: CharacterString – only used for non-numerical versions

– version and revisions should be mandatory unless alternativeVersion is used

NEW: JUNE 2021 – TCARIS - Consider including the S-100 version into the product spec version structure for the purpose of machine readability. The intent is that implementations are designed based on the format specifications in S-100 and the product spec would be a refined profile of the S-100 encoding. It is important for an end system to know what version of S-100 the encoding will comply to. At the moment this can only be found by reading the product spec document and building some sort of lookup table into using systems.

Add S-100 version property to the S100_ProductSpecification metadata class.

From Furuno: Non-standardized free character strings do not facilitate machine readable automation.

If this type remain the attribute has no value and the “Mult” should be changed as “0..1”

Suggestion to create a new class called S100_VersionNumber and to create three attributes for the three things defined under 2/2007.

From Furuno: The date is just interesting to know. Should be optional

From Caris: Is the name and version not enough, why is this field needed and could these numbers change over time?
Is it possible that a product could exist that is not registered in the IHO GI registry? Such as an unofficial product/dataset. In which case this field would need to be optional.

Will still need work

JUNE 2021: Having the product spec name and version should be enough to be able to find it in the IHO registry. The registry index number seems redundant and likely to change if the registry DB gets rebuilt etc.

Remove the registry index number from the product specification class.

From Caris: This statement in effect means that only one language per support file is allowed. This should probably be explained somewhere else in greater detail.

Needs to be WAY more perscriptive in this section

From Caris: If this is numeric then it should be an integer.

If this is meant to be machine readable information for systems to decide whether it can open the file or not perhaps codelists or something should be used.

If it is meant to be like ‘mp4’ then that is probably redundant with the file extension/type and would be better as a codelist.

Need to be more specific in the support file format list and remove this class.

NEW: Recommend adding more specific entries in the S100_SupportFile list so that there are different code list entries for each version which needs to be supported.  Include the version, if applicable, into the codelist description.

Having to add a new codelist entry to allow a new version gives an indication to implementors that support needs to be added for a new format version and makes it clear from the one format code exactly what is expected.

If this is not done then manufacturers are on the hook to support any random set of format versions which will add associated costs, testing/validation  and functional inconsistencies.

Remove this property in favour of more explicitly defined support file codelist entries.

Consider dropping the entire ‘supportFileSpecification’ field and class altogether and just use the ‘datatype’ fields with the S100_SupportFileFormat codelist.

From KR: Some product specifications expect updating of feature and/or portrayal and/or interoperability catalogues. Since this function is likely assumed to be identical for all specifications, it may be advisable to define the FC/PC/IC updating process at the S-100 level and include guidance in the product specification template to recommend that product specifications should consider making use of the common methodology.

Support for the concept – invite ROK to submit a full proposal on how it should be included in S-100

From CCG: Multiple files and file locations indicate that there need to be some ordered pairing. How will this work with portrayal catalogue consisting of hundreds of files? It it probably best to have one S100_CatalogueMetadata instance per catalogue, and this has impact on packaging of catalogues. Some form of container file is probably needed. It may also have impact on other attribute multiplicities in this class.

Support the concept,Changed multiplity from 1..* to 1 to fix this

NEW from TCARIS:

The versionNumber and issueDate fields are described as being the version of date of the product specification.  These are also sub fields of the productSpecification type and thus are redundant.

Drop versionNumber and issueDate fields since they are redundant.

From CARIS: Should be an integer or defined format string

This should be part of the new version class that will be developed and harmonized across the metadata.

From CCG: Think there is a need for better guidance in the use of these classes and for this guidance to be formulated in a way that reduces the need for further elaboration in Prod.Specs.

Canada to follow up.