|  | SE | 1.2 |  | ge | Wrong References in IHO S-44 IHO S-32 ISO 8601:2004 | Change to: IHO S-44 6th Edition IHO S-32, 2019 ISO 8601:2019 |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | SE | 1.3.2 |  | ge | Could we not simply reference the previously mentioned S-32? That way we don’t need to keep this updated all the time. If there are terms not present in S-32 perhaps they could be mentioned or added to S-32. | Reference S-32 |  |
|  | SE | 1.3.2 |  | ge | Depth = The vertical distance from a given water level to the bottom. | Change to: Depth = The vertical distance from a given reference level to the bottom. Need to be changed in S-32. |  |
|  | SE | 1.3.3 |  | ge | We have cut all ties to BAG, so perhaps this could be removed? The word is not present anywhere else in the document | Remove BAG from the abbreviations |  |
|  | SE | 4.2.1.1.1.2 |  | ge | In this section we use the word Real for the value type, but in the rest we use Float. For example in the tables under section 10.2 | Harmonize perhaps based on the BSH proposal regarding Data Types. |  |
|  | SE | 4.4.2.1 |  | ge | In the third paragraph: The vertical distance is from a given water level to the bottom | Change to: The vertical distance is from a given reference level to the bottom |  |
|  | SE | 5.1 |  | te | We are having problems understanding this section: Each sample in a grid represents the value in the grid at a point location at the coordinate specified, rather than an estimate over any area with respect to the coordinate. | As we interpret it we suggest that it should be an estimate over the cell area and not the node position or perhaps both. Like it is described in Annex F S-102 Gridding Methods The Shoalest Depth algorithm Description: The Shoalest Depth algorithm examines depth estimates within a specific area of influence and assigns the shoalest value to the nodal position. The resulting surface represents the shallowest depths across a given area. |  |
|  | SE | 5.1 |  | ge | Last sentence in the first paragraph: …. precision to locate the grid with accuracy no worse than a decimetre on the surface of the ellipsoid of rotation of the chosen horizontal datum. | Remove the highlighted text. Confusing |  |
|  | SE | 5.1 |  | ge | Last sentence in the last paragraph: Note the vertical datum is defined through a second association role to a vertical reference system. | Remove? Don’t really know what that means. Maybe remove whole sentence since it is also mentioned in 5.3? |  |
|  | SE | 5.3 |  | ge | Second paragraph: The vertical datum must be taken from the code-list defined by S100_VerticalAndSoundingDatum | SMA agrees with this, but for us to be able to create products in our inland waters that are locate far above the 0-level in our vertical reference system, we need some kind of offset metadata/attribute that describes the adjustment we made to the depths to avoid heights instead of depths. |  |
|  | SE | 5.4 |  | ge | ISO 8601:2004 | Update to ISO 8601:2019 |  |
|  | SE | 7 |  | ed | First sentence second paragraph: There are a number of sounding techniques, including SONAR and LIDAR that are used to capture bathymetric data. | Remove the specific platforms |  |
|  | SE | 10.2 |  | ge | In table 10.2: No 6: Epoch of realization No 7: Bounding box No X | Actions No 6: Clarify that it is the horizontal epoch of realization No 7: If the product is intended for navigational use the only option here is WGS84 No X: Also add Vertical epoch of realization if present. If accepted also add it in the S102_DatasetDiscoveryMetadata (12.7)? |  |
|  | SE | 12.2 | Table 12-2 and 12-3 | ge | depthCorrectionType | Suggest to remove this section and the metadata attribute depthCorrectionType. Is this information relevant for this product and its end users? |  |